## Slide 1
ZTE Corporation
Shao Weixiang
Discussion on Work Task 1 (System and Operational Aspects)
6G_NDTAPP_Enablement

## Slide 2: ITU-R M.2160-0 Framework and overall objectives of the future development of IMT for 2030 and beyond
Digital twin and virtual world: IMT-2030 is expected to be used to replicate the physical world into a digital virtual world as precise real-time representations or digital twins. Digital twins have the potential to provide ubiquitous tools and knowledge platforms for the modelling, monitoring, managing, analysing and simulating of physical assets, resources, environments and situations. Using advanced technologies such as integration of communication with, to the extent practicable, AI, sensing and computing, digital twins could also synchronize the digital world to the physical world and provide connections between the digital replica components. Digital twins are expected not only to replicate but also to affect the physical world by providing digital maps for virtual experiences to humans and computed control to machines. Digital twins are envisaged to become a powerful tool in the evolution of multiple industries including health care, agriculture and construction.
Technology enablers to enhance the radio network: With real-time interactive mapping between the physical and virtual twin networks, digital twin networks (DTNs) can help efficiently and intelligently verify, simulate, deploy and manage IMT‑2030 networks.
Usage scenarios and overarching aspects of IMT-2030

## Slide 3: ITU-T Y.3090 Digital twin network - Requirements and architecture
Digital twin network (DTN) is a virtual representation of a physical network. It is useful for analysing, diagnosing, emulating and controlling the physical network based on data, model and interface, so as to achieve the real-time interactive mapping between the physical network and the digital twin network.
Key characteristics of digital twin network
A reference architecture of digital twin network
3 layers:
Physical network layer
Network digital twin layer
  Unified data repository
  Unified data models
  Digital twin entity management
Network application layer

## Slide 4: 3GPP SA5 TR 28.915 Study on management aspect of Network Digital Twin
The NDT can be requested by the consumer to model a mobile network or part of one, support evaluating the corresponding impact, and return the report of the simulated impact generated by the NDT. The NDT may be used as a replica of a mobile network, which may synchronize data from the managed network for modeling. The digital twins provide modelling capabilities that are used by the network automation functions (e.g. MDA, SON, etc.) to accomplish their automation functionality. The related automation capabilities are provided by the network automation functions regardless of whether the digital twin models are integrated within or external to the network automation functions.
Relation of NDTs with network automation functions
NDTs may support many use cases in network management and automation. In all the use cases, NDTs provide modelling capabilities that are then applied by the network management and automation functions or applications to achieve the desired outcomes.Use cases where NDT may provide support include:
- Use case 1: Network management RAN ES policy verification using NDT
- Use case 2: Signalling storm analysis
- Use case 3: Emergency preparedness (see clause 5.3).
- Use case 4: Network failure and risk prediction (see clause 5.4).
- Use case 5: NDT support to network automation
- Use case 6: Using NDT to generate ML training data
- Use case 7: Nested NDTs
- Use case 8: Visualization of network topology and traffic
- Use case 9: Configuration verification
- Use case10: Network issue inducement
- Use case 11: Measuring customer satisfaction with the network services

## Slide 5: 3GPP SA5 TS 28.561 Management aspects of Network Digital Twins
NDT Management Service
Inheritance UML diagram for NDT management
Relationship UML diagram for NDT management
NDT management capabilities include:
Control and life cycle management of NDTs - DTLCM
NDT support for network automation
NDT support for verification – NDTVER
NDT support for data generation
Advanced NDT capabilities - NDTADV
NDT Mns management operation:
NDT function management
NDT job management
NDT report management

## Slide 6: 3GPP SA1 TR 22.870 Study on 6G Use Cases and Service Requirements (1)
Operator may deploy Network Digital Twin (NDT) to simulate different threat/attack scenarios, analyze the associated behaviour, and identify the root cause, then validate corresponding countermeasure in the NDT before applying to living network.
Security tests and applied measures may also be measured in term of their energy consumption, allowing to find the best trade-off and most efficient security solutions at the lowest energy cost. The energy consumption of the NDT may be significant to enable the complex representation of the network, its functions, traffic and users, especially for large simulations. (this should be mitigated by the energy optimisation capabilities that NDT could provide e.g. energy savings on the real network.)
The appropriate usage and design of NDT would prevent the need to instead test security measures in extensive labs setups, avoiding some of the material resources needed for the different labs elements e.g. emulators, RF chambers. The intense deployment and usage of NDT (by adding new usages such as simulations against security vulnerabilities) will increase the need for cloud HW and data center capacity, inducing material impact on water (manufacturing and cooling) and key material elements (e.g. copper, rare minerals…).
The operator's mobile network is mirrored in the NDT environment and continuously synchronized to the NDT environment. NDT environment can collect security event and logs from the mobile network. With such NDT, security-related operations (such as vulnerability scanning, security/penetration test, the application of countermeasures, etc.) could be conducted in the virtual replica before making any changes to the living mobile network, also considering real-time factors.
In TR 28.915, no security related use case or requirement has been identified.
[PR 5.5.8.6-1] Subject to operator’s policy, the 6G network should be able to support a Network Digital Twin for network and service management.
5.5.8 Use case on security control enhancement with NDT in 6G network

## Slide 7: 3GPP SA1 TR 22.870 Study on 6G Use Cases and Service Requirements (2)
Network Digital Twin (NDT) are real-time digital counterparts of physical networks or in other words. A NDT is a digital replica of the full life cycle of a physical network, gaining recognition as a transformative technology for designing, diagnosing, simulating, conducting what-if analyses, and enabling AI/ML-driven real-time optimisation and control in sixth generation (6G) wireless networks. It could be capable of generating perceptive and cognitive intelligence based on collection of historical and on-line network data. It may also be capable of continuously seeking the optimal state of the physical network in advance and enforcing management operations accordingly.
Energy efficiency is a key focus for 6G, as networks are expected to support exponentially higher data rates and device densities. The 6G system should leverage NDTs to enable real-time optimisation of energy consumption across the network. This involves creating a digital replica of the network that continuously monitors energy usage, predicts demand, and dynamically adjusts network resources (e.g. turning off unused components, scaling down capacity during low traffic) to minimize energy consumption while maintaining service quality.
NDT can optimise energy efficiency in both network communications and computing workloads. The goal is to minimize carbon footprint by dynamically adjusting network and cloud resource usage based on real-time and predictive AI-driven models. The NDT continuously monitors and simulates network energy consumption, IT infrastructure workload distribution, and application energy efficiency. It helps operators achieve carbon neutrality targets by optimising data centre operations, edge computing resource allocation, and green network routing.
While SA5 (TR 28.915) studies NDT for network management, this use case specifically focuses on sustainability and energy efficiency optimization across computing layers.
[PR 5.8.7.6-1] The 6G network shall provide suitable means for communicating with the NDT of operator controlled compute resources that are in the Service Hosting Environment or the cloud, for the purpose of energy consumption analysis and optimisation.
5.8.7 Use case on green communications and computing optimisation using network digital twin

## Slide 8: 3GPP SA1 TR 22.870 Study on 6G Use Cases and Service Requirements (3)
Network Digital Twin (NDT) are digital virtual representation of physical networks, as an environment potentially enabling AI/ML- for delivering better services to users of in sixth generation (6G) wireless networks. For 6G networks and their operations, NDT will play a key role in Autonomous Networks supporting a wide range of use cases such as network simulation and planning, network optimization and management and others.
By introducing the capabilities of network digital twins, two critical aspects can be enabled for network optimization. First, the service awareness achieves by digital twin to provide comprehensive network traffic restoration. This enables sufficient QoE evaluation and analysis to support better service offering. Second, the simulation-based validation via digital twin enables solution (e.g. adjusting user QoS policies) to be tested before real-network deployment, achieving full closed-loop network autonomy.
Additionally, based on prior scenarios, the operator can prepare an intent and provide it to NDT and NDT can deduce optimal configurations to satisfy the intent.
SA5 has not studied related key aspects such as how digital twin enables the autonomous networks and its impact on the network structure (e.g. data synchronization between network digital twin and the physical network).
Currently, SA2 (e.g. NWDAF) has specified AI related capabilities, such as network performance analysis. However, it lacks end-to-end service experience visibility to identify root causes of QoE issues. Network digital twins solve this by correlating spatiotemporal network data to reconstruct complete service trajectories, enabling QoE diagnosis for better optimization. Furthermore, 6G needs to establish self-optimization mechanisms, current AI-generated network policies lack validation, risking reliability. Digital twins provide a verification environment to test policies (e.g. QoS adjustments) in simulated real-world conditions before deployment, a critical capability requiring standardization in 6G.
[PR 5.9.3.6-1] The 6G system shall support the digital twin in the 6G network to enable autonomous networks, which through simulating in the network characteristics and behaviours provide services to users (e.g. user traffic running on the virtual replica of mobile network or part of it).
[PR 5.9.3.6-2] The 6G system shall expose an API for the 6G network to transfer network function related information (e.g. NF configuration, UE context related data such as UE QoS etc.) to NDT to replicate 6G network in NDT.
[PR 5.9.3.6-3] The 6G system shall expose an API for the 6G network to receive feedback (e.g. optimal QoS parameter values, NF configuration etc.) from NDT.
[PR 5.9.3.6-4] The 6G system shall be able to transfer timely the data (e.g. related to service outage) stored from 6G Network to NDT.
5.9.3 Use case on network digital twin in the 6G network

## Slide 9: 3GPP SA2 TR 23.700-84 Study on Core Network Enhanced Support for Artificial Intelligence (AI)/Machine Learning (ML)
Figure 6.26.1.1-1: ReLF architecture supporting data-driven recommendation service
Solution #26: NWDAF-assisted policy control with Recommendation logical function
The ReLF includes two data-driven parts as following:
-Verification part, which collects data and derives the output. For example, the verification part may collect data related to service experience and derives the service experience. The verification part may also request analytics from other NWDAF(s) for deriving the Model outputs.
-Recommendation part, which generates recommended parameters based on the deviation between the model outputs and the optimization goals. The recommendation part tries to derive the recommended parameters within the parameter ranges that the consumer can accept (i.e. parameter constraints) to minimize the deviation from the optimization goals (i.e. the objective function of the recommendation part indicates that the model outputs and the optimization goals should be as close as possible).
NOTE 1:To further optimize the recommendations, the output of the recommendation part could be the input of the verification part, the verification part may be implemented by using a ML model or digital twin, which can verify the goals that can be achieved after using the recommendations and generate new model outputs, then it can be checked whether new deviation between the new model outputs and the optimization goals is small enough. The recommendation part may derive new recommended output based on the new deviation and the parameter constraints. The loop between the verification part and recommendation part is optional. The loop can be performed one or multiple times as needed, and the recommendation part can decide when to stop the loop and then provide the output to the consumer.
Recommendation Logic Function (ReLF) is new NWDAF functionality which may request a plurality of analytics (i.e. multiple analytic ID) from one or more NWDAFs or collect data directly from one or more NF(s) and derives recommendation information (e.g. recommended QoS parameters) that can fulfil the optimization goals (e.g. MOS>=4) provided by the consumer, and exposes recommendation service to the consumer (e.g. PCF).

## Slide 10: ETSI TS 103 846 SmartM2M; Digital Twins: Functionalities and communication Reference Architecture
High level abstraction of a Digital Twin Blueprint Architecture
Management Interface (MNI) enables dynamic control, configuration, and management of DT behavior, acting as a digital control Center
Mapping to SA5 NDT Management service
Physical Interface (PI) responsible for interacting with the physical world
Mapping to SA6 NDTAPP usage Sensing, EnergySys enablers
Digital Interface (DI) interacts with the digital space, exposing descriptions, states, events, and triggers for DT actions through various protocols
Mapping to SA6 NDTAPP expose to vertical / application specific layer
Monitoring Interface (MOI) supporting operational analytics and predictive maintenance strategies.
Mapping to SA6 NDTAPP usage AIML, ADAES enablers

## Slide 11: 6G-study Proposal Overview: FS_6G_NDTAPP
Background/Motivation
  SA1 TR 22.870 has 6G use cases on network digital twin (e.g. security control enhancement with NDT in 6G network, green communications and computing optimisation using network digital twin, network digital twin in the 6G network).
  SA5 TS 28.561/ TR 28.915 support management aspects of Network Digital Twins.
SI / SIs
  Dedicated SI, new TR
Continuation or New topic
  New topic
Objectives
  Support 6G Application Enablement for Network Digital Twin service
TUs required
  8 Tus, start 2025 Q4, end 2027 Q1
Dependency on other WGs
  SA2, SA5

## Slide 12: Detailed 6G-study Proposal: FS_6G_NDTAPP
1) Analyse Rel-20 requirements related to Network Digital Twin and further identify key issues, develop corresponding architectural requirements at the application enablement layer and exposure Network Digital Twin services to the vertical / application specific layer such as:
  Simulate security-related operations (such as vulnerability scanning, security/penetration test, the application of countermeasures, etc.)
  Enable AI/ML-driven real-time optimisation and control (such as continuously seeking the optimal state of the physical network in advance and enforcing management operations accordingly, etc.)
  Real-time optimisation of energy consumption and energy efficiency in both network communications and computing workloads.
  Support autonomous networks by network simulation and planning, network optimization and management.
  Deduce optimal configurations to satisfy intent.
2) Study architectural and functional implications on existing SA6 application enablers (e.g. AIML, ADAES, Sensing, EnergySys and other SEAL services) for supporting Network Digital Twin services.
3) Identify potential solutions, including the information flows and developer-friendly application enablement APIs, where necessary to satisfy the architectural requirements and enhancements identified in bullets 1) and 2).
4) Investigate possible impacts of application layer support for Network Digital Twin services for different deployments and business models.
NOTE: The study will take into consideration the ongoing SA2 & SA5 6G study aspects to avoid potential

## Slide 13: Thank you！