## Slide 1: Discussion paper on ad hoc group combine
Ericsson
Rana.alhalaseh@ericsson.com

## Slide 2: Content
Stage 1 requirements
Our proposal to combine ad hoc groups
Conclusion

## Slide 3: Stage 1 requirements
[R-6.15.5.2-001] The MCX Service shall provide a mechanism for an authorized MCX User to combine an ad hoc multiplicity of MCX Users into a MCX Service Ad hoc Group Communication.
NOTE: Selection of the list of MCX Users can be manual, or automatic based on certain criteria (e.g., location). This is left for implementation.
[R-6.15.5.2-016] The MCX Service shall provide a mechanism for an authorized MCX User to combine multiple Ad hoc Group communications.

## Slide 4: Stage 1 requirements
Observation 1: there is no requirement that dictates that ad hoc group call setup is either set up only via criteria, or only via a list of participant, but not both.
Question: are individual ad hoc groups to be combined must have the same setup type? i.e., ad hoc group 1 (criteria based) and ad hoc group 2 (list of participant based) shall not be combined.
Observation 2: based on the discussions in Athens (SA6#65 and SA1#109), a potential new requirement to “uncombine” a combined ad hoc groups is to be added by SA1.
Conclusion: the approach/procedure we choose now to combine ad hoc groups needs to be simple in order to easily uncombine them.

## Slide 5: Our proposal: create a new ad hoc group

## Slide 6: Our proposal: create a new ad hoc group
An ad hoc group call request that follows ad hoc group call combine response needs to include only the MCPTT ad hoc group ID provided by the MCPTT server in the combine response message
MCPTT server is aware which MCPTT users to invite based on the ad hoc group IDs provided in the combine request
A standalone ad hoc group call request needs to include either a MCPTT ID list or criteria as per existing procedures
The MCPTT server provides MCPTT user 1 the MCPTT ad hoc group ID associated with the combined ad hoc groups

## Slide 7: Our proposal: create a new ad hoc group
A new ad hoc group is created to combine individual ad hoc groups
  Combining is done on ad hoc group ID level, and not on individual MCPTT user level
The MCPTT users to join the new ad hoc group are already known at the MCPTT server in the form of ad hoc group IDs (sent by initiator in the ad hoc group combine request)
  The focus is on ad hoc group IDs, not on the members of the individual groups (as well as not on the type of the individual ad hoc groups)
The combining is MCPTT server centric
  If an authorized MCPTT user (different from the combining initiator) has previously added (or removed) MCPTT users from any criteria based ad hoc group to be combined, these MCPTT users will be known/marked at the MCPTT server to be added (or not added) to the new combined ad hoc group
    (ref. step 2 of cl. 10.19.3.1.4 and 10.19.3.1.6 of TS 23.379)
Potential uncombine: A mapping between the individual ad hoc group ID and respective participants (in the form of criteria or list of participants) can be stored (unmodified) at the MC server for potential uncombining

## Slide 8: Advantages
Combining ad hoc groups is based on combining ad hoc group IDs, not based on members of the individual ad hoc groups
MCPTT server is fully aware of the members of each individual ad hoc groups
  The combining is done at the MCPTT server
  Based on existing procedures, authorized MCPTT users are optionally notified of either who did/ did not acknowledge the ad hoc group call request, or has joined or did not join, or left the ad hoc group call
  Based on cl. 10.19.3.1.5, the authorized MCPTT users are not notified of added or removed participants by the MCPTT server
  MCPTT users which were added to (or removed from) individual criteria-based ad hoc group by an authorized MCPTT user (despite the criteria) are known at the MCPTT server so that they will not be removed from (or added to) the respective ad hoc group
MCPTT server can store (unmodified) information related to the individual ad hoc groups for potential uncombining
  The criteria/ list of participants of individual ad hoc groups can be easily stored (unmodified)

## Slide 9: Conclusion
We need to choose an ad hoc group combine procedure that
  is simple
  enables the possibility to maintain the information of individual ad hoc groups (criteria or list of participants per individual ad hoc group) for potential uncombining
Allow the ad hoc group call request following an ad hoc group combine response to include an ad hoc group ID associated to the combine procedure
The MCPTT members to be invited to the new ad hoc group ID are known at the MCPTT server

## Slide 10: Thank You!