## Slide 1: Discussion on the Way Forward for WT5.5
MediaTek Inc.
Contact: Yu-Jen Ku (Yu-Jen.Ku@mediatek.com)

## Slide 2: Outline
Justification/Clarification on WT5.5
Summary
Appendix

## Slide 3: WA5: Compute and Communication Aspects WT5.5
TEMLATE
Summary of comments
  The definition of "network resources" is not clear
  May be covered by WT5.4 (Compute co-ordination with CN)
Justification/Clarification
  SA1 already has use cases and requirements that needs the support of compute offloading (e.g., AI model inference and XR rendering)
  These use cases may require intensive support of both computing and communication services
  Jointly considering the communication and computing requirements is required in 6G to achieve good performance of computing task offloading
    e.g., An efficient AI inference splitting between UE and Edge server requires end-to-end information, including UE/Edge computing and network communication information
    e.g., To ensure end-to-end delay performance of compute offloading, if the communication delay increases, the server can add more resources for the task to reduce the computing delay (see Appendix)
  WT5.4 mainly focuses on the coordination between the computing services at CN and 3rd party. But the joint consideration of computing and communication requirements should be studied too.
Way forward (e.g. revised WT, merging etc)
  Revise WT as: How to enable joint consideration of the communication and computing requirements among UE/Edge/Cloud
Candidate Work Task | Support | Do not support | Moderator Remarks
WT5.5: Network resources vs compute resources at edge/cloud | Lenovo, CMCC, Apple, Samsung, ZTE | Interdigital, CATT, MediaTek, Huawei, Nokia, Ericsson | Merge with WT5.4, Needs clarification, SA2 overlap, Merge to WT5.4

## Slide 4: Summary
For WT5.5, revise the WT as:
  How to enable joint consideration of the communication and computing requirements among UE/Edge/Cloud

## Slide 5: Appendix: Performance Evaluation on Joint Consideration of Computing and Communication Requirements
Disjoint delay management (legacy):
  A job is successful offloaded if both (1) and (2) are met
    (1) Communication Delay ≤ Communication Delay Budget
    (2) Compute Delay ≤ Compute Delay Budget
Joint delay management:
  A job is successful offloaded if
    Communication Delay + Compute Delay ≤ Total Delay Budget
System Model
Job Offload
( Wired )
Uu
Communication Delay
Compute Delay
Total Delay
Budget Design | Compute Capacity Scale
Joint | 8
Disjoint | 11
More efficient use of compute capacity
System Service Capacity KPI
System Service Capacity KPI
Gain via joint delay budget design
Budget Design | Service Capacity
Joint | 80
Disjoint | 55
45% Increase