## Slide 1: Discussion Paper: Server-Server message for MCPTT and MCData
Frank Koersten, Juhee Seong, Andreas Platzer
04.11.2025, BDBOS

## Slide 2: Status
At SA6#69, Wuhan 4 CRs were agreed to resolve Editor’s Note on server-to-server messages.
  S6-254431 (Rel-18) and S6-254432 (Rel-19) for MCPTT and
  S6-254429 (Rel-18) and S6-254430 (Rel-19) for MCData
In all 4 CRs the Editor’s Note was formally resolved (but not technically) to the following:
  NOTE: Whether the server-to-server message is needed in a call request is out of scope of the present document.
Notes: The original editor´s note in 10.19.2.3 Ad hoc group call request (MCPTT server – group host MCPTT server) and 10.19.2.6 Ad hoc group call response (MCPTT server – MCPTT server) reads as follows:
Editor's Note: It is FFS if the server to server message is needed in a call request or response message.
Deleting the editor´s note in clauses 10.19.2.3 Ad hoc group call request (MCPTT server – group host MCPTT server) and 10.19.2.6 Ad hoc group call response (MCPTT server – MCPTT server):
Editor's Note: It is FFS if the server to server message is needed in a call request or response message.

## Slide 3: Current description in ad hoc calls 1/2
TS 23.379, 10.19.3.2.1 Procedure for ad hoc group call setup …
Notes: See step 6 and 7 !
… The primary MCPTT server further initiates an ad hoc group call request message to the MCPTT users of the partner MC system. The ad hoc group call request message is routed to the MCPTT users via the MCPTT server of the partner MC system.
… The ad hoc group call response message is routed to the MCPTT server of the primary MC system via the MCPTT server of the partner MC system.

## Slide 4: Current description in ad hoc calls 2/2
Ad hoc GC procedures in TS 23.379; 10.19.3.2 and TS 23.282; 7.17.3.2 describe server-server messages in the text, but not clearly, the server-server steps are missing in the figures
it is required to show the actual steps more in detail (in figures and procedure steps)
the server - server information flows in TS 23.379; 10.19.2 and TS 23.282; 10.17.2 shall not be deleted

## Slide 5: BDBOS proposal in ad hoc calls
TS 23.379, 10.19.3.2.1 Procedure for ad hoc group call setup …
Notes: The correct description is already there (6 out of 7 procedures)
10.19.3.2.1
6. The primary MCPTT server further initiates an ad hoc group call request message to the MCPTT users of the partner MC system. The ad hoc group call request message is routed to the MCPTT users via the MCPTT server of the partner MC system.
The receiving MCPTT clients notify their corresponding MCPTT users about the incoming ad hoc group call request with the information of the MCPTT group ID for the ad hoc group. The MCPTT users upon receipt of the invitation may accept or reject the call, and respond with the ad hoc group call response. The ad hoc group call response message is routed to the MCPTT server of the primary MC system via the MCPTT server of the partner MC system.
Or 10.19.3.2.3
NOTE 3: The ad hoc group call request and response exchanged between MCPTT server 1 of primary MC system and MCPTT client 3/MCPTT client 4 will always traversal through the MCPTT server 2.

## Slide 6: Reasons for requirements
each SIP-Session between 2 or more users always require a server-server (S-CSCF <-> S-CSCF) communication (IMS TS 23.228; 5.4.0)
enhancement for readers undestanding of stage 2 architecture documents required
a clarified depiction is required for future EU server to server interconnections and for
descriptions of server to server testing in GCF, ETSI Plugtest, etc.
BTW: other 3GPP procedures have the details described correctly (pls. see clause additional information)

## Slide 7: Way forward
BDBOS proposes to
  remove the Note in Rel-20 MCPTT and MCData specifications
  add correct figures & description in the relevant procedures for MCPTT and MCData.
  add missing server - server information flows
In 2026, 1st meeting
  Bring back removed IFs for MCVideo and
  add correct figures & description in the relevant procedures for MCVideo

## Slide 8: Additional Information
Examples of existing server to server messages:

## Slide 9: Current behaviour Server-Server 1/2
TS 23.379, 10.7.2.3 Private call within several MCPTT systems

## Slide 10: Current behaviour Server-Server 2/2
TS 23.379, 10.6.2.4.1 Group call for non-broadcast temporary groups across multiple MCPTT systems