| 3GPP TSG-2 meeting #5 | Document | T2-99661 |
| --- | --- | --- |
| Helsinki, Finland, 6-9 September 1999 |  |  |
| 3G CHANGE REQUEST |  |
|  | 27007 | CR |  | Current Version: | 3.1.0 |  |
| For submision to TSG |  | for approval | X |  |
|  | for information |  |  |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM |  | ME | X | UTRAN |  | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Ericsson | Date: | 1999-08-30 |
| Subject: | ECSD AT command correction |
| 3G Work item: | EDGE circuit switched data |
| Category: | F Correction |  |  |  |  |
|  | A Corresponds to a correction in a 2G specification |  |  |  |  |
| (only one category | B Addition of feature |  |  |  |  |
| shall be marked | C Functional modification of feature |  |  |  |  |
| with an X) | D Editorial modification | X |  |  |  |
| Reason for change: | A reference to GSM 0x.xx in the recently introduced +CHSA AT command, needs removal |
| Clauses affected: | 6.18 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

## 6.18	HSCSD non-transparent asymmetry configuration +CHSA

Table 1: +CHSA parameter command syntax

| Command | Possible response(s) |
| --- | --- |
| +CHSA=<mode> |  |
| +CHSA? | +CHSA: <mode> |
| +CHSA=? | +CHSA: (list of supported <mode>s) |

Descriptiont

Set command controls the preferred asymmetry bias for  non-transparent ECSD calls. Downlink biased asymmetry means that 8-PSK modulation is preferred downlink and GMSK modulation uplink.  Uplink based asymmetry means that 8-PSK modulation is preferred uplink and GMSK downlink. Changing of <mode> affects the current call only if <topRx> (refer +CHSN) was non-zero when call was established.

Test command returns values supported by the ME/TA as compound values.  The <mode> subparameter range indirectly indicates the MS Type; range (0-1) indicates MS Type A and range (0-2) indicates MS Type B.

NOTE:	ECSD is also controlled by +CHSD, +CHSN and +CHST.

Defined values

<mode>:

0	No preference

1	Downlink biased asymmetry

2	Uplink biased asymmetry

Implementation

Mandatory when non-transparent ECSD is implemented.