| 3GPP TSG-T2 | Document | T2-99667 |
| --- | --- | --- |
| Helsinki, Finland, 06-09 09 1999 |  |  |
| 3G CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 27.010 | CR |  | Current Version: | V3.1.0 |  |
| 3G specification number ( |  | ( CR number as allocated by 3G support team |
| For submision to TSG | T#5 | for approval | x | (only one box should |
| list TSG meeting no. here ( | for information |  | be marked with an X) |
| Form: 3G CR cover sheet, version 1.0 The latest version of this form is available from: ftp://ftp.3gpp.org/Information/3GCRF-xx.rtf |
| Proposed change affects: | USIM |  | ME | x | UTRAN |  | Core Network | x |
| (at least one should be marked with an X) |
| Source: | Nokia | Date: | 30/08/1999 |
| Subject: | Correction of the bits in the start and close flags of the frame in the example on Annex B |
| 3G Work item: | TEI |
| Category: | F Correction |  |  |  |  |
|  | A Corresponds to a correction in a 2G specification | x |  |  |  |
| (only one category | B Addition of feature |  |  |  |  |
| shall be marked | C Functional modification of feature |  |  |  |  |
| with an X) | D Editorial modification |  |  |  |  |
| Reason for change: | There are several bits that are wrong. |
| Clauses affected: | Annex B B.1 Example (new) B.2 Reflected bits (new) |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other 2G core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

# B.1	Example

A SABM frame on DLCI 1. Note that bits are written as they are sent on the serial port, LSB bit first and MSB bit last. No start stop bits, transparency bytes, BOFC or EOFC are included in the message. (The length octet is only included in the FCS for UI frames).

| BOFC | DLC | Ctrl | FCS | EOFC |
| --- | --- | --- | --- | --- |
| 10011111 | 11100000 | 11111100 | To be calculated | 10011111 |

k=8*2=16

message=11100000 11111100

# B.2	Reflected bits

In the example the bits where shown as they was sent on the serial line, this is however not they way the application sees the octets, it will see MSB first and LSB last, so before calculating the FCS the octets bit order must be reversed.

| BOFC | DLC | Ctrl | FCS | EOFC |
| --- | --- | --- | --- | --- |
| 0xF9 | 0x07 | 0x3F |  | 0xF9 |
| 11111001 | 00000111 | 00111111 | To be calculated | 11111001 |

1	Reverse all bit in octets

2	Calculate FCS

3	Reverse all bits in FCS

4	Send the reversed FCS

Fortunately there is an easier way of doing the reversing of the bits, when implementing the CRC calculation using table lookup the table can be reversed.

# B.3	Implementation

Implementation is very simple because the FCS will be as wide as the lookup table (8 bits). To avoid having to reverse all bits in the octets all the octets in the crc table is reversed instead.

The termcorresponds to initialising the FCS with 0xFF.