## Slide 1: Wi-Fi and LAA Presentation by Wi-Fi Alliance to 3GPP LAA Workshop
August 29, 2015
Beijing China

## Slide 2: Topics
Introducing Wi-Fi Alliance® and 5 GHz market overview
Background on Wi-Fi Alliance activities regarding unlicensed LTE
Input on LAA LBT design
Open Platform Coexistence Simulation Initiative
Coexistence Testing Initiative
Next Steps

## Slide 3: The Wi-Fi success story
Everyone:
Embraced by consumer, enterprise, and service providers
Massive installed base – 5.3 billion devices this year, 10 billion by 20201
Every laptop, every tablet and 70% of smartphones1
Everywhere:
700 million+ Wi-Fi households today, growing to 1.2 billion worldwide in 20182
8 million+ hotspots and 55 million home spots - and growing to 340 million in 20183
Carrying much more than half of the world’s internet traffic4
1 ABI Research
2 Strategy Analytics
3 iPass
4 Cisco VNI

## Slide 4: Huge diversity of Wi-Fi product types, including handsets but also consumer electronics
Computing and peripherals
Consumer electronics
Handsets
Networking
Other
Reference Design/Module

## Slide 5: 5 GHz Wi-Fi is already mainstream
5 GHz band already widely used by Wi-Fi devices, and trend is increasing

## Slide 6: 5 GHz Wi-Fi will soon become nearly universal
With the launch of Wi-Fi CERTIFIED ac in 2014 the Wi-Fi industry has focused its future on 5GHz

## Slide 7: Background: Wi-Fi Alliance activity regarding Unlicensed LTE

## Slide 8: Background on Wi-Fi Alliance activity on Unlicensed LTE
Wi-Fi Alliance’s Coexistence Task Group was established to investigate fair sharing with unlicensed LAA
  Provides input and guidance on staff-directed coexistence testing and simulation initiatives
  All Wi-Fi Alliance members interested in coexistence are encouraged to participate
Testing effort is initially focused on effect of a duty-cycle interferer on Wi-Fi
  We intend to also address LAA as the specification matures and as prototypes become available
Simulation is focused on the effects on Wi-Fi of both LAA and duty-cycle interferer

## Slide 9: Input on Fair Sharing Mechanisms

## Slide 10: Wi-Fi Alliance Input on Fair Sharing Mechanisms
  Fair coexistence with Wi-Fi is a requirement
  It is now our understanding that 3GPP will require LBT in all regulatory domains
We are generally pleased with 3GPP’s direction towards a single Category 4 LBT algorithm
Significant analysis and simulation work is still required before finalization to ensure coexistence with Wi-Fi
  detailed algorithm is still to be determined
  potential algorithm variation in actual deployments needs to be characterized
  continuing simulation of coexistence mechanisms during the work item phase of LAA should be performed

## Slide 11: Wi-Fi Alliance Input on Fair Sharing Mechanisms
We generally support the input from IEEE (link) including these key issues which we believe require further analysis:
  LBT inclusion of exponential backoff for both DL and UL transmissions
  LBT timing rules and thresholds for energy detect that meld with Wi-Fi
  Preamble detection and/or reservation signaling
Simulation scenarios need to be enhanced
  Our specific recommendations on the following slides
  These recommendations pertain not only to Wi-Fi Alliance efforts going forward, but should also be part of 3GPP’s continuing work

## Slide 12: Performance metrics for simulations
    In addition to throughput and latency, the following performance metrics for evaluation of coexistence behavior should be included:
      Jitter (measured at MAC layer, especially for “real-time” media flows)
      Packet loss (measured at MAC layer)
      Frame retransmission rate (measured at MAC layer)
      Beacon loss and deferral (including beacon jitter)
      Power save signaling loss and deferral (including PS signaling jitter)

## Slide 13: Additional simulation requirements
    The coexistence behavior in a multi-operator scenario should be considered
    The coexistence behavior with wider bandwidth Wi-Fi channels should be considered
    The coexistence behavior in higher density deployments should be considered
      100s of clients per AP/eNB
      moderate coverage overlap on a given channel between APs/eNBs

## Slide 14: Open Platform Simulation Initiative

## Slide 15: Wi-Fi Alliance Open Platform Coexistence Simulation Initiative
We believe that an open platform approach to coexistence simulations will benefit all stakeholders in the unlicensed bands
Open to substantive peer review
Allows for contributions from any interested stakeholder
Based on ns-3 open simulation platform
Goal: provide a tool that can inform the development of cross-industry coexistence solutions

## Slide 16: ns-3 Overview
Third generation of a network simulation framework, supporting performance evaluation of computer/communication networks
  Wi-Fi and LTE models are the most widely used and developed by multiple contributors over the past 5-10 years
Unique capabilities in support of software reuse and network emulation
  ns-3 offers unique full-stack simulation capabilities allowing Linux kernel code and applications such as iperf to be integrated with simulation models of LTE and Wi-Fi
  ns-3 can operate with a real-time scheduler and uses standards-compliant frame formats, allowing ns-3 to interoperate with real devices in testbed settings
A leading platform for published network research on LTE and Wi-Fi
Free, open-source software backed by an active open-source project

## Slide 17: ns-3 is in wide use
Search of keywords on Google Scholar
  Search performed on July 28, 2015 (excluding citations and excluding patents)
  "ns-3 simulator LTE" yields 1040 results
  "ns-3 simulator wifi" yields 1170 results
175 authors credited with code contribution
Active mailing lists
  ~5200 subscribers to
  main user's mailing list
  generating ~30 messages
  per day
ns-3-users subscribers since 2008

## Slide 18: Current status of Coexistence Simulation Initiative
Wi-Fi Alliance has contracted with University of Washington and CTTC
  This work intended to establish foundational platform that can subsequently be used (and contributed to) by all interested stakeholders
Initial focus has been to establish the simulation platform and to integrate pre-existing Wi-Fi and LTE capabilities
  Indoor and outdoor simulation scenarios and evaluation set up, as per TR 36.889, are already supported.
Effort is now underway to implement basic LAA Category 4 LBT algorithm
  Incorporation of ETSI BRAN flowchart
Intent is to track the specification of LAA LBT as it is finalized
  Results can provide feedback on LBT proposals throughout the 3GPP decision process
Resulting platform will be useful to all stakeholders even beyond the 3GPP Work Item phase
  deployment guidelines, best practices, scripts to facilitate reproducibility

## Slide 19: Coexistence Testing Initiative

## Slide 20: Coexistence Testing Initiative
Wi-Fi Alliance is working on a suite of tests for coexistence with Wi-Fi in a representative set of scenarios
We will work with LAA product vendors as early as possible to test products to determine if they can pass the Wi-Fi Alliance coexistence tests across all allowable configurations
We will encourage operators to test the LAA equipment they plan to deploy using their intended configuration parameters as per the Wi-Fi Alliance coexistence tests
We would like to explore how our coexistence testing initiative can complement or contribute to the 3GPP and operator testing processes for LAA

## Slide 21: Next Steps

## Slide 22: Next Steps
  We are encouraged by this workshop and look forward to closer engagement with 3GPP
  Updates on simulation initiative will be provided
  Future testing efforts with LAA will commence once devices are available