## Slide 1: 5G Use Cases, Deployment Scenarios and Framework of Requirements
3GPP RAN Workshop on 5G
September 17-18, 2015
Phoenix, USA

## Slide 2: The NGMN Alliance is supported by key industry players
26 Worldwide Leading Mobile Operators
36 Worldwide Leading Technology Vendors
25 Universities / Research Institutes
Notes: The goal of the NGMN alliance is:
- Enable creation of desirable products
- Provide viable economic incentives
- Be built on feasible technology
The role of NGMN alliance is to:
- Articulate requirements of future mobile broadband networks, devices & services
- Drive customer & service centric innovation
- Collate and uses the expertise of its partners to develop a viable ecosystem
- Promote the adoption of NGMN technologies by the industry and users
- Be business driven with a strong focus on end-to-end requirements
- Minimise fragmentation of technologies & maximises economies of scale
The organisation of the NGMN as of JUne 2008:
      19 Members who are mobile operators
      28 Sponsors who are vendors of various size, but do include all the key manufacturers of devices and infrastructures
      3 University advisors
The key working groups of the NGMN are:
  IPR
  Spectrum
  Ecosystem Development
  Technology currently focused on the networks and devices and
  Trials, both technology trials and eventually customer trials.
  One may also want to point out that the NGMN LTD is a very small operation with 6 staff including Peter Meissner as its operating officer.

## Slide 3: NGMN Alliance 5G White Paper and Work Programme
Business Principles Group BPG
Requirements & Architecture
Spectrum
IPR Forum
Ensuring that 5G is architected and underpinned by solid business principles
Identifying & modelling elements & capabilities of future business models
Providing timely guidance on 5G solutions to all relevant industry stakeholders – definition of technical requirements, e2e architecture principles, input to SDOs and other organizations.
Providing continuous contributions to international fora and groups regarding NGMN spectrum requirements, in order to ensure the allocation of sufficient spectrum for future 5G services.
Co-operate with relevant industry partners to develop implementation plans for the 5G IPR recommendations outlined in the NGMN 5G White Paper.
  Guidance for the whole industry
  Operator driven global end-to-end view
  Specific, comprehensive requirements
  Business perspective
NGMN 5G White Paper published in March 2015
NGMN 5G Work Programme launched in June 2015

## Slide 4: Introduction
3GPP RAN and ITU-R will start work to define 5G use cases and requirements from early 2016.
Prior to this work, preliminary consensus building is essential to avoid delay of 5G standardization activities.
NGMN has set up a 5G work-program to develop early consensus on requirements and architecture principles to facilitate 3GPP and ITU-R activities.
  There are requirements workstreams on: eMBB, and Verticals (i.e. Automotive, eHealth and others)
This document is a status report from the ongoing work, focusing mainly on requirements for eMBB. It summarizes the use cases, deployment scenarios and the requirements framework being developed in NGMN and it also introduces the future work planned.

## Slide 5: 5G supports a wide range of services
HIGH SPEED TRAIN
SENSOR NETWORKS
Broadcast-like services
BROADCAST SERVICES
Ultra-reliable communications
E-HEALTH SERVICES
Lifeline communications
NATURAL DISASTER
Extreme real-time communications
TACTILE INTERNET
PERVASIVE VIDEO
50+ MBPS EVERYWHERE
50
Overview 5G Use Case Families and Use Case Examples
Photos: © iStockphoto.com
Massive Internet of Things
Higher user mobility
Broadband access everywhere
Broadband access in dense areas
See the NGMN 5G White Paper for a detailed list of all NGMN use cases
Focus of today’s presentation
(eMBB use case families)
Other use cases requirements are subject to discussions with verticals

## Slide 6: Mapping of use case families to deployment scenarios for eMBB (enhanced mobile broadband)
Dense urban
Rural coverage
High speed
Deployment scenarios
High density
Urban coverage
Broadband access in dense area
Broadband access everywhere
High user mobility
eMBB Use case families
Indoor hotspots
Photos: © iStockphoto.com

## Slide 7: Deployment scenarios (1/2)
Indoor hotspots
Deployments
*Indoor deployment for indoor hotspots, e.g., office, residential and shopping mall
Attributes
*Indoor base stations
*Indoor users
*Very high data rate
*Low mobility
*Very high user density
*Both low and high frequency
*HetNet, e.g., two layers, micro /macro cells with small cells
*Outdoor base stations
(Possibility of indoor base stations is FFS)
*Indoor and outdoor users
*High data rate
*Low mobility
*High user density
*High-rise/mid-rise buildings
*Both low and high frequency
*Homogeneous deployment with macro cells
*Outdoor base stations
*Indoor and outdoor users
*Medium to high data rate
*Low to medium mobility
*Medium user density
*Low frequency
Very high mobility: 250 km/h -500 km/h
High: 50 km/h -250 km/h
Medium: 3 km/h -50 km/h
Low: 0 km/h -3 km/h
Deployments
Deployments
Attributes
Attributes
Dense urban
Urban coverage
Photos: © iStockphoto.com
Very high user density: ≥100,000 / km2
High: 10,000-100,000 / km2
Medium: 1,000-10,000 /km2
Low: <1,000 /km2
Very high data rate: ≥1Gbps
High: >100Mbps
Medium: >50Mbps
Low：>25Mbps

## Slide 8: Deployment scenarios (2/2)
*Outdoor base stations
*Indoor, outdoor and vehicular users
*Medium data rate
*Low to high mobility
*Low user density
*Low frequency
*Specialized deployment for high speed trains
*Outdoor base stations
(e.g., special railway sites with outdoor-indoor relay mounted on the train)
*All users in trains
*Medium data rate
*Very high mobility
*Very high end-user density in trains
*Low frequency for outside link, low and high frequency for inside link
* Specialized deployment for stadium/ large-scale gathering
*Indoor or outdoor base stations
*Indoor or outdoor users
*Low to Medium data rate
*Low mobility
*Very high user density
*Both low and high frequency
Very high mobility: 250 km/h -500 km/h
High: 50 km/h -250 km/h
Medium: 3 km/h -50 km/h
Low: 0 km/h -3 km/h
*Homogeneous deployment with macro cells
Rural coverage
High speed
High density
Deployments
Attributes
Deployments
Deployments
Attributes
Attributes
Photos: © iStockphoto.com
Very high user density: ≥100,000 / km2
High: 10,000-100,000 / km2
Medium: 1,000-10,000 /km2
Low: <1,000 /km2
Very high data rate: ≥1Gbps
High: >100Mbps
Medium: >50Mbps
Low：>25Mbps

## Slide 9: Framework of requirements
Test environments |  | Key Performance Metrics |  |  |  |  |  | 
 |  | General KPIs (GKPI) |  |  | Test environment-specific KPIs (SKPI) |  |  | 
 |  | GKPI1 | GKPI2 | …. | SKPI1 | SKPI2 | SKPI3 | …
eMBB | eMBB1 |  |  |  |  |  |  | 
 | eMBB2 |  |  |  |  |  |  | 
 | eMBB3 |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  | 
MMC | MMC1 |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  | 
URC | URC1 |  |  |  |  |  |  | 
 | … |  |  |  |  |  |  | 
Separate requirements for low and high frequency bands for some KPIs.
Specific evaluation of the performance for indoor users served by outdoor (small cell) base stations via high frequency bands.
Some key considerations

## Slide 10: List of eMBB requirement metrics
Cell average spectrum efficiency*
Spectrum efficiency of worst 5-percentile users*
User experienced data rate a
Connection density b
Area traffic capacity c
Device speed
Network energy efficiency d
Peak spectrum efficiency*
User plane latency
Control plane latency
Handover interruption time
System bandwidth*
General KPIs
Test environment-specific KPIs
* Separate requirements for low (e.g., ≤ 6GHz) and high frequency bands (e.g., > 6GHz) . Thresholds for low and high bands FFS.
a The required user experienced data rate should be available in at least 95% of the locations (including at the cell-edge) for at least 95% of the time within the considered environment.
b Connection density is only relevant for dense urban and high density scenarios.
c This requirement can be derived from cell average spectrum efficiency, cell bandwidth and cell density.
d Requirement on the energy efficiency considering idle, bursty and active mode need to be investigated.

## Slide 11: Other key aspects for eMBB scenarios
Consistent user experience (at least throughput and latency) required
  Required “user experienced data rate” to be available in at least 95% of locations for at least 95% of the time
Video and social media to dominate eMBB traffic volumes
Large proportion of eMBB traffic is expected to be for indoor users
Network energy efficiency (e.g., Base Station energy efficiency) should be one of the basic design principles and energy performance should be evaluated.
Reasonable deployment assumptions required
  Site densities/dimensions, and backhaul assumptions
  Rural scenarios should not require more sites than existing networks
Requirements are based on the operator vision of 5G in 2020 as well as beyond 2020. As such, not all the requirements will need to be satisfied for 2020 deployments.
  NGMN plans to further prioritise requirements accordingly

## Slide 12: Summary and next steps
NGMN will continue to develop and refine the requirements framework and develop test environments to guide IMT-2020 development.
For eMBB, NGMN has identified six deployment scenarios and a requirements framework of interest for 5G.
The following milestones are currently planned to progress eMBB:
  Develop relevant test environments (2015.12).
  Refine and detail key performance metrics, deployment scenarios and test environments (2015.12).
  Provide values of (some) requirement metrics (2015.12).
  Define evaluation framework for the requirements (2016.3).
For non-eMBB (e.g. MMC, URC), NGMN will develop requirements, deployments scenarios and test environments, based on inputs from verticals (date tbc).
MMC = Massive Machine Communications
URC = Ultra-Reliable Communications

## Slide 13: Thank You