## Slide 1: Anticipations for the Final IMT-2020 Submission: Rel-16 Outlook for System and Core Network Aspects
Erik Guttman 3GPP TSG SA Chairman Samsung R&D Institute UK

## Slide 2: IMT-2020 Submission Non-Radio Aspects
As in past IMT submissions, 3GPP will include an informative list of all non-RAN specifications.
  It is important to emphasize that the 3GPP system is much more than the 3GPP radio aspects.
This list will not include the same specifications as in past submissions, as the 5G system explicitly does not support full backward compatibility with the 2G and 3G system (IMT-2000).

## Slide 3: 5G 3GPP Specifications
5G specifications began in Release 15.
  These specifications include not only the new 5G components, but also the continuing evolution of the 4G system.
New 5G specifications have been introduced across 3GPP.
Some 4G specifications are now 5G specifications, from Rel-15
  The Enhanced Packet Core and other 4G standards are important components of 5G.
  Operators will deploy and integrate 5G functionality in different ways, including continuing use of the EPC for some time.
  See TS 21.205 – which links to a list of 1113 specifications.

## Slide 4: System and Core Network Aspects
System and Core Network Aspects, as discussed in this presentation, include everything in scope of 3GPP standardization except Radio Access Network aspects.
System Aspects include: Security, Media and Codecs, Operations and Management, Applications, Terminal and End to End Aspects, Interworking with External Networks and Smart Card Application Aspects
Core Network Aspects include: all functions to support for services provided by the 3GPP system.
  These categories are somewhat arbitrary. Some functions could be considered both Core Network and System Aspects.

## Slide 5: Overview of 5G System and Core Network Aspects
The following slides offer a brief introduction to the major 5G specifications and what they include.
Though not a comprehensive introduction, this is a starting point to understand 5G.
This overview considers the output of Rel-15.
Following this overview, we will summarize the areas of ongoing study for Rel-16.
  Normative specification for System and Core Network Aspects of Rel-16 will occur in 2019.

## Slide 6: Overview of System Aspects (1/3)
Stage 1 – Service Requirements for 5G
  TS 22.261 “New Services and Markets Technology Enablers”
Stage 2 – 5G System defined in
  TS 23.501 “System Architecture for the 5G System”
  TS 23.503 “Policy and Charging Control Framework for the 5G System”
  TS 33.501 “Security architecture and procedures for 5G System”

## Slide 7: Overview of System Aspects (2/3)
Stage 2, continued
  Application : TS 23.222 “Common API Framework for 3GPP Northbound APIs”
  Media: TS 26.118 “3GPP Virtual reality profiles for streaming applications”
  Charging*: TS 32.291 “5G System Charging Service”
  OAM*: TS 28.530..554 “Management and orchestration”, many aspects
  OAM*: TS 28.304..306 “Control and Monitoring of Power, Energy and Envirnomental Parameters”
* All stages (1, 2 and 3) were completed for these specifications

## Slide 8: Overview of System Aspects (3/3)
Stage 3
  TS 24.501 “Non-Access-Stratum (NAS) protocol for 5G System”
  TS 24.502 “Access to the 3GPP 5G Core Network via non-3GPP access networks”
  TS 29.522 “Network Exposure Function Northbound APIs”

## Slide 9: Overview of Core Network Aspects
Stage 3
  TS 29.500 “Technical Realization of Service Based Architecture”
    Each service defined in TS 23.501 and 23.502 (Procedures) is specified a new TS.
    All control plane and user plane functions and interactions are specified at the protocol level in new TSs, including centralized state repositories.

## Slide 10: 3GPP Rel-16: Ongoing Studies (1/3)
Focus Area | System Studies | RAN Studies
URLLC for 5G | Enhancement of URLLC support in 5G, Enhanced support of Vertical and LAN Services, Cyber-physical control applications in vertical domains | Physical layer enhancements for NR UR Low Latency Cases, NR-based access to unlicensed spectrum, NR Industrial Internet of Things
V2X for 5G | Architecture enhancements for 3GPP support of advanced V2X services | NR Vehicle-to-Everything (V2X)
Positioning | Enhancement to the 5GC Location Services, 5G positioning services | NR positioning support
UE Capabilities | Optimisations on UE radio capability signalling | Optimisations on UE radio capability signalling – NR/E-UTRA Aspects
5G Satellite Aspects | Architecture aspects for using satellite access in 5G, Integration of Satellite Access in 5G | Solutions for NR to support non-terrestrial networks (NTN)
Common 5G focus areas across Radio Access Network and System / Core Network
Many other features have impacts across the system (both in RAN and non-RAN areas), however, these are mainly handled on one side or the other. They require alignment not significant coordination.

## Slide 11: 3GPP Rel-16: Ongoing Studies (2/3)
Stage 1 (Rel-17): Asset tracking, Critical Medical Applications, Unmanned Aerial Vehicles, Audio Visual Service Production…
Stage 2 (Rel-16) (beyond the previous slide)
  Efficiency: Enablers for Network Automation for 5G, Access Traffic Steering, Switch and Splitting support in the 5G System
  New Capabilities: Wireless Wireline Convergence, Enhancements to Network Slicing, to Service Based Architecture, CIoT for 5G
  Security for each aspect on this slide and the previous slide

## Slide 12: 3GPP Rel-16: Ongoing Studies (3/3)
Media
  eXtended Reality (XR) in 5G, QoE metrics for VR, V2X Media Handling and Interaction…
OAM
  Self-Organizing Networks, Tenancy in 5G network and network slicing management, Integration of ONAP and 3GPP aspects, Management of edge computing, …
Application
  Mission Critical services support over the 5G System

## Slide 13: Summary
In Rel-15 5G specifications supported the foundation for many services enablers – mainly for eMBB and some URLLC.
In Rel-16
  5G specifications will support URLLC and mIoT extensively, and increasing OAM and media capabilities.
  We have extensive and fruitful collaboration with different business sectors, e.g. fixed networking, satellite communications, automotive, industrial automation.
In Rel-17 we already see even more engagement, e.g. in logistics, e-health, unmanned aerial vehicles and more.

## Slide 14
www.3gpp.org
For more Information:
info@3gpp.org
Erik.Guttman@samsung.com