## Slide 1: Anticipations for the Final IMT-2020 Submission: Rel-16 Outlook for System and Core Network Aspects
Erik Guttman 3GPP TSG SA Chairman Samsung R&D Institute UK

## Slide 2: System and Service aspects in the IMT-2020 submission

## Slide 3: IMT-2020 Submission Non-Radio Aspects
As in past IMT submissions, 3GPP will include an informative list of all non-RAN specifications.
  It is important to emphasize that the 3GPP system is much more than the 3GPP radio aspects.
  This list will include fewer specifications than in past submissions, as the 5G system explicitly does not support full backward compatibility with the 2G and 3G system (IMT-2000).

## Slide 4: 5G 3GPP Specifications
5G specifications began in Release 15.
  These specifications include not only the new 5G components, but also the continuing evolution of the 4G system.
New 5G specifications have been introduced across 3GPP.
Some 4G specifications are now 5G specifications, from Rel-15
  The Enhanced Packet Core and other 4G standards are important components of 5G.
  Operators will deploy and integrate 5G functionality in different ways, including continuing use of the EPC for some time.
  See TS 21.205 – which links to a list of 1113 specifications.

## Slide 5: System and Service aspects in Release 16

## Slide 6: System and Core Network Aspects
System and Core Network Aspects, as discussed in this presentation, include everything in scope of 3GPP standardization except Radio Access Network aspects.
System Aspects include: Security, Media and Codecs, Operations and Management, Applications, Terminal and End to End Aspects, Interworking with External Networks and Smart Card Application Aspects
Core Network Aspects include: all functions to support for services provided by the 3GPP system.
  These categories are somewhat arbitrary. Some functions could be considered both Core Network and System Aspects.

## Slide 7: Overview of System & CN Aspects (1/2)
Stage 1 – Service Requirements for 5G
  TS 22.261 “New Services and Markets Technology Enablers”
Stage 2 – 5G System defined in
  TS 23.501 “System Architecture for the 5G System”
  TS 23.502 “Procedures”
  TS 23.503 “Policy and Charging Control Framework for the 5G System”
  TS 33.501 “Security architecture and procedures for 5G System”
Stage 1 – Service Requirements for 5G
  Adds requirements for verticals from Industrial & Vertical automation, 5G Satellite, LAN support, High Precision Positioning, QoS Monitoring. New specification TS 22.104 on Cyber-Physical Control Applications.
Stage 2 – 5G System expands in
  Adds support to the TSs for verticals: URLLC, 5G LAN, 5GC Location Services, Enhanced V2X, Cellular IoT
  Adds support for new accesses: Wireless Wireline Convergence, Satellite, SRVCC from 5GS to 3G
  Enhancements to the base system: Network Automation, Traffic Steering/Switch/Splitting, Service Based Architecture, Network Slicing, Radio Capabilities, User Data Interworking…
Release 15 (5G Phase 1)
Release 16 (5G Phase 2)

## Slide 8: Overview of System & CN Aspects (2/2)
Stage 2, continued
  Application : TS 23.222 “Common API Framework for 3GPP Northbound APIs”
  Media: TS 26.118 “3GPP Virtual reality profiles for streaming applications”
  Charging*: TS 32.291 “5G System Charging Service”
  OAM*: TS 28.530..554 “Management and orchestration”, many aspects
  OAM*: TS 28.304..306 “Control and Monitoring of Power, Energy and Envirnomental Parameters”
Stage 2, continued
  5G Support for verticals: Mission Critical support over 5G (Spec TBD), V2X Application support (Spec TBD)
  5G support for media: coverage and handoff enhancements, QoE metrics for VR, 5G Mobile Broadband Media Distribution, V2X Media Handling, Extensions or 5G Conversational Services, Many enhancements, study on XR (Extended Reality) (Specs TBD)
  OAM support extends to: ONAP interworking for Configuration Management, Data Collection, Analytics and Events, Self-Organizing Networks, QoE measurement collection, slice management, energy efficiency, orchestration & virtualization….
Release 15 (5G Phase 1)
Release 16 (5G Phase 2)

## Slide 9: 3GPP Rel-16: Ongoing RAN-SA Studies
Focus Area | System Studies | RAN Studies
URLLC for 5G | Enhancement of URLLC support in 5G, Enhanced support of Vertical and LAN Services, Cyber-physical control applications in vertical domains | Physical layer enhancements for NR UR Low Latency Cases, NR-based access to unlicensed spectrum, NR Industrial Internet of Things
V2X for 5G | Architecture enhancements for 3GPP support of advanced V2X services | NR Vehicle-to-Everything (V2X)
Positioning | Enhancement to the 5GC Location Services, 5G positioning services | NR positioning support
UE Capabilities | Optimisations on UE radio capability signalling | Optimisations on UE radio capability signalling – NR/E-UTRA Aspects
5G Satellite Aspects | Architecture aspects for using satellite access in 5G, Integration of Satellite Access in 5G | Solutions for NR to support non-terrestrial networks (NTN)
Common 5G focus areas across Radio Access Network and System / Core Network
Many other features have impacts across the system (both in RAN and non-RAN areas), however, these are mainly handled on one side or the other. They require alignment not significant coordination.

## Slide 10: 3GPP Rel-17: Things to come
Stage 1 (Rel-17): So far
  Asset tracking
  Critical Medical Applications
  Unmanned Aerial Vehicles
  Audio Visual Service Production
  Maritime
  Extended Reality
Ongoing development will occur for
  Automotive, Railway, Maritime sectors
  Industrial Automation
  Critical Communications
  Fundamental enablers: IoT, Broadcast, Slicing, Network Automation, Orchestration and Management

## Slide 11: Summary
In Rel-16 adds 5G Vertical support
  Vehicle Communication, Mission Critical Communications, Industrial Automation and Verticals, Audio Visual Production,
Rel-16 also adds enhances the system
  5G LAN, High Precision Positioning, Cellular IoT for 5G, URLLC capabilities, Fixed and Satellite as 3GPP accesses, ONAP interworking, QoS Monitoring, Network Automation, protocol and core network improvements…
In Rel-17 – more verticals and service enablers
  logistics, e-health, unmanned aerial vehicles…
  XR, …

## Slide 12
www.3gpp.org
For more Information:
info@3gpp.org
Erik.Guttman@samsung.com