## Slide 1: Panasonic view on 6G RAN
Sources: Panasonic
3GPP workshop on 6G
Incheon, Korea, March 10-11, 2025
Agenda: 4
TDOC: 6GWS-250034
For: discussion

## Slide 2: New RAT as module level introduction
NR design takes into account forward compatibility. Many of features have been and would be introduced without new framework thanks to following.
  Design of minimizing always-on signal
  Flexibility on subcarrier spacing
  Flexibility on PDCCH reception like CORESET concept
  PDSCH/PUSCH is flexible resource assignment
  Flexible design on PUCCH, SRS, DMRS, PRS and so on.
There are strong views on the need of smooth evolution and software oriented [4][5].

## Slide 3: New RAT as module level introduction
Even based on NR framework of subframe/slot framework, new technology would be possible to be introduced.
  Radio interface enhancement like extreme-MIMO, in-band full duplex, reconfigurable intelligent surfaces and so on could be introduced by certain subframe.
  THz and OAM may require some numerology but the framework may be still kept.
    Introduction of PA friendly DL, e.g. SC-FDMA based DL may require framework change and careful study would be required.
  Radio network enhancement like ultra-dense network, user-centric network, native-AI enabled RAN functions, ubiquitous connectivity and so on would not require the drastic change of airinterface.
  Integrated sensing and communication may require some new reference signal but would be able to be introduced in NR framework.

## Slide 4: New RAT as module level introduction
Introduce new change as module level.
  Full redesign for new RAT is not required.
  More flexibility on “backward compatibility”
    Even if initial access per cell is different,
      it can be backward compatible by multiple cells.
      other functions are compatible allows smooth introduction.
NR framework
NR framework
Module
NR
Initial
access proceudre
New
Initial
access proceudre
New
paging
NR
paging

## Slide 5: New numerology and FEC
Numerology and Time/frequency resource usage?
  Current subcarrier spacing of 15, 30, 60, 120, 240, 480 and 960 kHz is flexible enough. If necessary, other spacing like 7.5 kHz, 1920 KHz can be introduced.
  As far as subframe/slot concept is kept, new waveform other than OFDM/DFT-s-OFDM could be introduced.
    Scalable numerology in NR is to keep the number of symbols in a slot, which reduces the coverage when Tx power has the limitation. To keep slot length may be another alternative.
  Similar to NB-IoT and/or eMTC, certain time/frequency resource can be reserved e.g. for Ambient IoT.
New FEC coding scheme?
  New coding scheme than Polar coding and LDPC can be introduced for PDCCH/PUCCH/PDSCH/PUSCH when/if necessary.

## Slide 6: Initial access procedure
Initial access procedure of non-backward compatibility can be considered e.g. for FR3. It can be also for existing frequency range when other than synchronization raster is used.
  Although current one shot reception principle of SSB allows flexibility, 20ms default UE assumption and maximum 160ms periodicity of SSB have limitation on network power saving.
  TDM/FDM of multiple of SSB in a cell sometimes limit resource utilization.
    Optimized design for analogue beam forming of TDM in FR2 has limitation on network power saving.
  Fixed design of CORESET0 makes congestion on the DL control and limit operational flexibility.

## Slide 7: System information, paging, random access
System information design
  MIB/SIB content can be more than self-provisioning cell but can be obtaind as pre-configuration.
    It can be obtained from other cells of 4G/5G or even from WiFi via application layer. It would be similar to sidelink pre-configuration or eSIM provisioning.
      “The information in SIB1 does not frequently change. .. The configuration to request SIB1 could be kept static and minimal.” in [6]
    Only index can be sufficient over the air for pre-configuration case. The configuration change is just to indicate the change of index.
    PLMN selection may be limited to the cell of self-provision.
Paging resource usage
  More flexibility on the resource usage. Not limited to TDM of SSB for Network energy saving.
  More direct integration of LP-WUS.
Random access resource usage
  To avoid excessive preamble resource usage for SSB/QoS/UE type distinction. Msg3 can be modified.
  More flexibility on the resource usage.

## Slide 8: L1 signalling
“L1 indication of the index of configured/pre-configured table” can minimize the signaling without limiting the flexibility.
  PDCCH time domain resource allocation table in NR is good example.
  Other fields can be designed by configured table index manner for better extension with the reduction of payload size.
CORESET size should be allowed more than 3 symbols for better reliability of PDCCH.
Number of Blind decoding for PDCCH can be increased as it has been same over 2 generations. This is especially for hyper reliable and low latency communication.
Simplification of PUCCH and PUSCH relation on the interaction.
UCI design should be more generalized instead of HARQ-ACK and CSI feedback.
  Such moduler design allows more flexible UCI e.g. AI based CSI feedback.

## Slide 9: BWP
BWP was designed too flexible.
  Some more limitation on the candidates parameters would be required to obtain the merit.
    Current 1 PRB granularity of BWP is difficult to realize AD/DA power saving merit.
BWP has several limitations and it can be enhanced.
  BWP was designed only within time/frequency resource. The concept can be extended for spatial domain as “beam”. i.e. TCI and BWP interaction/integration.
  BWP is not required to be limited only within one cell/carrier.
    A BWP can be mapped in the other carrier, which makes “a cell” to be virtualized for efficient NES operation.

## Slide 10: L2 and L3
Some reconsideration on the relation among L1, L2 and L3
  Some function may be duplicated just because of the difference of the layer like mobility relation. Faster RRC can simplify them?
  CU/DU split and RRC/MAC split relation?
For AI performance monitriong and model transfer/delivery, fat c-plane almost same as u-plane would be required.
Ambient IoT requires redesign of the protocol but can be progressed independence of 6G. It would be one of essential component of 6G.

## Slide 11: References
[1] Rec. ITU-R M.2160 Framework for IMT 2030
[2] Rep. ITU-R M.2516 Future Technology Trends
[3] Beyond 5G White Paper, eyond 5G Promotion Consortium
[4] “6G POSITION STATEMENT”, NGMN Alliance
[5] S1-241189, “Vodafone’s view on 6G”, Vodafone, SA1#106
[6] RP-242141, "On demand SIB 1 and the need for case 1 for multi-vendor RAN", Vodafone, Deutsche Telekom, Orange, Lenovo, Google, Fraunhofer IIS and Fraunhofer HHI, ETRI, CEWiT", RAN#105