## Slide 1: 3GPP & O-RAN ALLIANCE Joint Workshop on 6G Coordination 3GPP and O-RAN – RAN testing
3ORW-250013
Keysight Technologies
April 24-25, 2025
Sophia Antipolis, France

## Slide 2
3GPP and O-RAN – RAN Testing
Key Areas
1. 6G RAN Architecture
3GPP defines the overall 6G architecture
O-RAN updates/creates its 6G specifications based on 3GPP 6G architecture decisions
2. Open Fronthaul
3GPP defines the 6G air interface
O-RAN specifies the fronthaul interface for 6G
3. SMO and Automation
3GPP evolves RAN & Core domain management architecture
O-RAN continues to evolve the SMO architecture and services for RAN management systems in 6G.
3GPP and O-RAN align to ensure unified architecture, services, and NRM
4. Intelligence including AI/ML
3GPP specifies an AI/ML architecture and related LCM aspects that enables AI/ML use cases support across CN, RAN, OAM, and UE.
O-RAN aligns with the 3GPP specified AI/ML architecture and functional frameworks and strives for consistent data management and LCM aspects aligned across both organizations.
O-RAN leads the development of additional complementary AI/ML services and automation use cases
5. Cloud
Cloudification of network functions and cloud infrastructure management aspects are expected to be out-of-scope for 3GPP.
O-RAN specifies cloudification of network functions and cloud infrastructure management aspects.
O-RAN evolves SMO management of the cloud infrastructure and deployment in 6G.
6. Security
3GPP and O-RAN should strive to define a consistent 6G security architecture with complementary capabilities
Reference
[Source: 3ORW-250020 - Work split between 3GPP and O-RAN ALLIANCE for 6G coordination]

## Slide 3
3GPP and O-RAN – RAN Testing
1. 6G RAN Architecture
3GPP (listing test specs work which are/can be leveraged to O-RAN) | O-RAN ALLIANCE
Not Available - from the RAN full protocol stack testing perspective | NR - O-RAN test specifications for E2E, Security, 3GPP interfaces interoperability profiles (e.g. F1, X2, Xn) 6G - continue to evolve test specifications based on the 6G architecture aligned between 3GPP and O-RAN ALLIANCE
3GPP E2E (RAN) Tests
RAN
Real UEs /
UE Emulator
Core / Core Emulator
3GPP interfaces Interoperability profiles Tests (e.g., F1)
gNB-DU
gNB-CU
Real UEs /
UE Emulator
O-CU and Core Emulator
System Under Test (gNB)
O-RAN interfaces Conformance and Interoperability Tests
SMO
O-RUs
Non-RT RIC
O-CU
O-DU
Near RT RIC
xApps
R1
rApps
rApps
O-Cloud
O1
E2
O1
A1
WG4 M-Plane
Y1
O-Cloud Notification APIs
R1 Services
Transport
Near RT RIC API
E2
Fronthaul
xApps
F1
O2
Open RAN
WG2 Conformance & Interoperability Tests (A1, R1)
WG3 Conformance & Interoperability Tests (E2)
WG4 Conformance & Interoperability Tests (Fronthaul)
WG6 Conformance & Interoperability Tests (Cloud)
WG8 Interoperability Tests (Stack)
WG9 Transport Tests
TIFG E2E Tests
WG11 Security Tests
WG5 Interoperability Tests (X2, Xn, F1)
NOTE: Test specifications for LTE are available but not referenced in this contribution

## Slide 4
3GPP and O-RAN – RAN Testing
2. Open Fronthaul
3GPP (listing test specs work which are/can be leveraged to O-RAN) | O-RAN ALLIANCE
NR - Base Station Conformance (TS 38.141, 141-1, 141-2) 6G - continue to evolve Conformance tests (e.g. extend to FR3) | NR - O-RAN WG4 fronthaul Conformance & Interoperability tests (IOT) 6G - continue to evolve O-RAN fronthaul conformance and IOT
4
BS Transmitter Tests
BS Receiver Tests
Example
[Source: 3GPP TS 38.141-1, Figure D.1.1-1]
Example
[Source: 3GPP TS 38.141-1, Figure D.2.1-1]
O-RU
O-DU Emulator
Signal Analyzer
3GPP Conformance Tests
O-RU
Signal Source
O-DU Emulator
BS under TX test
BS under RX test
O-RAN Fronthaul Conformance Tests
O-RU
Signal Source and Analyzer
O-DU Emulator
O-DU
UE + O-RU Emulator
O-CU and Core Emulator
O-RAN Fronthaul Interoperability Tests
O-RU
O-DU
Real UEs /
UE Emulator
O-CU and Core Emulator
NOTE: Test specifications for LTE are available but not referenced in this contribution

## Slide 5
3GPP and O-RAN – RAN Testing
3. SMO and Automation
3GPP (listing test specs work which are/can be leveraged to O-RAN) | O-RAN ALLIANCE
Not Available | Develop test cases for SMO and Automation
Reference
[Source: O-RAN Architecture Description - Figure 5.3.1.2.1-1: SMOSs in the SMO SBA representation]
SMO Service (SMOS): Standardized cohesive set of management, orchestration and automation capabilities offered by an SMO Function.

## Slide 6
3GPP and O-RAN – RAN Testing
4. Intelligence including AI/ML
3GPP (listing test specs work which are/can be leveraged to O-RAN) | O-RAN ALLIANCE
6G - Develop AI/ML Test and Evaluation framework taking into considerations requirements to support AI/ML use cases across CN, RAN, OAM, and UE | NR - O-RAN test specs for R1 and RIC-enabled use cases 6G - Develop AI/ML Test and Evaluation framework taking into considerations the RIC architecture, rApps and interfaces
Example
[Source: O-RAN R1 Interface Test Specification, Figure 4.2.2.1-1: Illustration of R1 conformance testing of rApps]
DUT
Test Simulator
Common Requirement - Operators are keen to evaluate the benefits / gains versus the complexity, cost and tradeoffs for “Network for AI” and “AI for Network” use cases in a consistent and quantitative manner.
Common Challenge - Current approach to AI/ML requires considerable efforts to analyze achievable benefits, complexity increase, testability aspects and normative work per use case.
Proposal - 3GPP and O-RAN to consider collaborating on AI/ML Test and Evaluation framework in the following listed candidate common areas
LCM aspects that enable AI/ML use cases support concerning RAN
Digital twin approach (including datasets) for models training, testing, evaluation and validation
Multi-domain KPIs definition, including the complexity and impacts (such as energy consumption) for use cases of common interests in both organizations.
O-RAN R1 / rApps Tests
NOTE: Test specifications for LTE are available but not referenced in this contribution

## Slide 7
3GPP and O-RAN – RAN Testing
5. Cloud
3GPP (listing test specs work which are/can be leveraged to O-RAN) | O-RAN ALLIANCE
Not within 3GPP scope of work | Continue to develop test cases for O-Cloud, O2 interface and Acceleration Abstraction Layer (AAL)
O-RAN O-Cloud Interoperability Testing
WG6 Interoperability Tests (Cloud)
  Notification API
  Acceleration Abstraction Layer (AAL) Interface
  O2 Interface (Infrastructure & Deployment Management Services)
WG6 Conformance Tests (Cloud)
O-RAN O-Cloud Interface Conformance Testing
Example
[Source: O-Cloud Interface Conformance Test Specification, Figure 4.1-1: The overview of O-Cloud Interface test]
SMO
O-RUs
Non-RT RIC
O-CU
O-DU
Near RT RIC
xApps
R1
rApps
rApps
O-Cloud
O1
E2
O1
A1
WG4 M-Plane
Y1
O-Cloud Notification APIs
R1 Services
Transport
Near RT RIC API
E2
Fronthaul
xApps
F1
O2
Open RAN

## Slide 8
3GPP and O-RAN – RAN Testing
6. Security
3GPP (listing test specs work which are/can be leveraged to O-RAN) | O-RAN ALLIANCE
NR - SCAS General (TS 33.117), gNB (TS 33.511) 6G - continue to evolve 3GPP SCAS in General and for RAN (e.g., including Post Quantum Cryptography (PQC) etc.) | NR - Continue to develop test cases for O-RAN specific network functions, apps, interfaces and additional security test cases (on top of 3GPP SCAS) 6G - Define 6G security test requirements based on the 6G security architecture aligned between 3GPP and O-RAN ALLIANCE.
Security Assurance Specification (SCAS) for gNB
O-RAN End-to-End Security Testing
gNB
Real UEs /
UE Emulator
Core / Core Emulator
Example
[Source: O-RAN Security Test Specification, Figure 24-3: C-Plane eCPRI DoS Attack Test Setup]
WG11 Security Test Specification
NOTE: Test specifications for LTE are available but not referenced in this contribution

## Slide 9
3GPP and O-RAN – RAN Testing
Summary
Areas | 3GPP (listing test specs work which are/can be leveraged to O-RAN) | O-RAN ALLIANCE
1. 6G RAN Architecture | None from the RAN full protocol stack testing perspective | NR - O-RAN test specifications for E2E, Security, 3GPP interfaces interoperability profiles (e.g. F1, X2, Xn) 6G - continue to evolve test specifications based on the 6G architecture aligned between 3GPP and O-RAN ALLIANCE
2. Open Fronthaul | NR - Base Station Conformance (TS 38.141, 141-1, 141-2) 6G - continue to evolve Conformance (e.g. extend to FR3) | NR - O-RAN WG4 fronthaul Conformance & Interoperability 6G - continue to evolve O-RAN fronthaul conformance and IOT
3. SMO and Automation | Not Available | Develop test cases for SMO and Automation
4. Intelligence including AI/ML | 6G - Develop AI/ML Test and Evaluation (T&E) framework taking into considerations requirements to support AI/ML use cases across CN, RAN, OAM, and UE | NR - O-RAN test specifications for R1 and RIC-enabled use cases 6G - Develop AI/ML Test and Evaluation framework taking into considerations the RIC architecture, rApps and supporting interfaces
 | Collaborating on the AI/ML T&E framework in common areas of interest (a) LCM aspects (b) Digital twin approach (inc. datasets (c) KPIs | 
5. Cloud | Not within 3GPP scope of work | Continue to develop test cases for O-Cloud, O2 interface and Acceleration Abstraction Layer (AAL)
6. Security | NR - SCAS General (TS 33.117), gNB (TS 33.511) 6G - continue to evolve 3GPP SCAS in General and for RAN (e.g., including Post Quantum Cryptography (PQC) etc.) | NR - Continue to develop test cases for O-RAN specific network functions, apps, interfaces and additional security test cases (on top of 3GPP SCAS) 6G - Define 6G security test requirements based on the 6G security architecture aligned between 3GPP and O-RAN ALLIANCE.
NOTE: Test specifications for LTE are available but not referenced in this contribution

## Slide 10: Thank You