## Slide 1: 3GPP & O-RAN ALLIANCE Joint Workshop on 6G Coordination: Summary
Source:
Puneet Jain (3GPP TSG SA Chair)
Axel Klatt (3GPP TSG RAN Vice Chair)
Douglas Knisely (O-RAN SDFG Co-chair)
Kei Andou (O-RAN WG4 Co-chair)
3ORW-250035
AI# 4
3ORW-250035, 3GPP - O-RAN ALLIANCE Joint Workshop on 6G, Sophia Antipolis, France, 24 - 25 April 2025

## Slide 2: 3GPP & O-RAN ALLIANCE Joint Workshop on 6G Coordination
Workshop Presentations: Link
Objectives:
  To share high-level information of 3GPP (e.g., 3GPP structure, 6G schedule, and planned studies (plenary level and working group level), and O-RAN
  To invite contributions regarding interaction and collaboration between 3GPP and O-RAN, including detailed areas (e.g., fronthaul, SMO, RIC, etc.) and time planning
  To establish a high-level understanding of the work split between 3GPP and O-RAN, future cooperations (e.g., work plannings, means of cooperations, etc.), etc., in order to avoid any fragmentation or conflict
418 registrations, 130 in-persona registrants.
23 input contributions
April 24th to 25th 2025, Sophia Antipolis, France
Time | Thursday April 24th | Friday April 25th
1st session (09:00 – 10:30) | AI 1: Opening AI 2: Introduction AI 3: Interaction and Collaboration between 3GPP and O-RAN | AI 3: Interaction and Collaboration between 3GPP and O-RAN – Cont’d
Morning break (10:30 – 11:00) | Morning break | Morning break
2nd session (11:00 - 12:30) | AI 3: Interaction and Collaboration between 3GPP and O-RAN | AI 3: Interaction and Collaboration between 3GPP and O-RAN – Cont’d (6) AI 4: Summary
Lunch break (12:30 – 14:00) | Lunch | Lunch
3rd session (14:00 – 15:30) | AI 3: Interaction and Collaboration between 3GPP and O-RAN – Cont’d | AI 4: Summary AI 5: Closing (no later than 4:00pm)
Afternoon break (15:30 – 16:00) | Afternoon break | 
4th session (16:00 – 17:30) | AI 3: Interaction and Collaboration between 3GPP and O-RAN – Cont’d | 

## Slide 3: General Disclaimer
  The summary is based on a compilation of input papers submitted for the 3GPP - O-RAN workshop on 6G coordination and the discussions held during the workshop.
  The summary is non-binding and does not reflect any formal agreement, as the workshop has no decision-making authority.
  Any further discussions, consensus-building, and formal agreements are expected to occur within the respective organizations.

## Slide 4: General Themes
  3GPP and O-RAN commit to establish a common understanding of each of the organization's roles that support the success of 6G.
  The industry should leverage the strengths of both organizations to streamline development and minimize fragmentation.
  Duplication between 3GPP and O-RAN is to be avoided.

## Slide 5: High level principles on 6G collaboration
  3GPP defines the 6G Specifications. O-RAN will complement 3GPP 6G specifications to support its use cases.
  3GPP defines the overall 6G architecture. O-RAN updates/creates O-RAN specifications related to 6G based on 3GPP 6G architecture decisions in parallel, where feasible.
  3GPP and O-RAN can use LS and company contributions for collaboration.
  The need for follow-up co-ordination/checkpoints can be evaluated between the two organizations.

## Slide 6: Timeline and availability of 6G specifications
  3GPP published their 6G workplan/timeline (see 3ORW-250002, slide 9 to slide 11).
  O-RAN strives for alignment of its 6G release cycles with 3GPP for timely 6G specification delivery.

## Slide 7: 6G Fronthaul Interface
  3GPP defines the 6G air interface.
  O-RAN specifies the fronthaul interface including LLS for 6G.
  Some companies proposed to include a Radio Unit (RU) as standalone entity in 3GPP RAN architecture and reference the O-RAN fronthaul specification in 3GPP specifications.
  Some companies proposed to not include Radio Unit (RU) in 3GPP RAN architecture and not reference the O-RAN fronthaul specification in 3GPP specifications.
  Some companies proposed the following compromise as a package for 6G:
    3GPP to capture the following in a [normative] Annex of TSxx.401 (RAN3) or TSxx.300 (RAN2)
      6G NodeB may include a Radio Unit (RU).
      The functions hosted by the RU as well as the interface between RU and other parts of 6G NodeB is not specified in 3GPP.
    RU and the interface between RU and other parts of 6G NodeB are not shown in the 3GPP 6G architecture or other parts of 3GPP 6G specifications.
    3GPP is not to reference O-RAN specifications relating to the interface between RU and other parts of 6G NodeB.
  These proposals require further discussion/endorsement within 3GPP TSG RAN.

## Slide 8: AI/ML
  3GPP specifies an AI/ML architecture and related LCM aspects that enable an operator to support AI/ML use cases across CN, RAN, OAM, and UE.
  O-RAN aligns with the 3GPP specified AI/ML architecture and functional frameworks and strives for consistent data management and LCM aspects aligned across both organizations.
  O-RAN specifies complementary AI/ML services/functionalities for additional use cases including automation.

## Slide 9: SMO and Automation
  3GPP remains responsible for RAN and CN management architecture and management services for 6G.
  O-RAN continues to evolve the SMO Architecture and services for RAN management systems including O1, O2 and M-Plane interfaces.
  3GPP and O-RAN align to ensure unified management architecture, services, and NRM.

## Slide 10: Other Areas
  Cloud
    3GPP specifications are agnostic to whether the network runs on cloud infrastructure or not. 3GPP management system continues to act as a consumer of cloud management.
    O-RAN specifies cloudification of network functions and cloud infrastructure management aspects
  Security
    3GPP and O-RAN strive to define a consistent 6G security architecture with complementary capabilities
  Testing
    Collaboration on the testing aspects can be evaluated between the two organizations.
  Process
    Some companies suggested O-RAN to make draft O-RAN specifications and other working documents publicly available.