## Slide 1: Delay spread vs hall volume

## Slide 2: Background (1)
In R1-1905202 in Xi’an, Ericsson and CEA-LETI compiled all contributions on RMS delay spread in Industrial halls
  Based on the compilation, Ericsson proposed a model for the delay spread that is dependent on the hall volume

## Slide 3: Background (2)
In the email discussion [97-NR-10] different proposals on LSP parameters including DS have been collected
  Includes the hall volume-dependent function but also proposals based on new measurements and simulations
The purpose of this presentation is to see whether these proposals support or contradict the volume-dependent model proposal

## Slide 4: Parameter proposals converted to 99th percentile
For a Gaussian distribution, the 99th percentile is equal to: mlgDS+2.33*slgDS
Using the LSP DS proposals in [97-NR-10] and also additional contributions to the F2F as summarized in R1-19xxxxx LSP parameter proposals_v4_HHI.XLSX, the 99th percentiles in NLOS have been estimated as follows:
Source | Hall volume, V [m3] | Estimated 99th percentile DS [ns] | Notes
ZTE | 360000 | 230-376 | Ray-tracing
CMCC | 42000 | 336-381 | 
DOCOMO |  |  | Data already included in previous compilation
CEA-LETI | ? | 192 | Hall volume unknown
Huawei: Shanghai | 150000 | 1074 | Large sigma gives very high 99th percentile. Possibly better to check 99th percentile directly on measurement data?
Huawei: Munich | 2875 | 60-91 | Slightly reducing with frequency
Fraunhofer HHI + IIS | 8126-65541 | 30-270 | Hall sizes taken from arxiv paper DS is increasing with Tx height and frequency
Fraunhofer HHI | ~51000 | 130 | 

## Slide 5: Adding these proposals to the plot of DS vs hall volume
New additions compared to R1-1905202 in red
These additions appear to be reasonably aligned with the model
  Exception: the Huawei results from Shanghai appears to be an outlier due to a large s – can the 99th percentile be assessed directly from data instead?
  CEA-LETI results can be included if hall volume can be supplied
ZTE
Huawei: Shanghai
(1074 ns, outside range of plot)
Huawei: Munich
Fraunhofer HHI + IIS (range due to frequency- and height-dependence)
CMCC

## Slide 6: Summary
Observations
New proposals and results appear to confirm trend of increasing DS with hall volume
Conflicting frequency dependence trends:
  Huawei observes 30% decrease from 6.75 GHz to 60.75 GHz
  Fraunhofer HHI observes 4x increase from 2 to 6 GHz
  ZTE observes almost flat trends over 2 to 100 GHz
Range of variability between different measurements is much larger than any differences between sub-scenarios
Proposals
Model DS as frequency-independent
Use common model for all NLOS sub-scenarios
Use the model proposed by Ericsson as this seems be in line with most other proposals and observations