## Slide 1: Components of Mobility Latency
FFS whether the time to use a high-performance beam (CSI-RS measurement and TRS tracking) should be included
UE reconfiguration
DL synchronization
UL synchronization
TRRC
Tprocessing,1
Tsearch
TΔ
Tmargin
TIU
TRAR
Tmeas
Candidate config
Cell switch command
10ms
5ms
0ms
20ms
2ms
15ms
4ms
RAR
Preamble
interruption
New cell & TCI state
Tcmd
Tprocessing,2
Target appears
[Rapp] The figure is provided here for easier editing. Please copy-paste your revision to the Word file.

## Slide 2
Component | Meaning | Value
TRRC | Processing time for RRCReconfiguration carrying candidate configurations | Up to 10ms
Tprocessing,1 / Tprocessing,2 | Time for UE processing, before/after cell switch command. This may include L2/3 reconfiguration, RF retuning, baseband retuning, security update, etc. | Total up to 20ms
Tmeas | The time UE measures target cell (from candidate configuration to cell switch command) | -
Tcmd | Time for processing L1/L2-based cell switch command (HARQ and parsing) | Up to 20ms
Tsearch | Time required to search the target cell | 0ms (assume cell is known)
TΔ | Time for fine tracking and acquiring full timing information | SMTC periodicity (typ. 20ms)
Tmargin | Time for SSB post-processing | Up to 2ms
TIU | interruption uncertainty in acquiring the first available PRACH occasion in the new cell | Typ. 15ms
TRAR | Time for RAR delay | Typ. 4ms