## Slide 1: TEI17_IPU
Discussion material for SA2 conference call
January 18, 2021
Stefan Rommer (Ericsson)

## Slide 2: TEI_IPU
Objective:
  Define support of providing IP pool information from UDM to SMF as part of SM level subscription data. The solution will apply to non-roaming and home-routed roaming cases where UDM and SMF are in the same PLMN.

## Slide 3: Rel-15/16 background
SMF may allocate UE IP address before or after it establishes the SM policy association with PCF (see e.g. 23.502, clause 4.3.2.2.1)
The following cases apply:
  If SMF allocates UE IP address before SM policy association establishment:
    SMF allocates UE IP address and provides it to PCF in the Create request.
    PCF will not provide an “IP Index” to SMF in the Create response
  If SMF allocates UE IP address after SM policy association establishment:
    SMF does not provide UE IP address to PCF in the Create request.
    PCF may provide an “IP Index” to the SMF in the Create response
    SMF allocates UE IP address and provides it to PCF in a later Update request.
The SMF may use “IP Index” to assist in selecting how the IP address is to be allocated when multiple allocation methods, or multiple instances of the same method are supported

## Slide 4: Possible cases in rel-17
Add support for providing IP pool information from UDM to SMF as part of SM level subscription data
SMF allocates UE IP address before SM policy association establishment:
  UDM does not provide “IP index” to SMF
    Same as in rel-15/16
  UDM provides “IP index” to SMF
    New in rel-17
  In either case, SMF allocates UE IP address and provides it to PCF in the SM policy association Create request
   PCF will not provide “IP Index” to SMF
SMF allocates UE IP address after SM policy association establishment:
  UDM does not provide “IP index” to SMF
    Same as in rel-15/16
  UDM provides “IP index” to SMF
    New in rel-17
  In either case, SMF does not provide UE IP address in the SM policy association Create request.
   PCF may provide an “IP Index” to the SMF in the Create response
   If SMF received an “IP Index” from both UDM and PCF, the PCF-provided value applies

## Slide 5: EPS IWK
N7 is used when UE is on 4G side and 5G side
  So in case PCF provides IP Index, it can apply also when the UE established a PDN Connection in 4G to PGW-C+SMF
Proposal: In case UDM provides IP Index, SMF may retrieve the SM subscription data from UDM also when UE connects via 4G, in similar way as already supported today for Subscribed S-NSSAI