## Slide 1: MAC-CE Risk Analysis Methodology
Niraj Rathod
SA3 Delegate, Ericsson

## Slide 2: Methodology
  Identify:
    For January 2026 conference call#2, identify type of information in MAC-CE that is security critical. E.g., identity (C-RNTI).
      Prioritize (P1) MAC-CE that carry such information.
    Ambition for February 2026 meeting:- to get an agreed converged shortlisted specific MAC-CE from RAN2, that are time-critical and are sensitive to overhead. An LS from RAN2 to SA3 with shortlisted MAC-CE would help know RAN2 identified time-critical MAC-CE. SA3 may risk analyze these, if not covered in (A) above.
  Analyze: review security risks for information carried only for above prioritized + (RAN2 shortlisted) MAC-CE.
    Use STRIDE threat modelling tool for risks resulting from violation of identity, privacy, & CIA triad.
  Evaluate: classify specific risks in high – medium – low categories.
    Place DoS to gNB and privacy (UE’s identity & location) risks in category ‘high’. This becomes SA3 provided bottom line for current MAC-CE and future introduction information in MAC-CE.
    Place resource drain (e.g., UE battery) and QoS degradation related risks in category ‘medium’.
    Place measurement, optimization related performance degradation related risk in category ‘low’.
  Treat: after qualitative risk analysis, prioritize treating agreed ‘high’ risk from #3 above.
  Risk tolerance: Discuss and agree risk appetite (risk tolerance) in SA3. E.g., acceptance criteria. If RRC existing procedure provides recovery, does some MAC-CE manifested risk need to be treated?
  Estimated F2F (February 2026) TU consumption to converge on output of MAC-CE risk analysis: 1 TU

## Slide 3: Pros-Cons
Pros:
Methodology makes analysis collaborative between WGs. Do it together, not in silo. Formalizes joint WoW framework between WGs RAN2 – SA3 that can be a precedent for future releases.
Functional and non-functional (i.e., security) consideration, thus 2-dimensional activity by combination of “functional grouping” of MAC-CE from RAN2 and severity categorization based on “security risk classification” from SA3 to determine priority.
Focusing on targeted subset of MAC-CE that has “functional” and “security” implications, not a tedious review of all 80+ MAC-CE.
Methodology helps avert security overkill and preserves core purpose of MAC-CE. i.e., time-criticality where millisecond decisions are made during scheduling runtime. Therefore, methodology also considers input from RAN2 with their shortlisted MAC-CE with such critical considerations of latency and overhead. Also, not all MAC-CE carry security sensitive information so SA3 – RAN2 should remained focused on MAC-CE that matter.
Cons:
Methodology is not a cross-protocol stack or system wide analysis.
WGs inter-dependent so could take additional time and effort.
Requires companies in RAN2 to converge on shortlisting MAC-CE for SA3 to risk analyse.

## Slide 4: Q to RAN2
6G roadmap of MAC-CE. How will RAN2 take into account SA3 risk review of MAC-CE while designing MAC-CE going forward?
Design evolution of control information between 6GR base station and UE. E.g., use and emphasize on MAC-CE in conjunction with RRC
Protocol stack dependent RAN procedures’ implications on time-sensitive MAC-CE processing
Potential new key hierarchy in RAN and its implication on risk management decisions made for 5G NR MAC-CE