## Slide 1: SID proposal for Secure RRC connection Setup
Nokia
Jan 2022

## Slide 2: RRC Connection Setup up to Msg5 is not secure

## Slide 3: Lack of security for RRC Msg5
Since security is lacking for RRC Msg5, sensitive information cannot be shared with the AMF/network or the base station.
This is a basic issue for multiple features, for e.g. in Network Slicing, Non terrestrial networks etc.
If this Msg5 is made secure,
  Network Slice selection parameter could be included outside the NAS packet for BS to parse and route the NAS RR to correct AMF in the desired NS.
  For Non-Terrestrial UEs, location information can be included outside the NAS packet for BS to parse and route the NAS RR to correct AMF.
Msg5 is the last of the remaining messages to be secured and if this is secured a host of issues can be solved with multiple features, like Network Slicing, NTN etc.

## Slide 4: SID Proposal: Secure RRC connection setup
Objective: Study security mechanisms to secure the RRC connection setup procedure so that sensitive information can be shared between genuine network elements BS and AMF even before UE is authenticated and UE specific security context is established.
Both roaming and as well as non-roaming UEs should be under the scope of the study.
Once the UE is authenticated and UE specific NAS and AS security contexts are established, as currently done, messages shall be protected by the UE specific security context.
Parameters within the RRC connection setup messages are not within the scope of the study. They will be defined by respective WGs as necessary based on features.