## Slide 1: Discussion paper on Exposure

## Slide 2
Exposure Architecture – Option 1
EGMF in OSS
Management Service
Management Domain
External customer A
eMnS A
(e.g. exposure IOC)
eMnS B
(e.g. exposure IOC)
eMnS C
(e.g. exposure IOC)
BSS
External customer B
External customer C
eMnS Discovery service for exposure
EGMF
The potential functionalities of EMGF are:
Authentication for exposure
MnS discovery service for exposure
Access control
Exposure IoC
internal MnS consumer
The potential functionalities of internal MnS consumer is:
The internal MnS consumer acts on behalf of the external customer.

## Slide 3
Exposure Architecture – Option 2
EGMF in BSS
Management Service
Management Domain
External Consumer A
eMnS A
(e.g. exposure IOC)
eMnS B
(e.g. exposure IOC)
eMnS C
(e.g.exposure IOC)
BSS
External Consumer B
External Consumer C
The potential functionalities of EMGF are:
TMF API GW, e.g. service catalog
MnS discovery service for exposure
EGMF
(e.g. service Catalog)
eMnS Discovery service for exposure
internal MnS consumer
The potential functionalities of internal MnS consumer are:
The internal MnS consumer acts on behalf of the external customer.
Exposure IoC

## Slide 4
Exposure IOC
- exposure IOC to eMnS consumer in order to make the exposure more customRegroup the IOC regarding Network slice management exposure and exposes the er friendly；
NetworkSlice
operationalState
administrativeState
serviceProfileList
Attribute related to role
networkSliceSubnetRef
eNetworkSlice
ServiceType (live video streaming, V2X, etc)
eServiceProfile
Exposed IOC for video streaming
NetworkSlice
eServiceProfile(live video streaming)
Latency
reliability
DelayTolerance
Jitter
- The exposure IOCs are based on different verticals (e.g. live video streaming) ；
Exposure IOC
- Exposure IOC can be easily used by CSP to serve its external customer；
eServiceProfile(V2X)
Latency
UEMobilityLevel
V2XCommModels
- The exposure IOCs are based on the current concept of NRM；
NetworkSlice
operationalState
administrativeState
serviceProfileList
Attribute related to role
networkSliceSubnetRef
eNetworkSlice
ServiceType (live video streaming, V2X, etc)
eServiceProfile
Exposed IOC template for video streaming
NetworkSlice
eServiceProfile
Attribute1
Attribute2
Attribute3
Attribute4