## Slide 1: Pause points for ACCL
Lenovo, Motorola Mobility

## Slide 2: Rationale
RAN Vendor 1
RAN Vendor 2
Core Vendor 3
ACCL
ACCL
ACCL
NSIMnSP
NSI
Closed loops implemented by a vendor are now deciding how to change an operator network
Vendor implemented ACCLs

## Slide 3: What option does the operator have
Testing – but testing in simulation is different from live network operation
Disable – means no automation
Proposal: Review the actions of the ACCL is about to execute, till you trust the ACCL and then let it run

## Slide 4: Pause points
Solution: The operator can enable a pause for review after execution
CL Execution stage
Network
Notification of pause point
Approval
for resuming the CL
The consumer can enable a pause-point for changes to NF1
Change attribute X for NF1

## Slide 5: Solution options
Option 1: A filter text associated with an ACCL. If the text matches execution stage output the ACCL a notification is sent.
If empty pause is disabled.
Option 2: A datatype with MOI FQDN or ID and Attribute in the MOI associated to an ACCL. When the ACCL modifies that attribute of the MOI a notification is sent.
If NULL pause is disabled.
Proposal: Option 2 is preferred – but open to discussion

## Slide 6: Discussion paper on Conflict Management SID proposal
Lenovo, Motorola Mobility

## Slide 7: Rationale
Automation is picking up momemtum
- Closed loops in Management
- NWDAF assisted closed loops in core
2. Combined with complex management deployment, multi-tenancy and virtualization different automation objectives or intents and corresponding closed loops may exist in the network – there is a high chance that they may conflict.

## Slide 8: What is a conflict?
A conflict is essentially any undesirable state of the network that is caused by one or more entities adversely influencing each others behaviour. Example of conflict in term of 3GPP include:
Contradictory instructions to managed entities, for example, from different CLs
Instructions to managed entities that result in sub-optimal network behaviour
Thrashing – configuration of the same entity in a repeated manner that results in cyclic oscillation
RAN Vendor 1
RAN Vendor 2
Core Vendor 3
ACCL
ACCL
ACCL
NSIMnSP
NSI
These ACCLS can do different sub-optimal things if not correctly coordinated

## Slide 9: Example Causes of conflict – Closed loops
CL Conflict and Coordination analysis for ETSI GS ZSM009-1

## Slide 10: Example conflict – actions from multiple NF instances
Different NF instances may suggest different actions for the same perceived cause causing different parts of the same network to behave differently

## Slide 11: Example of sub-optimal conflict
In this case not all decisions may be needed
OAM should coordinate such behaviour

## Slide 12: Objectives of the SID
The key objectives would be
Identifications of scenarios that result in possible conflicts between closed loops in the management plane or in the control plane (NWDAF assisted closed loops) and requirements towards possible resolutions
Mechanisms for coordinating various aspects, such as but not limited to:
  Enabler for goal configuration coordination of closed loops in management and control plane
  Enablers for pre and post execution coordination in closed loops in management and control plane
  Enablers for management plane coordination of NF actions
  Enabling coordination at the NF