## Slide 1: Discussion paper on way forward for R17 NSA_SBMA
Huawei

## Slide 2: SA5#140e related tdocs
(6164/6165/6392/6580/6581/6618/6619)
Scope extension proposals:
  TS 28.662:
    [SA5#140e], 6.3-MAINT, GROUP#12(S5-216213/S5-216214) Update Generic RAN NRM to be applicable for SBMA
  TS 28.658:
    [SA5#140e], 6.3-MAINT, GROUP#11(S5-216211/S5-216212) CR TS 28.658 Update EUTRAN NRM to be applicable for SBMA
Update of stage2 and stage 3 proposals according to WID scope:
  TS 28.632/633:
    [SA5#140e], 6.4.22-NSA_SBMA, GROUP#1(S5-216092/S5-216398/S5-216401) Inventory Management
  TS 28.659/663:
    [SA5#140e], 6.4.22-NSA_SBMA, GROUP#2(S5-216164/S5-216165/S5-216392) RAN NRM

## Slide 3: Current situation for R17 NSA_SBMA
4 Objective
The objectives of this work item are to support enhancement of service-based management architecture in the following aspects:
1. Specify the solution sets for management of 5G NSA scenarios identified in TR 28.925, (i.e. providing YANG and YAML solution set for legacy nodes NRM in the EUTRAN NRM and RAN NRM).
2. Specify what parts support the Service Based Management Architecture (SBMA; used in 5G) and what parts support the IRP architecture (used before 5G) in the Generic NRM TS (supports both SBMA and IRP architecture).
3. Specify inventory NRM for 3GPP systems using SBMA.
R17 NSA_SBMA WID objective
Discussion in SA5#139e and SA5#140e
Related tdocs:
YAML SS: 6164 (EUTRAN 28.659)+6165 (Generic RAN 28.663)
YANG SS: ?(EUTRAN 28.659)+6392(Generic RAN 28.663)
Objection raised during SA5#140e:
Nokia believes we should not simply write a YANG or YAML definition for 28.662.
Reasons include:
•TS 28.662 is geared towards the IRP framework. It has no references to SBMA. For example references related to notifications point to the Kernel CM IRP and the Alarm IRP. This is confusing for readers.
•Besides that, we also need to revisit the IS itself, for example:
oThe maxAzimuthValue in AntennaFunction is writable. What does that mean? Is this value not given by the antenna? If yes, why is it writable then? Does it mean that the max value is controllable and may be set to values below the max value given by the antenna design?
oMore general, REQ-GRAN_NRM-CON-002 suggests this NRM is for Reading only, but many attributes are actually writable.
oThe combination IsWritable=F and isInvariant=F is not allowed according to 32.156, but used.
•What is the impact of massive MIMO on the model?
6618: The two issues “no reference to SBMA”and “references related to notifications point to the Kernel CM IRP “ have been addressed.
Objection:
Nokia’s position is that the IS needs to be revisited before making the NRM applicable to SBMA. Revisiting the IS requires most likely a new TS. Trying to squeeze all changes for SBMA into the existing IRP based TS may make the TS unreadable.

## Slide 4: Objection issues with stage2
Objection issues with the stage2 for Generic RAN NRM
More general, REQ-GRAN_NRM-CON-002 suggests this NRM is for Reading only, but many attributes are actually writable. (Note to Balazs: Read the requirements carefully before you comment again I am wrong.)
The term NR has been added in some figure titles, but the required additions to the model have not been done, for example:
  The “CommonBsFunction” attribute “shatedTechnologies” is not updated to include NR.
  The “ProxyBsFunction” is not updated to include NR.
  The “ProxyCell” is not updated to include NR.
A “ProxyBsFunction” is related to only one “CommonBsFunction”. This is probably too restrictive.
It is nor clear how “CommonBsFunction” should be used in practice.
The type of “sharedTechnologies” is an integer with multiplicity “1”, which is nonsense of course. It should be an ENUM(of base type string) with multiplicity “1…4”.
The “maxAzimuthValue” attribute of “AntennaFunction” is writable. What does that mean? Is this value not given by the antenna? If yes, why is it writable then? Does it mean that the max value is controllable and may be set to values below the max value given by the antenna design? The attribute definition states the attribute has no operational impact, though-
The definition of “fqBand” points to a voided clause.
The “tmaStateFlag” attribute pulls the representation of an alarm condition on the Iuant interface into OAM. I wonder why this is not translated into the normal alarm conditions we have. At least it is specified “TMAFunction” supports alarm notifications.
Above open issues are not relevant to the NSA_SBMA WID objectives, which request major stage2 update

## Slide 5: Proposed Way forward for R17 NSA_SBMA
1. Specify the solution sets for management of 5G NSA scenarios identified in TR 28.925, (i.e. providing YANG and YAML solution set for legacy nodes NRM in the EUTRAN NRM and RAN NRM).
wayforward: Related to the objection on the broader issue of stage2. Pause the stage 3 modification in Rel-17 until stage 2 is fixed by the group.
2. Specify what parts support the Service Based Management Architecture (SBMA; used in 5G) and what parts support the IRP architecture (used before 5G) in the Generic NRM TS (supports both SBMA and IRP architecture).
wayforward: Select what IOCs in 28.622 can be reused in SBMA, and add related description in the corresponding IOC. We can try to finalize this in Rel-17 next meeting.
3. Specify inventory NRM for 3GPP systems using SBMA.
wayforward: Related to the objection on the broader issue of stage2. Pause this modification in Rel-17 until stage 2 is fixed by the group.
With the analysis above, we propose to update the rel-17 WID with only focus on objective 2 with modification of TS 28.622. I.e. Remove objective 1 and 3. If group agrees, we will bring update WID and related contributions. The target is to finalize the Rel-17 WID in SA5#141e.