## Slide 1: Discussion paper on Management Data Collection Job
Nokia, Nokia Shanghai Bell

## Slide 2: Rationale
Data consumer requests for management data
  Trace, MDT, RLF report, RCEF report,
  PM (performance metrics),
  KPI (end-to-end key performance indicators)
  any combination of above.
Allow a simple request for management data; Data consumer of Management Data Collection Job shall not have to take care of DN(s) of the affected MOI(s).
Notes: RCEF: RRC Connection Establishment Failure

## Slide 3: Identification of Target Managed Object Instances
Area of interest
  Geographical area (latitude-longitude pairs) – it’s obvious that the coverage area of the target cells will usually not exactly map to the described shape
  Cell ID
  Tracking area ID
Discussion/Disagreement on
  Domain: RAN, core
  Traffic type: user plane, control plane
  Slice type: eMBB, URLLC,…
  List of Measurements, category

## Slide 4: Extract of TS 28.622
Attribute properties Table
performanceMetrics | List of performance metrics. Performance metrics include measurements defined in TS 28.552 [20] and KPIs defined in TS 28.554 [28]. Performance metrics can also be specified by other SDOs, or be vendor specific. Performance metrics are identified with their names. For measurements defined in TS 28.552 [20] the name is constructed as follows: "family.measurementName.subcounter" for measurement types with subcounters "family.measurementName" for measurement types without subcounters "family" for measurement families For KPIs defined in TS 28.554 [28] the name is defined in the KPI definitions template as the component designated with e). A name can also identify a vendor specific performance metric or a group of vendor specific performance metrics. allowedValues: N/A | type: String multiplicity: * isOrdered: False isUnique: True defaultValue: None isNullable: False

## Slide 5: PM in TS 28.552
DRB (Data Radio Bearer).
RRC (Radio Resource Control).
UECNTX (UE Context).
RRU (Radio Resource Utilization).
RM (Registration Management).
SM (Session Management).
GTP (GTP Management).
IP (IP Management).
PA (Policy Association).
MM (Mobility Management).
VR (Virtualized Resource).
CARR (Carrier).
QF (QoS Flow).
AT (Application Triggering).
SMS (Short Message Service).
PEE (Power, Energy and Environment).
NFS (NF service).
PFD (Packet Flow Description).
RACH (Random Access Channel).
MR (Measurement Report).
L1M (Layer 1 Measurement).
NSS (Network Slice Selection).
PAG (Paging).
NIDD (Non-IP Data Delivery).
EPP (external parameter provisioning).
TI (traffic influence).
CE (Connection Establishment).
SPP (Service Parameter Provisioning).
BDTP (Background Data Transfer Policy).
DM (Data Management).
BDTP (Background Data Transfer Policy).
AFQ (AF session with QoS).
UCM (UE radio Capability Management).
PAG (Paging)
HO (Handover)
Measurement families used in TS 28.552
Why not reusing the measurement families as “categories”? COVERAGE, CAPACITY, SERVICE EXPERIENCE, TRACE, ENERGY EFFICIENCY, MOBILITY, ACCESSIBILITY

## Slide 6: Extract of TS 28.622
Attribute properties Table
performanceMetrics | List of performance metrics. Performance metrics include measurements defined in TS 28.552 [20] and KPIs defined in TS 28.554 [28]. Performance metrics can also be specified by other SDOs, or be vendor specific. Performance metrics are identified with their names. For measurements defined in TS 28.552 [20] the name is constructed as follows: "family.measurementName.subcounter" for measurement types with subcounters "family.measurementName" for measurement types without subcounters "family" for measurement families For KPIs defined in TS 28.554 [28] the name is defined in the KPI definitions template as the component designated with e). A name can also identify a vendor specific performance metric or a group of vendor specific performance metrics. allowedValues: N/A | type: String multiplicity: * isOrdered: False isUnique: True defaultValue: None isNullable: False

## Slide 7: PM in TS 28.552
Cause (failure cause, resume cause, release cause, rejection cause).
5QI or QoS level (mapped 5QI or QCI in NR option 3)
S-NSSAI.
PLMN ID
Modulation schema
Layer at MU-MIMO case
SSB
Registration type (initial registration, mobility registration update , periodic registration update, emergency registration)
DSCP (Differentiated Service Code Point)
Error Code
Delivery Result
Subcounters in TS 28.552
Subcounters are only applicable for some measurements
Subcounters could be used to request measurements for a specific S-NSSAI

## Slide 8: Thank you!