## Slide 1: TR 28.869 conclusion and new WID discussion
China Mobile, NTT DOCOMO

## Slide 2: Overview of the TR 28.869: Current progress
Terminology and concepts
"cloud native VNF" is used in clause 5.1
"NF deployment" is used in clause 5.2 of the present document
According to SA5#157 approved pCR S5-246005 the following text was added:
The term "cloud native VNF" and "NF deployment" used in the present document are closely related, nevertheless there is no consensus on their definition and concepts used in this present document and are expected to be investigated in the normative phase.
Consensus for both WT1-WT2 and WT3 is that we will conclude the terminology used in the normative phase

## Slide 3: Overview of the TR 28.869: Current progress
5.1 Use of VNF generic OAM functions
5.1.1 Use case #1: Cloud-native VNF configuration management
5.1.2 Use case #2：Cloud-native VNF policy management
5.1.3 Use case #3: Cloud-native VNF Traffic management
5.1.4 Use case #4: Cloud-native VNF Upgrade
5.1.5 Relationship between 3GPP Management System (SBMA) and ETSI NFV VNF generic OAM functions and NFV-MANO
5.2 Use of industry solutions
5.2.1 Use case #1: 3GPP management architecture evolution
5.2.2 Use case #2: data streaming of a NF Deployment instance
5.2.3 Use case #3: Creation of a NF Deployment instance
5.2.4 Use case #4: Modification of a NF Deployment instance
5.2.5 Use case #5: Termination of a NF deployment instance
5.2.6 Use case #6: Scaling of cloud-native network functions
5.3 Support of different cloud deployment scenarios
5.3.1 Use case #1: Placement of cloud native NFs
(stlill have no solution agreed. )
Current progress
WT-1: there are solutions described, but there is no evaluation
related to WT-3 of the SID, so far there is no solution
WT-2: there are solutions described, but there is no evaluation

## Slide 4: Overview of the TR 28.869: Current progress
For all the items (WT-1, WT-2, WT-3) all the solutions and evaluations presented so far including the last SA5#157 meeting face the following issue:
Descriptions are in high level and lack of technical insight of the changes needed inside the 3GPP management system.
Especially for WT-1 and WT-2 it is not easy to derive a solid technical evaluation that can drive normative work developments
Challenges
In more detail:
WT-1: the interface between Generic OAM functions is well defined according to ETSI ISG NFV-IFA049, but the enhancements needed in the 3GPP management system have not been described in any of the solutions.
WT-2: interfaces exposed by systems other than NFV-MANO have not been described in any of the solutions like also the enhancements needed in the 3GPP management system.
WT-3: there is only one use case described but without endorsing any solution.

## Slide 5: The relationship between WT-1 and WT-2
Why WT-1 and WT-2 are closely related, and need to work together in the future.
VNF Generic OAM functions northbound interface is irrelevant of NFV-MANO operations.
3GPP Management System
VNF Generic OAM Functions
VNFs
NFV- MANO
Only used for Managing VNF generic OAM functions OAM
Deployment Option #1
- Generic OAM function northbound is irrelevant of NFV-MANO operations
- NFV-MANO supports VNF LCM and VNF Generic OAM Function LCM
3GPP Management System
VNF Generic OAM Functions
VNFs
NFV- MANO
Only used for Managing VNF generic OAM functions OAM
Deployment Option #2
- Generic OAM function northbound is irrelevant of NFV-MANO operations
- NFV-MANO supports VNF LCM but not VNF Generic OAM Function LCM
Other Management System
3GPP Management System
VNF Generic OAM Functions
VNFs
Only used for Managing VNF generic OAM functions OAM
Deployment Option #3
- Generic OAM function northbound is irrelevant of NFV-MANO operations
- A management system (not NFV-MANO) supports VNF LCM and VNF Generic OAM Function LCM
Other Management System

## Slide 6: TR 28.869 Conclusions and recommendations—option A：
6 Conclusions and recommendations (based on S5-245774)
6.1 General
  The present document introduces use cases related to the management of cloud-native VNF/NF Deployment instances, in terms of configuration, policy, traffic, upgrade, data streaming and LCM related aspects. Based on the different requirements and potential solutions, these research contents can be divided into 5.1 clause and 5.2 clause.
6.2 Issue on use of VNF generic OAM functions
  It is recommended to make enhancements in the 3GPP management system considering the configuration management, policy management, traffic management and upgrade management of cloud native VNF provided by external OAM entities. The detailed potential solutions in clause 5.1 can be used as baseline for normative work.
6.3 Issue on use of industry solutions
  It is recommended to make some enhancements in the 3GPP management system regarding the LCM of NF Deployment instances, considering the management capabilities provided by external orchestration and management entities. The detailed potential solution in clause 5.1, 5.2.3-5.2.6 can be used as baseline for normative work.
  It is recommended to make enhancements in the 3GPP management systemfor supporting data streaming for NF Deployment instances. The potential solution in clause 5.2.2 can used as baseline for normative work.
Question to the group:
- Such kind of recommendations can lead to consensus for continuing to the normative phase?
This contains detailed conclusions and recommendations for each solution, which will result in the WID scope containing related solutions content.

## Slide 7: TR 28.869 Conclusions and recommendations—option B：
6 Conclusions and recommendations
6.1 General
  The present document introduces use cases related to the management of cloud-native VNF/NF Deployment instances, in terms of configuration, policy, traffic, upgrade, data streaming and LCM related aspects. Based on the different requirements and potential solutions, these research contents can be divided into 5.1 clause and 5.2 clause.
6.2 Recommendations
  It is recommended to have normative work to specify:
  Specifying terminology and concepts for cloud native operations and aspects related to management and orchestration, including but not limited to those related to cloud-native VNFs and NF Deployment instances.
  Specifying the use cases and requirements, taking into account the relevant use cases from this study TR28.869.
  Specifying the management enhancements in the 3GPPmanagement architecture.
  Specifying the potential impacts on the existing 3GPP Management.
This contains a more general conclusion

## Slide 8: CMO New WID on cloud aspects of management and orchestration
Specifying terminology and concepts for cloud native operations and aspects related to management and orchestration, including but not limited to those related to cloud-native VNFs and NF Deployment instances.
Specifying the management enhancements for cloud-native VNFs /NF Deployment instances, including aspects of configuration, upgrade, traffic and policy management.
  Specifying enhancement in the 3GPP management system to support the capability of managing NF Deployment instances through interaction with VNF Generic OAM functions defined in ETSI GS NFV-IFA 049 via the corresponding interfaces specified therein.
Specifying the management enhancements for NF Deployment instances, including aspects of creation, modification, termination, scaling management and the use of declarative descriptor to convey deployment requirements.
  Specifying enhancements to support the capability to perform LCM operations for NF Deployment instances via a new deployment management reference point, which is flexible to support use of ETSI NFV MANO, but not limited to it.
  Specifying enhancement to support the capability of management data streaming for NF Deployment instances based on message bus technology.
The WID is to enhance the cloud aspects of management and orchestration based on conclusions and recommendations documented in TR 28.869.
Objectives of the new WID

## Slide 9: HOW to move forward
option | new WID | Objective | Expected Output | Recommendation
option 1 | Have a single new R19 WID | Terminology alignment WT-1 of the TR WT-2 of the TR WT-3 of the TR (if more solid) | Option#1.1.1 update existing TSs but also compile new TS(s) if needed based in the analysis and conclusions Option#1.1.2 no new TS only update existing TSs (e.g., TS 28.531, TS 28.533, TS 28.500, TS 28.525 etc) Option#1.1.3 compile only new TS(s) | Option#1 and sub-option# 1.1.1 If no WID is approved at SA5#158, we need continue with Option 2
option 2 | no new R19 WID continue working on the TR28.869 | Continue to conduct in-depth research on WT-1, WT-2 and WT-3 | When ready continue with option 1 but targeting Release 20 normative work | 
Option 3 | have two R19 WIDs | A new WID for WT-1 of the TR (and other topics) A new WID for WT-2 of the TR |  | Not recommended

## Slide 10: What happens if no new TS only update existing TSs
TS 28.500
concept, architecture and requirements
TS 28.525-28.528
Life Cycle
Management
TS 28.510-28.513
Configuration Management
TS 28.520-28.523 Performance Management
TS 28.531
Provisioning
TS 28.533
service based management architecture
Reference
advantages
There is no need to distinguish between the new TS and the old TS
disadvantages
The scope of influence is large, maybe requires much time for careful assessment to avoid adverse effects on other TSs.
TS 28.515-28.518 Fault
Management

## Slide 11: What happens update existing TSs but also compile new TS
TS 28.xyz
concept, architecture and requirements
create a new TS at R19, mainly focus on the concept, architecture and requirements,.etc, just like TS 28.500
advantages
The potential impact is more clearer
more convenient to continue working in the future phase,for example, if needed, we can only update the new TS 28.xyz in Realease 20
disadvantages
The relationship between the new TS and the existing TSs need to be distinguished
TS28.500
concept, architecture and requirements
TS 28.525-28.528
Life Cycle
Management
TS 28.510-28.513
Configuration Management
TS 28.515-28.518 Fault
Management
TS 28.520-28.523 Performance Management
TS 28.531
Provisioning
TS 28.533
service based management architecture

## Slide 12: Thank you!