## Slide 1: Wayforward on NB-IoT RRM measurement accuracy simulation assumption
Huawei, HiSilicon
R4-79AH-0274
3GPP TSG-RAN WG4 #78bis
Hong Kong, P.R.C, 28 – 30 June, 2016
Agenda Item: 2.3.1

## Slide 2: Background
RAN4 has discuss the simulation assumptions for RRM NRSRP/NRSRQ measurement accuracy and reached the following consensus.

## Slide 3: Consensus on RRM measurement
Following parameters need to be included in the assumptions for alignment of results:
Frequency error:
  +/- 50Hz @2 GHz
  Companies are encouraged to provide results also for +/- 100Hz @2 GHz
Minimum number of subframes containing NRS per L1 measurement period used by the UE for NRSRP/NRSRQ measurements:
  For L1 period of 400 ms: 10, 30 and 50 subframes containing NRS
  For L1 period of 800 ms: 20, 60 and 100 subframes containing NRS
  Time window over which coherent combining is done is to be disclosed by the companies for alignment purpose.
Measurement periods in non-DRX: 400 ms (normal coverage) and 800 ms (enhanced coverage)
Measurement accuracy requirements derived for maximum value obtained at the 5th and 95th percentiles of CDF
RF margin is assumed to be X. (2 dB ≤ X ≤ 3 dB)

## Slide 4: Simulation assumptions for RRM measurement
Note: RSSI is measured only from OFDM symbols containing NRS of measurement subframes.
Parameters | Value | Comments
Measurement bandwidth | 1 resource blocks | Both RSRP and RSRQ measured over 1 RB
System bandwidth | 1 resource blocks | 
L1 measurement period | 400 ms, 800 ms | 
Number of subframes containing NRS per L1 measurement period | 10, 30 and 50 for 400ms L1 measurement period 20, 60 and 100 for 800ms L1 measurement period | 
L3 filtering | Disabled | 
DRX | OFF | 
Antenna configuration | 1TX, 1RX | 
Mobility | Stationary UEs, | 
Channel model | AWGN, ETU 1Hz, EPA 1Hz | Models stationary device
Measurement type | NB-RS only based | 
CP length | Normal | 
Carrier frequency | 2 GHz | 
Ec/Iot | -15dB, …, 10 dB | AWGN noise
Frequency error modelling | +/-50 Hz | With respect to reference cell. Companies are encouraged to provide results also for +/- 100Hz