## Slide 1: Status Report of TSG RAN#110
Source: TSG RAN Chair
Agenda Item: 4.7
SP-251701

## Slide 2: Outline
Administrative Aspects
TSG RAN project update
ITU matters

## Slide 3: Administrative Aspects

## Slide 4: Administrative Aspects
Approved MCC TF 160 report in RP-252982
Approved Terms of Reference (2026) of MCC TF160 in RP-253098
Progress update and next steps for the CA database: Summarized in RP-253522

## Slide 5: RAN Leadership Change
Jerome Vogedes who was elected as RAN Vice Chair in RAN#107 in Mar. 25 was reconfirmed on Oct. 30 via RAN email reflector after change of affiliation (AT&T  T-Mobile USA Inc.)
RAN Chair
RAN Vice Chair
RAN Vice Chair
RAN Vice Chair
RAN Secretary
KIM, Younsun
Samsung Electronics Co., Ltd (TTA)
ZHOU, Xutao
vivo Mobile Communication Co. (CCSA)
VOGEDES, Jerome
AT&T (ATIS)

T-Mobile USA Inc.(ATIS)
BURACCHINI, Enrico
TELECOM ITALIA S.p.A. (ETSI)
KRAUSE, Joern
3GPP Support

## Slide 6: TSG RAN Project Update

## Slide 7: Release 19
Rel-19 ASN.1 review has been completed and ASN.1 is now frozen

## Slide 8: Release 20 AI/ML for Air Interface
Way forward agreements on inter-vendor collaboration
  Remove RAN4 checkpoints and SA checkpoints
  From RAN perspective, move forward with normative phase for both Direction A (3a-1, 4-1) with non-OTA solution and Direction C.
  Indicate to SA the intention to move forward and ask SA to kindly decide on the best way forward and down selection between SA5 and SA2 options.
  This does NOT imply that all three options will be done in 6G
  LS to SA in RP-253846
Way forward agreement on UE sided data collection:
  To avoid parallel work in 5G and 6G, no normative work in Rel-20 for UE side data collection. Focus data collection framework work on 6G, and use the lesson learned across all the WGs to design something for 6G.
  From RAN perspective, we see value for SA2/SA5 and SA3 to complete/finalize their study so we can use the lessons learned for 6G.
  The fact that 5G didn’t have normative phase does not preclude standardized solutions in 6G.
  LS to SA in RP-253847

## Slide 9: Release 20 RAN4 Spectrum WIs (1/2)
Following RAN4 spectrum work items for Rel-20 were approved in RAN#110
Tdoc# | Title
RP-253855 | New WID: Rel-20 Addition of channel bandwidths and power classes to existing NR bands and CA/DC combinations
RP-253833 | New WID: Additional NR and LTE band combinations for features in Rel-20
RP-253842 | New WID: Rel-20 Dual connectivity (DC) of x LTE band(s), y NR band(s) (1<=x<6, 1<=y<6, x+y<=6) and single or two NR Supplementary Uplink (SUL) bands
RP-253850 | New WID: Additional NR bands for NR features in Rel-20
RP-253841 | New WID: Introduction of the higher power classes, 3MHz channel bandwidth and eRedCap for the existing NR/IoT NTN bands
RP-253849 | New WID: Rel-20 NR Carrier Aggregation (CA)/Dual Connectivity (DC) for x bands DL with y bands UL (x<7, y<3) and Supplementary Uplink (SUL) band combinations/CA band combinations with a single SUL or two SUL cells
RP-253814 | New WID: basket WI on Rel-20 LTE-Advanced Carrier Aggregation for x bands (1<=x<= 6) DL with y bands (y=1, 2)

## Slide 10: Release 20 RAN4 Spectrum WIs (2/2)
Following RAN4 spectrum work items for Rel-20 were also approved in RAN#110
Tdoc# | Title
RP-253811 | New WID: Introduction of a new band for 1.5GHz Japanese allocation
RP-253840 | New WID: Introduction of EESS protection and PC1 for 40GHz

## Slide 11: 6G Study
Status report for Study on 6G Scenarios and requirements in RP-253417
RAN#110 focused on the following areas this week (details can be found in slides 19~24)
  Deployment scenarios
  Key performance indicators
  Requirements for architecture and migration
  Operational requirements (spectrum, diverse device types, …)
  Requirements of new and existing services
  Key technical principles
  Testing and conformance requirements
TR 38.914 v0.3.0 for Study on 6G Scenarios and requirements in RP-253750 was agreed

## Slide 12: 6G Study
There was a proposal for coordination between RAN2 and SA3 in the form of a joint session during the Malta WG meetings (RAN2#133-bis/SA3#127)
  Security framework for lower layer security and SIB security may impact both RAN2 and SA3 design and early collaboration between the WGs is useful to progress this work in a timely fashion (RP-253197, ZTE Corporation, Sanechips, Ericsson)
It was concluded that RAN2 and SA3 chairs can coordinate themselves regarding a joint session

## Slide 13: 6G Study
The following was agreed for 6GR peak data rate
  The minimum requirements for 6GR peak data rate are as follows:
    Downlink peak data rate is 36 Gbps.
    Uplink peak data rate is 18 Gbps.
  Note: The above peak data rate assumes 600 MHz aggregated BW
  Note: the actual peak data rate depends on actual spectrum allocation for each MNO
The following was agreed for 6G numerology
  SCS of 30kHz for mid-band (1-2.xGHz) FDD is not supported in 6G

## Slide 14: 6G Study
The following proposal on handling of AI traffic was agreed
  Ensure that any work on AI traffic characteristics in the RAN domain takes place in one place only (lead by RAN2) to avoid fragmentation and duplication with feedback from SA4 on AI traffic characteristics

## Slide 15: NR-NTN in Terrestrial Bands
There were requests from operators to specify the following terrestrial IMT-bands as new bands for NR-NTN deployment:
  n7 FDD band with a UE transmitting at 2500 MHz - 2570 MHz and SAN transmitting at 2620 MHz - 2690 MHz (requested by Telstra in Australia) [RP-253861, RP-253609]
  n25 FDD band with a UE transmitting at 1850 - 1915 MHz and SAN transmitting at 1930 - 1995 MHz (requested by T-Mobile USA and Rogers in Canada) [RP-253699, RP-253700]
RAN agreed on a way forward to scope coexistence studies to evaluate the impact of TN IMT frequency bands when deployed as NTN band in future meetings
RAN endorsed an LS to ITU-R to inform the situation in RAN and request guidance for future work (Endorsed LS to SA in RP-253878)

## Slide 16: ITU Matters

## Slide 17: ITU Matters
DRAFT Reply LTI to ITU-R WP5D/TEMP/405(Rev.1) = RP-253009 on the schedule for updating Recommendation ITU-R M.2012 to revision 8
  LS in RP‑253816
DRAFT Reply LTI to ITU-R WP5D/TEMP/404(Rev.1) = RP-253008 on the schedule for updating Recommendation ITU-R M.2150 to revision 4
  LS in RP‑253817

## Slide 18: Questions?

## Slide 19: Additional Info – 6G requirements of new and existing services (in RAN#110)
Mobile Broadband
  The 6GR and 6G RAN architecture shall support mobile broadband services with enhanced performance.
Immersive Communication
  The 6GR and 6G RAN architecture shall support immersive communications.
  The composite requirement in Clause 5.1.16 is used for immersive communication.
PHY minimum peak data rate is 10 Mbps in DL and 10 Mbps in UL for lowest-tier device.
6GR and 6G RAN architecture shall support efficient transmission/mechanism for AI applications and services.
Voice
  The 6GR and 6G RAN architecture shall support Voice in 6G.
  Editor note: whether and how to support voice services if they are not provided by 6G is to be decided by SA2. 6GR and 6G RAN architecture requirements will be aligned with that.
Regulatory Services
  The 6GR and 6G RAN architecture shall provide mechanisms to enable regulatory services such as emergency call, location services for regulatory compliance, Public Warning System (PWS), Lawful Interception (LI), eCall (for automotive), Disaster roaming.

## Slide 20: Additional Info – 6G requirements of new and existing services (in RAN#110)
Fixed wireless access (FWA)
  The 6GR and 6G RAN architecture shall support fixed wireless access (FWA).
Support for UAV communication
  The 6GR shall provide coverage, high-capacity connectivity and mobility for UAV. The 6GR shall allow for serving UAV with both UAV dedicated and UAV non-dedicated deployments.
Vehicular services
  The 6GR and 6G RAN architecture shall support services to vehicles over the Uu interface.
  5G NR sidelink is reused as is for 6G V2X services.
Mission Critical Communication Services
  The 6GR and 6G RAN architecture shall support Mission Critical Communications services (e.g. MCPTT, MCVideo, MCData).
  5G broadcast, 5G NR multicast and 5G NR sidelink are reused as is for 6G mission critical communications services.

## Slide 21: Additional Info – 6G requirements for architecture and migration (in RAN#110)
The design of the 6G RAN architecture shall allow the collection and transport of standardized measurement data (e.g. AIML data and sensing data) in an efficient way and under operator control to fulfil existing and new service requirements.
  User data privacy and anonymity is supported and preserved as part of data collection, transmission and operation.
  user consent as part of outcome of SA.
  Operator control: operator can control and configure the data to be collected, to have visibility of the collected data, and decide whether to start or stop data collection based on user consent where necessary, while ensuring user privacy and anonymity.
  Note: The term ‘user consent’ may be further modified depending on SA discussion/outcome.
The design of the 6G RAN architecture shall enable lower energy consumption with respect to current networks to achieve sustainability.
The 6G RAN shall at least support idle mode inter-RAT mobility between the 6GR and E-UTRAN.
The 6GR shall support coexistence with NB-IoT (all deployment modes) and eMTC via semi-static configuration.
  This text is moved to 5.2 and remove existing editor’s note
The 6G RAN shall support network performance monitoring.

## Slide 22: Additional Info – 6G diverse device types (in RAN#110) – Proposal 1
6GR supports the operation (but not required to be optimized for performance) in a minimum spectrum allocation of 3MHz with a 15kHz SCS Note: the following agreement made in RAN1#123 still holds, with the clarification that the bandwidth in Opt 1 below is assumed to be at least 5MHz with a 15kHz SCS.
  User data privacy and anonymity is supported and preserved as part of data collection, transmission and operation.
Regarding the smallest maximum UE bandwidth as discussed in the following RAN1 agreement, Opt 1 is excluded. Aim to conclude by RAN plenary no later than RAN#112 (June 2026).
  RAN1 and RAN4 is tasked to continue providing more analysis accordingly.
  Companies are encouraged to provide more analysis at RAN plenary particularly regarding the use cases, requirements, economy of scale, etc.
Agreement
If the minimum spectrum allocation is 3MHz with 15kHz SCS for 6GR,
Opt1: Design of the common signals/channels (at least for SSB) for initial access by assuming bandwidth larger than 3MHz, which is applicable to any spectrum allocations with adjustment, if applicable
Opt2: A single design of the common signals/channels (at least for SSB) for initial access by assuming minimum spectrum allocation as target bandwidth 3MHz, which is applicable to any spectrum allocations
Agreement
Study the following smallest maximum supported RF and BB UE BW without spectrum aggregation for at least one low-tier device type supported by 6GR framework from physical layer perspective, subject to further discussion and confirmation in RAN
  Opt1: 3MHz
  Opt2: 5MHz
  Opt3: 10MHz
  Opt4: 20MHz
  FFS: the UL bandwidth may be different to the DL bandwidth
  FFS: the bandwidth value may be different for different SCS, duplex modes, and bands.
  FFS: whether RF and BB UE BW are same or different

## Slide 23: Additional Info – 6G diverse device types (in RAN#110) – Proposals 2 & 3
Proposal 2
  Diverse device types as in 6G SIDs are expected to include supporting at least MBB (as highest priority), FWA, and Massive IoT services
  Companies are encouraged to further contribute at RAN plenary regarding the analysis of necessary aspects to help progress RAN WG technical design and evaluations.
  The detailed discussion for device types (how many, parameters, whether or not to define device types, whether or not to introduce minimum mandatory set of features, etc.) is on hold in RAN plenary and to resume from RAN#113 (September 2026). Discussions on device types are not to be discussed in WGs until further update from RAN plenary.
Proposal 3
  Capture the following aspects related to diverse device types into the TR:
    Scalable and forward compatible design
    Limited set of device types (based on the agreement in RAN#109)
  Detailed wording is to be drafted in RAN#111, along with possibly other aspects (e.g., scalability, differentiated services, etc.).

## Slide 24: Additional Info – Other 6G Operational Requirements (in RAN#110)
RAN sharing
  6G RAT shall support Network Sharing (i.e., MOCN, MORAN, and Indirect Network Sharing).
  Additional description and requirements for RAN sharing are provided in TR 38.760-3 [x].
Ease of operation and Self Organization
  Self-organization facilitates the automatic deployment of network nodes, including the establishment of basic operational parameters without manual intervention.
  6GR and 6G RAN architecture shall support automatic configuration and optimisation of the RAN, including ANR and collection of MDT data.
Network Resilience
  The 6G RAN shall be designed to ensure accessibility and service continuity with minimum interruption time in any failure condition.
Service awareness in RAN
  6G RAN shall be able to understand and be capable of adapting to traffic demands of applications while maintaining overall system efficiency in terms of radio resource utilisation and energy consumption.