## Slide 1: Analysis on Pre-establishing Dedicated Bearer Options
ZTE
3GPP TSG SA WG2#173
Goa, India, February 9 - 13, 2026
S2-25xxxxx

## Slide 2
Pre-Established Dedicated Bearer
Pros and Cons Analysis
Categories | Sub Categories | Benefits | Concerns
Before MO or MT call setup is initiated | Category 1. During attach/IMS PDN Connection Establishment | Reduce CST by 2.5 seconds (17%~27% overall CST reduction) [1] | 1. Resource occupation [2] or resource reservation [3] before Call Initiation. 2. Regarding pre-configure AGW address when reuse attach with dedicated bearer activation procedure, whether PGW has related information [4].
 | Category 2. During IMS Registration |  | 1. Resource occupation [2] or resource reservation [3] before Call Initiation. 2. Affect the existing IMS registration procedure, resulting in increased registration latency. 3. P-CSCF needs to be enhanced.
When MO or MT call setup is initiated | Category 3. When MO call setup is initiated | Resource occupation upon Call Initiation | 1. Optimization not applicable to MT[5]. 2. Increased signaling & latency for MO UE in CONNECTED mode[6]. 3. UE IMS and NAS Cross-Layer Complexity[7].
[1] Based on evaluation in S2-2508341, the measured Call Setup Time (CST) ranges from 9.3s to 15s for on-demand scenarios. By pre-establishing the dedicated bearer during the Attach/PDN connection procedure, the 2.5s delay associated with the 3 AIR message exchange is eliminated, resulting in a 17% to 27% reduction in total Call Setup Time.
[2] Physical resources like PRBs are only consumed during active data transmission, ensuring that no Uu interface resources are occupied when no IMS voice traffic occurs.
[3] Resource reservation is managed through Admission Control (AC), which is implemented having 2-step (Step1: check UE_COUNT and BEARER_COUNT, Step2: check Air Resource)
  Admission Control Decision == ((UE_COUNT<X) && (BEARER_COUNT<Y)) && (Available_Physical_Resource>Z)
    NOTE1: UE Count as the Primary Bottleneck: In practical implementations, the bearer limit is typically multiple times higher than the UE limit (e.g., Y=4000 vs.X=1000). Thus, the UE count serves as the primary system bottleneck in NB-IoT scenarios.
    NOTE2: Admission Based on Actual Resource Usage: Radio resource AC evaluates the actual physical resources (e.g., PRBs) currently consumed by active GBR traffic.
  Since pre-establishing a bearer neither affects the UE count quota nor consumes physical resource quotas while call is not ongoing, and the BEARER_COUNT in practical implementation is almost impossible to reach its upper bound, it (pre-establish Solution Category 1 or 2) does not impede the admission of new service requests.
Conclusion1: The benefit(shorter CST) of category 1 and 2 exists. The concern 1(resource issue) of category 1 and 2 does not exist.

## Slide 3
[4] In current implementations, since the PGW, P-CSCF, and AGW all belong to the same operator and the PGW already configures IMS-capable P-CSCF addresses, it is highly feasible for the PGW to pre-configure the List of AGW IP addresses for Voice over GEO, i.e., the PGW is fully capable of pre-configuring the AGW address information.
.
[7] Triggering establish dedicated bearer before sending SIP INVITE requires complex dependency/coordination between the IMS Application Layer and the NAS Layer.
Conclusion2: The concern 2(AGW address awareness) of category 1 does not exist. Remaining concerns for the category 2 and 3 exists.
Pre-Established Dedicated Bearer
Pros and Cons Analysis
State\UE type | MO | MT
IDLE | NO BENEFIT | NO BENEFIT
CONNECTED | HAS BENEFIT | NO BENEFIT
[5] The solution of category 3 are as follows: When MO UE is in RRC_IDLE mode, the MO UE triggers the MME to establish the dedicated EPS bearer via the RRC Establishment procedure. When MO UE is in RRC_CONNECTED mode, the MO UE triggers the Bearer Resource Allocation procedure. Providing no optimization for the Mobile Terminated (MT) UE, leaving terminating call performance not enhanced.
[6] When UE is in RRC_CONNECTED mode, the MO UE triggers the Bearer Resource Allocation procedure. 4 extra AIR messages are introduced before sending SIP invite. (Details in Annex). Providing no optimization and introduces higher latency for the connected MO UE.
  Compared to On-demand Establishment, this introduces 1 extra uplink signaling message (Bearer Resource Allocation), resulting in an additional delay of 0.285s*3 = 0.855s. (See Annex)
  Compared to Pre-establishment during Attach/PDN, this introduces 4 extra signaling message (Bearer Resource Allocation, RRC Reconfig, RRC Reconfig Complete, in UL Direct Transfer), resulting in an additional delay of 0.285s*(3*3 + 1)=2.85s. (See Annex)
Categories | Sub Categories | Benefits | Concerns
Before MO or MT call setup is initiated | Category 1. During attach/IMS PDN Connection Establishment | Reduce CST by 2.5 seconds (17%~27% overall CST reduction) [1] √ | 1. Resource occupation [2] or resource reservation[3] before Call Initiation. 2. Regarding pre-configure AGW address when reuse attach with dedicated bearer activation procedure, whether PGW has related information[4].
 | Category 2. During IMS Registration |  | 1. Resource occupation [2] or resource reservation[3] before Call Initiation. 2. Affect the existing IMS registration procedure, resulting in increased registration latency. 3. P-CSCF needs to be enhanced.
When MO or MT call setup is initiated | Category 3. When MO call setup is initiated | Resource occupation upon Call Initiation | 1. Optimization not applicable to MT[5]. 2. Increased signaling & latency for MO UE in CONNECTED mode[6]. 3. UE IMS and NAS Cross-Layer Complexity[7].

## Slide 4: Conclusion and proposal
Pre-establish dedicated bearer during attach/PDN connection establishment procedure has obvious benefit without any issue compared with other categories.
For IMS voice, it is proposed to establish dedicated bearer during attach/PDN connection establishment procedure.
Conclusion
Proposal
Categories | Sub Categories | Benefits | Concerns
Before MO or MT call setup is initiated | Category 1. During attach/IMS PDN Connection Establishment | Reduce CST by 2.5 seconds (17%~27% overall CST reduction) [1] √ | 1. Resource occupation [2] or resource reservation[3] before Call Initiation. 2. Regarding pre-configure AGW address when reuse attach with dedicated bearer activation procedure, whether PGW has related information [4].
 | Category 2. During IMS Registration |  | 1. Resource occupation [2] or resource reservation[3] before Call Initiation. 2. Affect the existing IMS registration procedure, resulting in increased registration latency. √ 3. P-CSCF needs to be enhanced. √
When MO or MT call setup is initiated | Category 3. When MO call setup is initiated | Resource occupation upon Call Initiation | 1. Optimization not applicable to MT[5]. √ 2. Increased signaling & latency for MO UE in CONNECTED mode[6]. √ 3. UE IMS and NAS Cross-Layer Complexity[7]. √

## Slide 5
Pre-establishment during call setup
(Connected MO UE)
Annex
Air message comparison during call setup
On-demand establishment
Pre-establishment during attach/PDN connection