## Slide 1: Discussion on a 6G Use Case: Embodied Video Internet (EVI)
China Mobile
  3GPP SA WG4 Meeting #134
  Dallas, US, 13–17 Nov, 2025
  S4-251826

## Slide 2: Motivation- The Shift to Mobile and Embodied Sensing
We are transitioning from a world of static, limited perception to one of dynamic, mobile, and embodied sensing
  The Old Paradigm (Static & Constrained): Relies on fixed cameras and sensors with limited fields of view, struggling to achieve comprehensive and flexible coverage of complex environments.
  The New Paradigm (Mobile & Embodied): Robots, UAVs, and other mobile devices are becoming our "mobile eyes and limbs." They can actively enter, explore, and interact deeply with the physical world.
  The multiple cameras and LiDAR sensors on these devices generate concurrent streams of beyond 2D video and other large-scale heterogeneous data. A vast gap exists between the limited on-device computational power and the immense processing requirements for advanced embodied tasks like real-time 3D scene understanding and autonomous decision-making.
Notes: 对运营商、设备商的好处 终端厂家的好处
不够显著，benefit，
6G data 可能是6G的一个main drive opportunity for all the parties or industry

## Slide 3: Reference Use Case: Network-Assisted Embodied AI
Use Case Description:
Devices such as robots and UAVs equipped with multiple cameras are required to capture and upload multi-modal concurrent data streams (e.g., video, point clouds) for network-based AI inference. These streams are transmitted via a unified bearer network to a network-based platform or third party platforms for distributed AI inference tasks, including multi-modal perception, 3D digital twin modeling, trajectory planning, and task orchestration. This supports various embodied tasks in educational, home, industrial, and special environments, such as automatic inspection and troubleshooting, human-computer interaction and remote operation.
Potential Requirements:
Compression and transmission of concurrent, heterogeneous data streams (2D video, beyond 2D media, etc.)
Core AI tasks such as perception, 3D construction, and planning are completed on the network or third party platforms.
The core demand for the network: It poses a severe challenge to the high data rate, and low latency of the uplink.
Support diverse scenarios（Educational、Home、Industrial、Dangerous environment）
Notes: 用 gap

## Slide 4: Example:
* An robot example from UBTECH.
6+0 MIC
Curved surface display screen *2
Four-ocular stereoscopic vision
Ultrasonic sensor *4
6-Axis Force/Torque Sensor
6-Axis Force/Torque Sensor
Notes: SA2 have related work in R18 and R19, but lack of unified architecture design,,需求从RAN时不时按场景来，但是缺统一架构设计。
RAN最新的LS关于模型传输的

## Slide 5: Required Performances from SA1 6G study
Scenario | I | II | III
6 & 8 Cameras (note 1) | 1080p * 6 | 1080p * 4 + 4K * 2 | 1080p * 2 + 4K * 4
Data rate (Mbps) (note 2) | 20 | 60 | 100
E2E RTT (note 3) | 100~300ms |  | 
NOTE 1: 6 RGB cameras are equipped for robot “Figure 02” [180], 8 RGB cameras are equipped for robot of Tesla Optimus [183] . NOTE 2: Data Rate = Video resolution*(Bits per colour*3) *Refresh rate/Compression ratio. Compression ratio of 240 and 8 bits per colour is assumed, thus data rate is around 3 Mbps for 1080p 15Hz, and around 24Mbps for 4K 30Hz. Compression ratio, bits per colour and refresh rate for 1080p refers to the similar cases for real-time video uploading of a vehicle as per YD/T 4778-2024 [182]. NOTE 3: See analysis for Reaction Time Statistics [181]. E2E Round Trip Time (RTT) including UL and DL |  |  | 
Table 6.27.1-1: real time video uploading for network-assisted AI inference offloading services for mobile embodied AI devices
The mobile AI embodied device has two cameras (same type) that operate at a resolution of 1080p and a frame rate of 15 Hz (6 Mbps data rate, 66,67ms data interval).
Four cameras (of another type) that function at a higher resolution of 4K and a frame rate of 30 Hz (96 Mbps data rate, 33,33 ms data interval).
The peak data rate of UL that needs to be processed can be estimated to be around
100 Mbps (3 * 2 Mbps + 24 * 4 Mbps)
The network-assisted AI inference task offloading operation is usually more demanding for the uplink in terms of data rate and communication latency.
:

## Slide 6: Data Acquisition & Collection：Active perception
Data types | Devices | Example/Usage
Video Streams | high-resolution cameras | providing overlapping fields of view for comprehensive scene understanding
Point Cloud Data | LiDAR/Depth sensors | Real-time 3D spatial data from LiDAR or depth sensors, crucial for navigation and 3D modeling.
Pose & Inertial Data | IMU、GPS、Wheel odometry | Continuous acquisition of the device's own six-degree-of-freedom pose (position and orientation), velocity, and angular velocity.
Table 6.27.1-2: Key data acquisition methods for mobile embodied AI devices
Task-Driven Adaptive Capture：
Dynamic Resolution/Frame Rate:
Adjusts video parameters based on task criticality and network conditions (e.g., high frame rate for rapid movement, lower resolution for static observation).
Region-of-Interest (RoI) Focusing:
On-device AI identifies critical areas, prioritizing their upload with higher quality.
Event-Triggered Bursts:
Initiates high-frequency data capture and transmission upon detecting predefined events (e.g., an anomaly, a specific sound).
Unlike passive recording, embodied agents actively interact with the environment, requiring a rich set of synchronized data streams.
:
Notes: NF变CN

## Slide 7: Key Differentiators vs. Traditional Fixed-Viewpoint Media
Feature | Traditional Fixed-Viewpoint Media | Embodied Vision-Interaction Streams (This Use Case)
Viewpoint & Perspective | Static, passive, third-person. Fixed Field of View (FoV). | Dynamic, active, first-person. Continuously changing viewpoint and FoV as the agent moves.
Data Content | Primarily 2D/3D video encoded for human vision. | Multi-modal Fusion Streams: Video + Point Clouds + other sensor data( e.g. Pose Data). It establishes the connection between data and the physical space
Primary Consumer & Purpose | Human visual perception (viewing, archiving). | Machine/AI perception and inference (3D reconstruction, path planning, manipulation).
Latency Sensitivity | Moderate (100s of ms to seconds). Focus on smooth playout. | Ultra-low latency (ms). Integral part of a real-time control loop.
Bandwidth Profile | Relatively stable and predictable. | Uplink-heavy, highly bursty, and unpredictable.
Interaction | Weak interaction (primarily communication). | Strong interaction. Data streaming enables real-time decision-making and physical action ("Perceive-Stream-Compute-Act").
Encoding & Transport | Optimized for human visual system (H.26x). | May require optimization for machine vision (e.g., feature map transmission, scalable coding for different AI tasks).

## Slide 8: Proposed way forward
Identify and document the Network-Assisted Embodied Video Internet（EVI） related use cases and requirements.
Study potential enhancement to current 3GPP media services to more effectively meet the EVI requirements, such as reducing latency and optimizing bandwidth efficiency.
Document potential EVI's data acquisition, content format, codecs, protocols and transmission solutions.
Explore potential optimization solutions to further reduce the uplink bandwidth consumption of EVI.
Explore how the 5G-A/6G network can be utilized to support EVI-related technologies.
Define QoE model for measuring EVI performance.
  User-centric parameters: multi-stream data types, the quality of data, the accuracy and reliability of the feedback results and etc.
  Network-centric parameters: network delivery speed, latency, end-to-end packet loss, network usage and etc.
Provide guidelines on what features should be recommended for support by the network.
We propose to include Embodied Video Internet (EVI) scenarios into SA4 6G study.