## Slide 1
8.1.2 MC service user identity (MC service ID)
The MC service user identity is also known as the MC service ID. The MC service ID is a globally unique identifier within the MC service that represents the MC service user. The MC service ID identifies an MC service user. The MC service ID may also identify one or more MC service user profiles for the user at the application layer.
There are attributes associated with the MC service ID configured in the MC service that relate to the human user of the MC service. Typically, this information identifies the MC service user, by name or role, may also identify a user's organization or agency, and may also identify MC service user's service subscription to one or more MC services. Such attributes associated with an MC service ID can be used by the MC service server to make authorization decisions about the MC service granted to the user. For example, if the MC service user is subscribed to MCPTT service, an attribute that identifies a user's role as an incident commander could automatically be used by the MCPTT service to grant the user additional administrative rights over the creation of groups, or access to privileged talk groups.
The MC service ID shall be a URI. The MC service ID uniquely identifies an MC service user in an MC system. The MC service ID indicates the MC system where the MC service ID is defined.
When required by the MC service provider, the MC service ID is hidden from the signalling control plane.
A default or temporary MC service ID may be used where a user is not yet associated with a device. When a user would like to use one or more MC services but has not been authenticated by the identity management server, a default or temporary MC service ID and a corresponding MC service user profile may be used.
For the purposes of this document, an MC service administrator, MC service dispatcher, or MC service authorized user is an MC service user that has been granted special privileges within the context of the client function being performed (e.g. MC service client, group management client, configuration management client, key management client). For example, the MC service ID of a group management client of an MC service administrator can be authorized within the group management server to create new groups and add members to groups (i.e. administrative function), but is not authorized to dynamically create group or user regroups (i.e. operational function). Alternatively, for example, the MC service ID of a dispatcher will typically be authorized to dynamically create group and user regroups, but is not authorized to create new groups or add/delete members to groups. The MC service authorization framework is defined in TS 33.180 [25].

## Slide 2: Key attributes of a MC service ID
It is a SIP URI in the form of
  SIP URI: sip: user1@PSCA.MCPTTServerEAST.att.com
A typical HTTP URI:
  HTTP URI: https: //PSCA.PUBHttp1.att.com/user1/123?format=json

## Slide 3: How MC service ID assigned to to be used in MC service

## Slide 4: Example of Call from user1 to userB
SIP: user1@MCPTT Server EAST.att.com
SIP: userB@MCPTT Server Y.EU5.com
FROM
TO

## Slide 5: HTTP routing
Subscribe: ??? ID of user1
(Notify) HTTP URI:
https: //PSCA.PUBHttp1.att.com/user1/123?format=json
SIP URI: sip: user1@PSCA.MCPTTServerEAST.att.com

## Slide 6: Possible way forward 1
Make MC Service ID flexible in 8.1.2
The MC service ID shall be a URI with the protocol it is used. The MC service ID uniquely identifies an MC service user in an MC system. The MC service ID indicates the MC system where the MC service ID is defined.

## Slide 7: Possible way forward - 2
Keep the current MC service ID definition in 8.1.2 which is the one used in the MC services and is SIP base.
Define a new MC ID that will used for HTTP transactions and update 10.9 with this new ID.