## Slide 1
ZTE’s view on 6G Core
3GPP workshop on 6G
Incheon, Korea, March 10-11, 2025
Agenda Item: 5
Source: ZTE Corporation
6GWS-250013

## Slide 2: 3GPP R20 Timeline(6G Study)
Note: All starting dates are indicative
2024
#103
Mar.
#111
Mar.
#107
Mar.
#104
Jun.
#108
Jun.
#112
Jun.
#105
Sep.
#109
Sep.
#102
Dec.
#106
Dec.
#110
Dec.
TSGs
Workshop 6G TSGs
Stage 3 6G SID def.
#113
Sep.
#114
Dec.
#115
Mar.
Jun
Workshop IMT-2030 use cases
#116
SA1 6G Study(ies)
SA1 6G SID def.
SA2 6G Study(ies)
Stage 3 6G Study(ies)
Rel-20 – FS_6G part
2025
2026
2027
SA2 6G SID def.
SA3/4/5/6 SID def. and compl. TBD
TBD
5GA SA1 Completion
5GA Stage 2 Completion
5GA Stage 3 Completion
Rel-20 – 5GA part
TBD
Ph1: key issue definition | Dec 2025, or Mar 2026
Ph2: Solution conclusion | Dec 2026, or Mar 2027
ZTE Preference

## Slide 3: Reuse functionalities from 5GC
The following aspects can be inherited from 5GC with potential enhancements
  Architecture aspects:
    MM, SM, QoS model, Edge-Computing, Network Sharing, Satellite Access, ATSSS, CAPIF
    Roaming Architecture, Policy Architecture,
    N2/N4 interface
  eMBB service: Voice, multimedia, XRM, etc,
  uRLLC service: NPN, TSN, 5G-LAN, DataNet, URLLC, etc
  mMTC: Redcap, UAS, NBIoT, etc.
  Specific service: PWS, SMS over NAS, Location, Priority service
  Other: Sensing, Energy Efficiency
The following feature can use 5G technology, i.e. not in first release of 6GC(R21):
  Interworking with EPS
  ProSe, LADN, PIN, V2X
  Ambient IoT

## Slide 4: Functionalities with re-design(Non-backward compatible)
The following non-exhaustive list of functionalities can be studied with non-backward compatible redesign
  Network Slicing: Reduce the complexity on both the UE part and on the management part.
  Non 3GPP access: Single solution for all non 3GPP access, to reduce the complexity on both UE side and network side.
  N1 interface: standalone connection management function and distributed NAS
  SBI evolution: HTTP3 over QUIC, NRF/SCP enhancement, etc.
  User plane: AI based service awareness, protocol enhancements, etc.

## Slide 5: New functionalities
Introduce new service based interface between 6G CN and RAN to achieve more flexible interaction, facilitating the exchange of RAN related information for new 6G features.
  For those new features, CN NF interacts with RAN directly, avoid impact on the AMF.
Other functionalities for new 6G services need inputs from result of FS_6G-REQ, some examples are listed below:
  Data service framework
  Computing service framework
  Sub-network concept
  Digital Twin
  AI Agent communication
To support new services, 6GC is a new core and is standalone architecture.
  NSA is not precluded at this stage, depending on scenarios and operator requirements

## Slide 6: Security aspect – Existing feature enhancement
Update of security key for SUCI
  The provisioning and updating of the Home Network Public Key, Home Network Public Key Identifier, protection scheme identifier, and SUCI calculation indication is left to implementation in 5G
Quantum security
  6G networks are expected to adopt quantum-safe cryptography technology to cope with the security challenges brought by quantum computing: New algorisms + 256 bit keys.
RAN security
  MAC CE has been widely used in 5G, but security protection for MAC CE is still missing. In 6G both PDCP security and low layer security can be supported, for DRB and MAC CE accordingly.
  Integrity protection for system information is missing in 5G: Integrity protection/verification for system information should be native supported

## Slide 7: Security aspect - Proactive Immunity security
6G networks need to consider proactive immunity security mechanisms, similar to the human immune system, to provide active defense functions for network infrastructure and software. This mechanism will enable 6G networks to predict and defend security attacks, rather than just passive responses
Potential topics
  AI for security: use AI predict and defend security attacks.
  Automatic security capability orchestration: introduce a new security NF to control the LCM and configure the security functionalities on demand via service based interface to improve the flexibility of network security capability.
  Security and privacy for new 6G services, e.g. sub-network, new data service

## Slide 8: Management Aspects
Primary features
  Automation and Intelligent
    Common framework for AI(MDAF evolution, Digital Twin, etc.)
    Intent based network management
    AI based close loop automation
    New technology: Generative Artificial Intelligence, RAG, AI Agent, etc.
Management of new 6G service
  Sensing, Data service, Computing service, etc.

## Slide 9: Network Exposure
Reuse 5GC CAPIF as 3GPP network exposure API framework
Introduce a new SBI between RAN and CN for new services, e.g. RAN information exposure/RAN AI capability exposure
Northbound APIs:
  11 Northbound APIs are defined in GSMA OPG/CAMARA
  Should 3GPP define northbound APIs for other scenarios?
    Computing resource, 6G Infrastructure Utilization, etc (from TR 22.870)

## Slide 10: 6G Overall Architecture(conceptual)
New Service(via Data SBI)
  6G Data service
  6G Data SBI
  Digital Twin
  Computing service
  New Security service
  Sensing Function
  AI Agent
SA(NSA not excluded)
RAN SBI for new services
ngPDG SBI for non 3GPP access
Existing Functionality Redesign
  CMF/AMF+/SMF+
  NRF+/SCP+
  6G N1
  6G SBI

## Slide 11: Thank You!