## Slide 1
Building the Foundation for 6G: Critical Broadcast Requirements for Next-Generation Collaborative Networks
3GPP workshop on 6G
March 10 – 11 2025, Incheon, Korea
Source: Shanghai Jiao Tong University

## Slide 2
The number of traditional broadcast users has been decreasing annually
Description
Chart: 
| 2017年 | 2018年 | 2019年 | 2020年 | 2021年 | 2022年
中国彩电销量（万台） | 4752 | 4774 | 4772 | 4534 | 3835 | 3634


中国电视开机率（%） | 70 | 51.3 | 39.1 | 60 | 27.7 | 7.04
2017 2018 2019 2020 2021 2022
Sales volume of color TV sets in China (10,000 units)
Average daily minutes of broadcast TV viewing in UK
User playback devices are more diverse
Mobile terminal becomes the main way of presentation

## Slide 3
Description
The reception quality of broadcast users is poor
  · Located at the edge of broadcast coverage
  · Multi-path
  · Doppler shift
  ...
The number of cellular subscribers has soared, and the quality of reception has deteriorated
  · Hot spot emergency
  · Popular linear live streaming, such as concerts, sporting events, etc
  ...
Different users need multi-quality, multi-view linear multimedia services
  · A variety of playback devices
  · Multiple forms of media content
  · Different reception environments
  ...

## Slide 4
The design of 6G broadcast core network can adapt to the above three service scenarios
Use case 1：Cellular networks support broadcast users to replace lost data
6G broadcast core network
HTHP
LTLP
video broadcasting
Cell towers replace lost data
HTHP
LTLP
Traffic offloading
Use case 2：Broadcast networks support offloading traffic from cellular networks
Use cases
core network
video broadcasting
Use case 3：Support multi-view, multi-quality immersive broadcasting
HTHP
LTLP
video broadcasting
Multi-channel data fusion
Common perspective
Unique perspective
cellular core network
6G broadcast core network
cellular core network
core network
6G broadcast core network
cellular core network

## Slide 5
2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
enTV
200 us CP
Dedicated Mode
FeMBMS
Long CP
Greater mobility
Rel-14
Rel-16
Rel-17
NR-MBS
Rel-18
Rel-9
Rel-12
Rel-11
Rel-10
eMBMS
eMBMS enhancement
DASH
Counting
Service continuity
QoE
MooD
Based on MBSFN
NR-MBS+
Rel-14
MTC
SC-PTM
3G/4G
5G
?
2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Rel-13
 | Single base station coverage | MBSFN
FeMBMS | 30km | √
NR-MBS | 1.5km | ×
Low spectral efficiency
Poor reliability
FeMBMS
support 6/7/8MHz
Rel-18
SC-PTM
Existing 3GPP broadcast technology route

## Slide 6
Design cooperative transmission mechanism and necessary functions in 6G broadcast core network
Potential New Requirements needed to support the use cases
Real-time monitoring mechanism
Adjust the transmission mode in real time according to user data changes
Decision mechanism
According to the collected information, scheduling is carried out according to the decision objectives
Information collection mechanism
Trigger request mechanism
Service screening
Adapt network resources to services
Broadcast user management
Multiple broadcast base station resource management
Service Announcement upgrade
· content provider trigger
· core trigger
· User trigger
Allows interaction with 5GC, content sources to get the necessary information
· Replace lost service data
· Switch transmission mode
· MBSFN
· Non-MBSFN
Design SA mechanism suitable for cooperative transport mechanism

## Slide 7
Use case 1：Cellular networks support broadcast users to replace lost data
Service Flows
The user receives the service normally through the broadcast.
The core network finds that a considerable number of users are about to enter the area with poor broadcast signal, and there is a risk of declining service quality.
The broadcast core network forwards corresponding services to the cellular core network.
The unicast base station helps broadcasters to continue to provide high quality replenishment services.
Broadcast base station
Cellular base station
Cellular base station
Cellular base station
Notes: 、

## Slide 8
Use case 2：Broadcast networks support offloading traffic from cellular networks
Service Flows
Users receive services through the unicast.
The number of users of the same (unicast) service increases rapidly on the cellular core network, which consumes a large amount of time-frequency resources, resulting in degraded service quality and network breakdown.
The cellular core network forwards corresponding services to the broadcast core network.
The broadcast base station helps unicast base stations continue to provide high-quality live broadcast services.
Broadcast base station
Cellular base station
Cellular base station
Cellular base station

## Slide 9
Use case 3：Support multi-view, multi-quality immersive broadcasting
Service Flows
Services are encoded to form multi-view, multi-quality media data.
Different users have different needs.
The common picture content is transmitted through the broadcast network, and the differentiated view picture is transmitted through the cellular network.
The display is recovered by end users by means of perspective superposition and data fusion.
Broadcast base station
Cellular base station
Cellular base station
Cellular base station
Common Layer
Unique Layer