## Slide 1: Functional alias as target in client originating procedures
Magnus Tränk (magnus.trank@ericsson.com)
Ericsson

## Slide 2: Functional alias - Overview
A functional alias (FA) is a user selectable alias that is tied to the assignment or task of the user. A MCX User can activate one or multiple functional aliases at the same time.
A functional alias can be used to identify for example the driver(s) of a particular train, identified by train number and the role of the user on that train.
Examples: +491622034711001@railways.org or driver.train4711@railways.org
Another example is a functional alias that is used to identify the user(s) currently assigned the dispatcher role in a control room.
Examples: 230001@police.org or dispatcher.stockholm@police.org
Note: All the above examples are also fully valid MCPTT IDs.

## Slide 3: Functional alias – MC Service ID
The functional alias and the MC Service ID are both:
  Globally unique URIs
  Used to identify the target user/client for any communication
No specific format of the two types of URIs has been defined that can be used to distinguish a functional alias from an MC Service ID

## Slide 4: Private call
For private call the end user or the MC client must know if the target is a functional alias or a MCPTT service ID.
Reference to TS 24.379, clause:
Consequence: Either the end user must indicate to the client that it wants to make a FA call or a normal call, or the client must, based on local client configuration be able to select FA or MCPTT ID.

## Slide 5: Several limitations
Several features lack or has limited support for FA, for example:
  Group call
  Remotely initiated private call
  Emergency private call
  Private call back
  Ambient listening
Current <PrivateCallList> in MCPTT user profile can not contain FA
Current <IncomingPrivateCallList> in MCPTT user profile can not contain FA

## Slide 6: Proposals
Remove the burden on the end user (or client) to know if the call is to a MCPTT ID or to a FA by:
  Adding a generic requirement in TS 24.379 that MCPTT ID and FA is both applicable URIs as target in any communication initiation.
  Make the MCPTT server responsible to identify the target MCPTT ID either based on the FA or MCPTT ID (see next slide for further clarification).
  For backward compatibility reasons keep the private call details on FA, but change “shall” requirements to “may”.

## Slide 7: MCPTT server – Controlling role
When the MCPTT server (controlling role) decides on the routing to the target MCPTT user, we rely on the server implementation:
How the server determines that a target is an MCPTT ID or an FA that need to be resolved to MCPTT ID(s) can be out of the scope of 3GPP.

## Slide 8: Thank You!