## Slide 1: Motivation for low-band carrier aggregation via switching enhancement in Rel-20
3GPP TSG RAN Meeting #109
Beijing, China, September 15-18, 2025
Agenda Item 9.1.4.7
Source: TELUS, Bell Mobility, Apple, BT plc, Skyworks Solutions, Inc, Murata, AT&T
RP-252702

## Slide 2: Rel-19 NR_LBCA_Sw WI status and its evolution
Current Status:
  In Rel-19 3GPP approved new WI (NR_LBCA_Sw) to enable low band-low band CA via switching [1]
  One CA combination approved for FDD + SDL low-band carrier aggregation (CA_n5A-n29A)
  Five additional combinations identified as candidates of interest, including FDD + FDD combinations, to be handled via basket WI approach [2]
  Carrier switching solution:
    Semi-static RRC-based solution has been adopted [1]
    While not optimum, this solution was mainly adopted to reduce RAN1 impact in Rel-19
Proposed evolution in Rel-20:
  Dual DL solution
  FDD + FDD low band carrier aggregation
  Non-RRC based switching solution

## Slide 3: Scenarios where this solution is applicable
Dual DL solution illustration

## Slide 4: Proposed low-low CA Evolution
Device needs to support inter-carrier scheduling: UE monitors PDCCH DCI of FDD Carrier 1, which has scheduling information for both carriers
Device switches to Carrier 2 based on DCI instruction
Device switches back to Carrier 1 after scheduled transmission interval of Carrier 2 is finished
TTI :
TTI :
FDD band
Tx
Rx
SDL band
Rx
Transceiver
TTI :
Tx
Rx
Rx
Transceiver
Tx
Rx
Rx
Transceiver
FDD band
SDL band
FDD band
SDL band
Note: below figure shows Carrier 2 as SDL carrier. Similar solution is applicable when Carrier 2 is FDD carrier

## Slide 5: References
[1] RP-243317: New WID on low band carrier aggregation via switching
[2] RP-242532: Motivation for a new work item on low band carrier aggregation via switching in Rel-19