## Slide 1: Discussion on Additional NR band combinations for NR features in Rel-20
China Telecom, Huawei, HiSilicon
2025.11
3GPP TSG-RAN WG4 Meeting #117
Dallas, USA, Nov. 17-21, 2025
R4-2520869

## Slide 2: Justification-overall
For certain NR features, specific requirements are defined for particular band combinations. To ensure support for each feature, these requirements must be analyzed and specified on a case-by-case basis. This WI is established for this purpose by introducing a consolidated framework.
Unlike previous releases which required individual WIs per feature, this WI provides a unified procedure for analyzing multiple features and their band combinations for each specific feature or objective. The potential objectives include
  Objective #1: DL interruption for NR and EN-DC band combinations at dynamic Tx Switching in Uplink
  Objective #2: Simultaneous Rx/Tx band combinations for NR CA/DC, NR SUL and LTE/NR DC
  Objective #3: TBC
Proposal：This WI provides a unified procedure for analyzing multiple features and their band combinations for each specific feature or objective.

## Slide 3: Proposed objective #1: DL interruption
    Justification：Request for FDD+FDD DL interruption analysis for uplink tx switching:
  Observation 1-1: This flexible multi-carrier scheduling scenario is not limited by FDD+TDD combinations, but the FDD+FDD combinations shall be considered, which can further improve the utilization of operator’s carriers.
  Uplink tx switching feature including FDD+FDD case has been supported by the current specification, no restriction to the duplex of the band
  Observation 1-2: Uplink tx switching feature including FDD+FDD case has been supported by the current specification
  Existing analysis/requirements for mandating no DL interruption mainly cover the CA combinations of FDD+TDD or TDD+TDD. Some analysis provided in R4-2413318 for mid band combination under Rel-19 DL interruption basket WI has shown possibility of mandating no DL interruption for FDD+FDD combinations, as shown in the figure 1.
  Proposal 1-1: Discussion on whether and how to introduce no DL interruption requirement for FDD+FDD CA in Rel-20, such as CA_n1-n5, CA_n1-n3.
  The advantage of uplink tx switching is not only to increase uplink throughput but also to enable flexible multi-carrier scheduling. For example, by considering the timely air interface information such as interference experienced by the UE, coverage of different frequency bands, and cell load conditions, the optimal carrier can be dynamically selected for scheduling among the entire available candidate spectrum, thereby further enhancing the utilization of operator carriers. This flexible multi-carrier scheduling scenario is not limited by FDD+TDD combinations, but the FDD+FDD combinations shall be considered.
n1
n3
n1
n1
n3
n3
Tx1
Tx2/Rx1
Rx2
Rx3
Rx4
1T-1T Switching
  Figure 1 1T-1T switching without DL interruption for n1-n3

## Slide 4: Proposed objective #1: DL interruption
    Justification： Request for adding more combinations supporting no DL interruption for 3 or 4 bands uplink tx switching:
  In Rel-18, up to 3 or 4 bands are involved in the determination of one uplink switching, which means under the downlink 3 or 4 bands CA, the switching cases include
    1) Two bands involved in the uplink switching belong to different uplink serving cells.
    2) More than two bands involved in the uplink switching.
  The first case can refer to the previous approach of Rel-17 basket WI to specify the note for no DL interruption clarification. For the second case, the newly introduced uplink switching in Rel-18 applies, if on any two of the bands the UE is configured with switchingOptionConfigForBandPair set to 'dualUL'. However, the corresponding mandating no DL interruption requirements are not specified in Rel-18 for any band combinations. Furthermore, now RAN4 existing requirement format such as “no for CA_nX-nY” of no DL interruption clarification for 2 uplink bands CA can not apply to 3 or 4 bands, which may need to be specified based on band pair rather than band combination.
  In Rel-19, a basket WI was set to work on the request for the band combinations to mandate no DL interruption for dynamic Tx switching. The clarification such as “no for CA_nX-nY” was updated by “no for nX-nY” was updated in order to apply to 3 or 4 UL bands configuration cases in Rel-19 basket WI, and some of band combinations are specified with no DL interruption for 3 or 4 UL bands configured. While, there are still requests for band combinations for the 3 or 4 UL bands configuration cases
  Proposal 1-2: Continue to work on the new request for band combinations with 3 or 4 UL bands configuration cases. Such as CA_n1-n3-n78 with n1, n3 and n78 UL bands configuration.

## Slide 5: Proposed objective #1: DL interruption
    Objectives：
    Discuss and specify inter-band uplink CA and EN-DC combinations for which DL interruption is not allowed when dynamic switching between two uplink bands is conducted, or when dynamic switching with 3 or 4 uplink bands is conducted for inter-band uplink CA.
  Based on the requested band combinations from operators, analyze if it is feasible to specify no DL interruption in RAN4 specification.
  Based on the feasibility analysis for specific combination, decide to introduce no DL interruption in RAN4 specification.
  Note: The requirement of “no DL interruption” to be specified for the band combinations in the WI applies to Rel-20.
    Specify REL-independent way for CA combinations of this WI.
  For the CA combinations with three or four bands specified in Rel-20, introduce for uplink Tx switching across three or four bands in a REL-independent way starting from Rel-18.
  Note: the CA and EN-DC combinations with two bands uplink switching have been introduced in a REL-independent way starting from Rel-16/17.
    The band combinations requested for mandating no DL interruption to conduct dynamic Tx switching are listed in table:
Configuration | Uplink band | contact name, company | Contact email | other supporting companies (min. 3)
CA_n1-n5 | n1, n5 | Bo Liu, China Telecom | liubo1@chinatelecom.cn | 
CA_n1-n3 | n1, n3 | Bo Liu, China Telecom | liubo1@chinatelecom.cn | 
CA_n1-n3-n78 | n1, n3, n78 | Bo Liu, China Telecom | liubo1@chinatelecom.cn | 

## Slide 6: Proposed objective #2: Simultaneous Rx/Tx
    Justification:
  Simultaneous Rx/Tx capability for inter-band CA, SUL and EN-DC band combinations were introduced from Rel-15. Specifically, for inter-band CA and EN-DC combination, the capability is used for TDD-TDD and TDD-FDD band combinations. According to the description of the capability, it is conditional mandatory and the condition is described in the field, i.e. indicated in the RAN4 spec which combinations should mandatorily support simultaneous Rx/Tx. For the combinations which have no such indication, the capability is optional, i.e. for UE supporting simultaneous Rx/Tx, the capability should be reported, otherwise, the capability is absent or not reported. Since the capability is important for network scheduling, it should be reported accurately.
  In Rel-17, the principles for judging the mandatory capability for a band combination have been discussed, and the cases include:
    FR1+FR1 FDD-TDD band combination
    FR1+FR1 TDD-TDD band combination
    FR1+FR2 FDD-TDD band combination
    FR1+FR2 TDD-TDD band combination
    FR2+FR2 TDD-TDD band combination
  In Rel-18, a basket WI for simultaneous Rx-Tx was created. In Rel-18 WI, as the capability is defined for CA, SUL, MR-DC and NR-DC band combinations, and applicability of the corresponding requirements cover different specifications, e.g., TS 38.101-1 and TS 38.101-3, the way to treat simultaneous Rx/Tx capability as well as the requirements is aligned among the specifications.

## Slide 7: Proposed objective #2: Simultaneous Rx/Tx
    Justification:
  In Rel-19, further discussions have addressed several specification issues concerning simultaneous Rx-Tx requirements originally identified in Rel-18. Key points include simplifying or removing redundant and overlapping Notes to enhance implementation clarity, clarifying the lack of mandatory simultaneous Rx-Tx notes for certain higher-order EN-DC band combinations to aid vendor implementation and testing, and examining the CA_n40-n41 combination where 4Rx requirements on n41 may require relaxation. The need to support simultaneous Rx-Tx in the CA_n5-n8 combination with overlapping spectrum was also discussed. Additionally, case-by-case analysis of band combinations will be conducted to prevent ambiguity, with outcomes documented in TR 38.793 as an extension of the Rel-18 work.

## Slide 8: Proposed objective #2: Simultaneous Rx/Tx
    Objective
  Identify feasibility of simultaneous Rx/Tx capability/operation for each requested FDD-TDD and TDD-TDD band combinations for CA, SUL, MR-DC based on technical analysis, especially for those with large MSD values. If needed, specify the MSD requirements for the identified band combinations.
    Note 1: Band combinations considered in this WI have to be introduced first via basket WIs or completed in previous releases if necessary.
    Note 2: Whether the simultaneous Rx-Tx capability could be supported or not depends on the evaluation of MSD for the requested band combinations case by case.
    Note 3: Applicability of simultaneous Rx/Tx capability to FDD-TDD band pairs should be reviewed
    Note 4: Band combinations of the following power classes are considered in this WI: PC3, PC2 and PC1.5.
  Align the specification treatment of simultaneous Rx/Tx capability for CA, SUL, MR-DC and NR-DC band combinations.
Band combination | Power Class | Note | status
CA_n5-n8 | PC3 | If not finished in Rel-19, will be moved to Rel-20 Study the feasibility of supporting UL CA operation for FDD-FDD inter-band CA band combination with partial overlap on UL and DL in Rel-19. Discuss and specify if needed, the general method of scheduling restriction for non-simultaneous Rx-Tx between n5 DL and n8 UL. | Pending
CA_n78-n104 | PC3, PC2 |  | Open
CA_n79-n104 | PC3, PC2 |  | Open

## Slide 9: Thanks!