## Slide 1: Test Frequency Calculation Tool, updates and way forward.
Document for discussion and information.
Agenda Item:5.3.3.10
R5-254695
3GPP TSG-RAN5 Meeting #108
Bangalore, Aug 25 – 29 2025

## Slide 2: Introduction
- This discussion paper will share the updates and suggested way forward for the development of the Frequency Calculation Tool.

## Slide 3: Updates since RAN5#107.
Support for new output format in .JSON was added.
The old output format (.CSV) is still available.
At this stage, .JSON output is only supported for intra band noncontiguous CA combination, including UL CA.

## Slide 4: What is supported by the tool today (38.508-1, Annex C)
C.3: Determination of SSB and CORESET#0
C.2.1.1: Determination of test frequencies for Low-, Mid- and High-Range, (FR1, FR2, FDD, TDD).
C.2.2: Determination of test frequencies for asymmetric NR bands and symmetric uplink and downlink channel bandwidth combinations.
C.2.3: Determination of test frequencies for asymmetric uplink and downlink channel bandwidth combinations.
C.2.4.2.2: Determination of test frequencies for Low-, Mid- and High-Range, for NR Intra-band Contiguous CA, FR1 and FR2, for 2 carriers only.
C.2.4.3: Determination of test frequencies for NR Intra-band Non-Contiguous CA , only FR1, only 2 carriers.
New: Determination of test frequencies for single frequency with flexible TX-RX separation (NTN)

## Slide 5: What is not supported by the tool today. (38.508-1, Annex C)
C.2.1.2: Determination test frequencies for Mid-Low and Mid-High-Range for signalling tests.
C.2.4.2A: Determination of test frequencies for FR1 NR Intra-band Contiguous CA without UL CA for bands with uplink bandwidth less than downlink bandwidth.
C.2.5: Frequency determination for supplemental uplink.
C.2.6: Frequency determination for EN-DC configurations.
C.4: Determination of SSB and CORESET#0 for RRM testing with SSB SCS 120 kHz and 240 kHz.

## Slide 6: Way forward
Sort out legal matters (copyright, etc) on how to handle the python tool.
Add handling of Notes to the calculation tool for .JSON tables.
Update tool to produce output according to JSON format definition for Intra band CA contiguous combination. (for other variants, like “single frequency” tables?).
Continue to remove manual input for different bands.