## Slide 1: Discussion of A-IoT Device Conformance Testing
CMCC, Huawei
3GPP TSG-RAN5 Meeting #108
Bengaluru, India, 25 – 29 August 2025 R5-255095

## Slide 2
Background
Unique_ID | Name | Acronym | Release | Start | Finish | %Complete
1020055 | Ambient power-enabled Internet of Things | AmbientIoT | Rel-19 | Mar. 2022 | Sep. 2025 | 95%
1020085 | Study on solutions for Ambient IoT (Internet of Things) in NR | FS_Ambient_IoT_solutions | Rel-19 | Dec. 2023 | Dec. 2024 | 100%
1060084 | Solutions for Ambient IoT (Internet of Things) in NR | Ambient_IoT_Solutions | Rel-19 | May 2024 | Mar. 2026 | 36%
1061084 | Core part: Solutions for Ambient IoT (Internet of Things) in NR | Ambient_IoT_Solutions-Core | Rel-19 | Oct. 2024 | Sep. 2025 | 84%
1062084 | Perf. part: Solutions for Ambient IoT (Internet of Things) in NR | Ambient_IoT_Solutions-Perf | Rel-19 | Dec. 2024 | Mar. 2026 | 0%
970078 | Study on Ambient IoT (Internet of Things) in RAN | FS_Ambient_IoT_RAN | Rel-18 | Sep. 2022 | Sep. 2023 | 100%
Observation 1: For the Rel-19 RAN work item Ambient_IoT_Solutions, the overall completion level for core part has reached 84% after RP#108 (June 2025) and will be completed after RP#109 (September 2025)

## Slide 3
Observation & Proposal
Observation 2: There are new TS specs produced for A-IoT in RAN1, RAN2 and RAN4
  RAN1: TS 38.291 “Ambient IoT Physical Layer (Release 19)”
  RAN2: TS 38.391 “Ambient IoT Medium Access Control Protocol specification (Release 19)”, only MAC requirements included without RRC/RLC/PDCP etc.
  RAN4: TS 38.191 “NR; Ambient IoT device radio transmission and reception (Release 19)” , only RF&RRM OTA requirements for Device 1 included without conducted mode.
Proposal 1: Considering “UE” has been removed or replaced with “Ambient IoT device” in RAN2 TS 38.391 and RAN4 TS 38.191, RAN5 to endorse a new WID for R19 A-IoT device conformance testing with title of “New WID on UE Conformance - Solutions for Ambient IoT (Internet of Things) in NR” and Acronym of “Ambient_IoT_Solutions-UEConTest”.
Device 1: ~1 µW peak power consumption, has energy storage, RF envelope detector receiver, initial sampling frequency offset (SFO) up to 10X ppm, neither R2D nor D2R amplification in the device. The device’s D2R transmission is backscattered on a carrier wave provided externally.

## Slide 4
Proposal
 | RAN5 New specification (TS/TR) | Remarks
1 | NR; Ambient IoT device conformance specification; Part 1: Radio transmission and reception (Release 19) | To specify RF & RRM conformance test cases for R19 A-IoT devices, including Common Environment Against RAN4 TS 38.191 “NR; Ambient IoT device radio transmission and reception (Release 19)”
2 | 5GS; Ambient IoT device conformance specification; Part 2: Protocol (Release 19) | To specify MAC conformance test cases for A-IoT devices Against RAN2 TS 38.391 “Ambient IoT Medium Access Control Protocol specification (Release 19)”
3 | 5GS; Ambient IoT device conformance specification; Part 3: Applicability of radio transmission, radio reception, radio resource management and protocol test cases (Release 19) | To specify recommended test case applicability for RF, RRM and protocol conformance test cases
4 | 5GS; Ambient IoT device conformance specification; Part 4: Common test environment (Release 19) | To specify common test environment for R19 Ambient IoT device
Proposal 2: To introduce new conformance specifications for A-IoT device conformance testing as indicated in the table below.

## Slide 5
Proposal
 | RAN5 New specification (TS/TR) | Remarks
5 | 5GS; Ambient IoT device conformance specification; Part 5: Common Implementation Conformance Statement (ICS) proforma (Release 19) | To specify common ICS proforma for RF/RRM and protocol conformance test cases
6 | 5GS; Ambient IoT device conformance specification; Part 6: Protocol Test Suites (Release 19) | To specify the protocol and signalling conformance testing in TTCN-3 (test model) for the A-IoT device
7 | NR; Derivation of test tolerances and measurement uncertainty and test points for Ambient IoT device radio transmission and reception conformance test cases (Release 19) | To specify Derivation of test tolerances and measurement uncertainty and Derivation of test points for R19 A-IoT devices

## Slide 6: Thank you !