## Slide 1: Discussion on test frequency simplification for inter-band CA and DC band combinations
ZTE Corporation, Huawei
3GPP TSG-RAN5 Meeting #109 R5-256314r1
Dallas, US, November 17 – 21, 2025

## Slide 2: Overview on test frequencies for inter-band CA/DC band combinations
In TS 38.508-1, test frequencies are specified for bands and band combinations.
For inter-band CA configurations, the test frequencies are specified by NR CA downlink / uplink configuration component bands / band combinations and applicable for protocol testing. The single component band and intra-band CA test frequencies can be further referred to the related test frequency tables in the spec. For example, for three bands inter-band CA_n1A-n3A-n78A, the test frequencies can be shown as below, in which the reference test frequencies for n1, n3 and n78 are further specified in clause 4.3.1.1.1.1/3/78 respectively. However, it can also be seen that in Table 4.3.1.1.2.2-1 most cases have similar test frequencies for CA_nXA-nYA-nZA with similar downlink and uplink configurations.
Observation 1 In TS 38.508-1, test frequencies for inter-band CA band combinations are specified by NR CA downlink / uplink configuration component bands / band combinations and applicable for protocol testing.
Observation 2 In most cases, same rules are followed in the test frequency table for different CA configurations, which makes the table looks quite redundant.

## Slide 3: Overview on test frequencies for inter-band CA/DC band combinations
In TS 38.508-1, many typos are found in the test frequency tables for inter-band CA due to the redundant contents.
CA_n8A-n78(2A)
(TS 38.508-1) (TS 38.521-1)
CA_n29A-n66B
(TS 38.508-1) (TS 38.521-1)
Observation 3 In TS 38.508-1, there are many typos in the test frequency tables for inter-band CA band combinations due to the redundant contents in the table.

## Slide 4: Overview on test frequencies for inter-band CA/DC band combinations
For inter-band EN-DC configurations, the following guidelines apply:
For the E-UTRA band and E-UTRA CA configurations, test frequencies as specified in TS 36.508, clause 4.3.1 are used.
For the NR band and NR CA configurations, test frequencies as specified in clause 4.3.1.1 are used.
For the EN-DC inter-band configuration that includes an EN-DC contiguous configuration, the EN-DC contiguous configuration is listed in the NR configuration column and the test frequencies as specified in clause 4.3.1.4.2 are used.
Observation 4 Similar to the cases in inter-band CA band combinations, some general rules are also applied to inter-band DC configurations. The test frequency table for EN-DC configurations also looks quite redundant which can be simplified if a symbolic configuration is applied, e.g. both the above DC_1A-3A_n28A and DC_1A-3A_n41A could be represented by DC_XA-YA_nZA where X, Y are E-UTRA bands and nZ is NR band.

## Slide 5: Overview on test frequencies for inter-band CA/DC band combinations
However, it is also noted that the test frequency tables for inter-band CA/DC band combinations are also essential in signalling as they specify which combinations are applicable and are used for the TTCN implementation. There are some concerns for signalling test if the explicit CA, NR-DC and EN-DC combinations are lost. To simplify the test frequency tables, it is suggested to keep the entry of combinations but to only simplify the “general rules”part. For the E-UTRA band and E-UTRA CA configurations, test frequencies as specified in TS 36.508, clause 4.3.1 are used.
Observation 4 Test frequency tables for inter-band CA/DC band combinations are also essential in signalling as they specify which combinations are applicable and are used for the TTCN implementation. Similar to the cases in inter-band CA band combinations, some general rules are also applied to inter-band DC configurations. The test frequency table for EN-DC configurations also looks quite redundant which can be simplified if a symbolic configuration is applied, e.g. both the above DC_1A-3A_n28A and DC_1A-3A_n41A could be represented by DC_XA-YA_nZA where X, Y are E-UTRA bands and nZ is NR band. The entries of combinations are suggested to be kept.

## Slide 6: Simplification on inter-band CA/DC test frequency tables
Proposal 1 It is suggested to simplify the inter-band CA test frequency table with the general rules as below.
The general rule for deciding test frequencies for inter-band CA configurations are represented by symbolic CA configurations using nX, nY and nZ as the different bands in the CA Configuration. E.g. CA_nXA-nYA-nZA could be representing the configuraion CA_n1A-n3A-n78A by interpreting of nX=n1, nY=n3 and nZ=n78. Any CA configurations not applying the general rule could be listed separately.
The specified NR inter-band CA configurations are kept as entries in the table (First two columns).
Example 1

## Slide 7: Simplification on inter-band CA/DC test frequency tables
Proposal 2 It is suggested to simplify the inter-band EN-DC test frequency table with the general rules as below.
The general rule for deciding test frequencies for inter-band EN-DC configurations are represented by symbolic DC configurations using band X, Y/nY and nZ as the different bands in the DC Configuration. E.g. DC_XA-YA_nZA could be representing the configuraion DC_1A-3A_n28A by interpreting of X=1, Y=3 and nZ=n28. Any DC configurations not applying the general rule could be listed separately.
The specified inter-band EN-DC/NE-DC configurations are kept as entries in the table (First two columns).
Example 2

## Slide 8: Thank you!