## Slide 1: 6G Computing Support: SA1 defined use cases and potential requirements
OPPO, Ofinno, Intel, Toyota, CMCC, China Unicom, ZTE, MediaTek, vivo, LG Electronics, Lenovo, China Telecom, NEC, CATT, Rakuten Mobile

## Slide 2: Computing in SA1
Definition
6G Computing Service: a service provided by 6G network utilizing computing resources in Service Hosting Environment, which can be used by a subscriber (via UE)/3rd party.
NOTE 1: The computing resources can refer to hardware and/or software that provides the required processing, storage capability etc. to perform computational tasks (e.g. XR rendering).
Service Hosting Environment: the environment, located inside of 6G network and fully controlled by the operator, where Hosted Services are offered from.
Use case requirement consolidation
Currently, about 70 Potential Requirements (PRs) adopted in TR22.870v0.4.1
The SA1 consolidation document is attached
All PRs can be categorized into 8 categories illustrated in the table in next page

## Slide 3: Categories for adopted SA1 computing requirements
 | Category | Requirement Description | Original PR# in TR22.870
1 | Computing Resource Provision | The 6G network shall provide computing resources required for AI services in the Service Hosting Environment, support the execution of computing tasks for UEs and authorized third parties, and the provision of subscription-based computing services, complying with user consent, operator policies and regulatory requirements. | PR 6.3.6-1, PR 6.5.6-1, PR W.2.6-1, PR 6.10.6-4
2 | Computing Task Offloading and Rendering Support | Support computing task offloading for third-party applications (including AI tasks, 6DoF video/spatial audio rendering), provide core network-controlled rendering-related computing services for authorized third parties, meeting privacy protection, operator policies and regulatory requirements. | PR 9.4.6-1, PR 9.5.6-2, PR 6.31.6-1, PR 9.5.6-1, PR 9.6.6-1
3 | Computing Requirement Definition and Conversion | Support UEs to specify parameters such as execution timing and latency of computing tasks; support converting requirements (e.g., latency) from third-party service providers into corresponding computing and communication resource configurations, requiring user consent and compliance with operator policies. | PR 6.5.6-2, PR 6.5.6-3, PR W.2.6-3, PR 6.25.6-2, PR 6.33.6-1
4 | Computing Resource Management | Collect status information (e.g., workload, available capacity, power consumption) of trusted computing resources in the Service Hosting Environment on-demand or periodically, support monitoring and reporting of resource usage, covering computing, service and network capability-related information of edge servers and cloud servers. | PR 6.2.6-3, PR 9.15.6-1, PR 9.15.6-2
5 | Information exposure | Inform UEs of computing service-related information to assist service invocation; expose service information to authorized third parties (e.g., usage pattern analysis); support information sharing within the Service Hosting Environment to optimize resource configuration, complying with operator policies and user consent requirements. | PR W.1.6-2, PR W.3.6-2, PR W.3.6-1, PR 6.2.6-1
6 | Computing Resource Selection and Coordination | Select one or more Service Hosting Environments based on UE location, resource capabilities, business requirements, etc.; support coordination among multiple environments, as well as collaborative decision-making between UEs and the network on splitting/offloading of rendering tasks, in line with operator policies, third-party agreements and regulatory requirements. | PR 6.14.6-3, PR 6.15.6-1, PR 6.34.6-2, PR 6.37.6-3, PR 6.53.6-1, PR 11.22.6-2, PR 9.15.6-4, PR 6.53.6-2, PR 9.3.6-2
7 | Performance Assurance and Service Continuity | Guarantee end-to-end latency and other performance indicators; support migration of computing tasks between different resources and resource reselection, ensure service continuity and user experience when UEs move or resources change, and support priority processing of computing tasks for high-priority users. | PR 6.15.6-2, PR 6.24.6-2, PR W.1.6-1, PR 6.2.6-4, PR 6.19.6-1, PR 6.33.6-2, PR 9.15.6-6, PR 9.6.6-2, PR 9.15.6-5, PR 6.34.6-3
8 | Security and others | Include resource configuration management, security and privacy protection, and energy consumption data collection; support the provision of computing services in satellite access scenarios and the transmission of computing information between satellites, complying with operator policies, third-party agreements and user consent requirements. | PR 11.22.6-1, PR W.2.6-2, PR 6.24.6-1, PR 8.9.6, PR 8.15.6, PR 6.2.6-2

## Slide 4: Example use case 1 – Offloading for AI model inference
Description
- AI model (e.g. LLM) is pre-installed in 6G network
- The 6G network can provide computing support for AI inference to the end-user.
- The 6G network can select a suitable computing node per subscriber per service based on the request from subscriber or service provider.
- The 6G network can leverage the overall E2E latency (i.e. communication delay+ computing delay) budget of an application service by adjusting communication and computing resource on demand.
- The 6G network also owns valuable data (e.g. sensing or positioning data as environmental information) which can be used for high quality AI inference
- When inference is needed, user send request to LLM in 6G network, and the network feedback the inference result with guaranteeing e2e round-trip latency
Essential Requirements
[PR 6.34.6-1] Subject to operator policy and user consent, the 6G network shall be able to authorize a user to offload task from a 3rd party application (e.g. an AI inference workload) to the Service Hosting Environment.
[PR 6.34.6-2] Subject to operator policy, the 6G network shall support selection of computing resources in the Service Hosting Environment for offloading tasks.
[PR 6.34.6-3] Subject to operator policy and user consent, the 6G network shall be able to prioritize the processing of offloading task request(s) from a high-priority user per service.
Reference: TR22.870 clause 6.34
“6G computing support for AI model inference”

## Slide 5: Example use case 2 – Offloading for XR rendering
Assumption and Description
Several computing resources for XR services are deployed distributed in different locations (owned by 3rd party or operators) and have been enrolled in 6G core network.
XR Application Platform provides the render services to various XR applications.
The UE supporting the XR application is the subscriber of the 6G network. It has registered to the 6G network and was authorized for the computing coordination service
Essential Requirements
[PR 9.15.6-1] The 6G network shall support mechanisms to acquire and maintain the information of trusted computing resources (i.e. edge server(s)) for coordinating the usage of computing resource on demand
NOTE: The information can be related to computing capabilities (e.g. xPUs, storage), service capabilities (e.g. supported applications, status), and network capabilities (e.g. allowed bandwidth).
[PR 9.15.6-2] The 6G network shall support mechanisms to collect status information (e.g. computing workload, congestion information, available capability, power consumption) of trusted computing resources (i.e. edge server(s) or cloud server(s)) on-demand or periodically
[……]
Reference: TR22.870 clause 9.15
“Use case on coordinating computing and communication for XR rendering”

## Slide 6: Example use case 3 – XR gaming acceleration
Assumption and Description
In split rendering: a client renders the most time-sensitive or low-fidelity objects that require less computing resources, while some delay tolerant or high-fidelity objects that demand powerful computing resources are rendered at the server
Mobile network is responsible for the convergence of mobile network and computing power with providing communication resources, computing resource
The 6G network receive the compressed data from application server and perform game rendering for VIP users, helps accelerate the VR game
The VIP user can enjoy the VR gaming without consuming more power on end-device side
Essential Requirements
[PR W.1.6-1] Subject to operator’s policy, the 6G network shall be able to fulfil the user-requested performance requirement (e.g. latency) for the 6G Computing Service.
[PR W.1.6-2] The 6G network shall be able to inform UE of the information related to 6G Computing Service in the Service Hosting Environment (e.g. guaranteed computing capabilities) to assist an UE to invoke a computing service.
Reference: TR22.870 clause W.1
“Use case on Computing service for XR gaming acceleration

## Slide 7: List of Computing related use cases (1)
Clause# in TR 22.870 | Use case | scenario
6.2 | Use case on optimizing 6G infrastructure utilization via resource exposure in 6G | Artifact Intelligence service
6.3 | Use case on end-to-end AI for connected cars | 
6.5 | use case on personalized AI for health monitoring | 
6.7 | Use case on AI-agents communication | 
6.9 | Use case on collaborative AI agents | 
6.10 | Use case on home robots | 
6.14 | Use case on intelligent UAV swarms | 
6.15 | Use case on 6G system assisted target object detection | 
6.18 | Use case on exposing achievable QoS to aid computational resource selection | 
6.19 | Use case on AI-based video analysis | 
6.21 | Use case on 6G network providing on-demand networking with AI Agent | 
6.24 | Use case on distributed 6G network for AI computing | 
6.25 | Use case on AI/ML model training and inference | 

## Slide 8: List of Computing related use cases (2)
Clause# in TR 22.870 | Use case | Scenario
6.31 | Use case on UE-Network collaboration with AI capabilities | Artifact Intelligence service
6.32 | Use case on disaster rescue planning enabled by network AI Agents | 
6.33 | Use case on AI text-to-video generation supported by computing | 
6.34 | Use case on 6G computing support for AI model inference | 
6.37 | Use case on energy efficiency for AI service | 
6.45 | Use case on flexible UE-Network coordination through AI agent(s) | 
6.49 | Use case on 6GS providing low-latency AI inference service | 
6.50 | Use case on real time video super-resolution service | 
6.53 | Use case on AI-driven smart factory with computing service | 
6.55 | Use case on shared embodied AI agents | 
8.9 | Use case on low-altitude logistics supported by NTN | Ubiquitous Connectivity service
8.15 | Use case on On board Computing in 6G NTN domain | 
9.2 | Use case on immersive gaming | Immersive Communication service

## Slide 9: List of Computing related use cases (3)
Clause# in TR 22.870 | Use case | Scenario
9.3 | Use case on multi-media services with deterministic experience via collaborative processing among UE-network-cloud | Immersive communication service
9.4 | Use case on XR rendering offload support | 
9.5 | Use case on seamless immersive reality in education | 
9.6 | Use case on collaborative service in multi-site involved immersive communication | 
9.15 | Use case on coordinating computing and communication for XR rendering | 
11.3 | Use case on cooperating mobile robots | Industry and vertical service
11.22 | Use case on spatial computing enabled dynamic material management | 
W.1 | Use case on computing service for XR gaming acceleration | Other service
W.2 | Use case on computing service enabling personal AI agent | 
W.3 | Use case on computing service in operator managed data network | 

## Slide 10: Proposal
SA1 has defined 36 use cases relevant to computing and may consolidate the potential service requirements into 8 categories in their 6G TR 22.870, SA2 should respect SA1’s effort.
Since SA1 6G study is still ongoing, if anything is missing in TR22.870, companies are welcome to work with SA1 colleagues to clarify in TR 22.870.
SA2 can figure out the according architecture requirements based on SA1 defined use cases and requirements during the solution development phase.
Repeating the work which SA1 has done in 6G study is a waste of precious time of SA2 6G study and unacceptable.