## Slide 1: Some background of broadcast/multicast using in MCX
Cuili
Huawei

## Slide 2
MCX server
MCX client
……
MBMS Broadcast bearer, MBS broadcast session
MBMS/MBS channel for media packet (RTP packet)
MBS multicast session
Receiving data in idle
Receiving data in RRC-Connected/inactive state
MBS multicast session
Receiving data in RRC-Connected/inactive state
Broadcast / multicast usage in MCX service
MCPTT server uses two MBS sessions, one is broadcast for floor control message, the other multicast one is for media packet.
When floor idle is sent over the broadcast channel, the UE receives it in idle mode and keeps in idle mode as it has not UL data to send.
The server receive floor request from MCX client A and sent floor granted to client A. Also send the floor taken via the broadcast channel.
Then server receives the UL media from client A, and sends the packet via the multicast channel to all the recipients.
The recipients receive the DL media via the multicast channel in RRC-Connected/inactive state
MBMS/MBS channel for floor control message

## Slide 3
MCX server
MCX client
……
MBS channel for media packet (RTP packet)
How the UE RRC-inactive capabilities helps
The MC system hopes to use the MBS multicast to improve the efficiency and also considering the transmission quality (comparing with broadcast)
After the MCX server have the full information of the multicast reception capabilities, it can determine who it prefer to keep in connected state.
For those who is able to receive in RRC-inactive, they dose not needs to be set as the preferred to keep in connected state participants, in order to cover the maximum users
MBS channel for floor control message
Multicast RRC-inactive receiving capabilities
Group A
Support RRC-inactive list:..
Only connective list:….