## Slide 1: Continued operator’s view on realistic TPR definition for IMT-2030 / “6G”
TSG RAN Meeting #109 RP-252122 Sept. 15-18, 2025; Beijing, China
Deutsche Telekom, Orange, Spark NZ, Telia Company, Bouygues Telecom, BT, Telefonica, Odido, Vodafone, KPN, Telecom Italia, Telenor, SK Telecom

## Slide 2: No overinflated performance expectations
History: The Technical Performance Requirements (“TPRs”) values defined by ITU had an artificial factor of 10x (ten times) between each generation
With IMT-2020 (aka 5G) very ambitious TPRs were set out, which are fulfilled theoretically with 3GPP’s 5G technology (“Radio Interface Technology - RIT”)
Real commercial cellular network deployments cannot reach such TPRs in practice as they are commercially simply not feasible
The expectations on 5G of both cellular users (Business-2-Consumer) and other industries (Business-2-Business) were far too high, as deployed networks failed to provide performance matching some key TPRs values (e.g. data rates and latency)
For IMT-2030 (aka 6G) realistic and practically reachable TPRs should be defined by ITU from the outset to avoid even higher expectations
With the current 3GPP RAN P SI, 3GPP is in the position to convey this message from commercial industry players to ITU early on to avoid dissatisfaction with 6G as we had seen this with 5G. ITU-R soon starts drafting IMT-2030 requirements.

## Slide 3: 10x ITU Data Rate TPRs are divorced from reality!
DL
UL
IMT2020
User Experienced Data Rates TPRs
If 10x
improvement
is assumed
50 Mbps
100 Mbps
DL
UL
e.g. 500 Mbps
e.g. 1 Gbps
1 Mbps?
Massive gap!
5 Mbps?
IMT2030
User Experienced Data Rates TPRs
Real network performance
Note: User Experienced Data Rates are 5th percentile values
Ookla Consistency data show <90% of speed test in the mobile networks in most countries currently do not offer both >1 Mbps UL & >5 Mbps DL
  https://www.speedtest.net/global-index
  Results include 4G tests. But 5G is not offering a low band UL link budget improvement to boost the cell edge indoor customer experience
IMT-2020 evaluation allowed a “bandwidth scaling” of full buffer simulation results allowing any User Experienced Data Rate to be reached with a sufficiently large bandwidth
  This leads to unrepresentative results on the UL as it doesn’t reflect practical UE power constraints
  A many-times improvement of UL UEDR should also not be expected for 6G without substantial site densification

## Slide 4
1-10-5
eMBB: 4 ms
URLLC: 1 ms
500 km/h
DL: 20 Gbps UL: 10 Gbps
DL: [50-500] Mbps UL: [2-200] Mbps
x 1.5 … 2
of IMT-2020
106
DL: 20 Gbps UL: 10 Gbps
DL: 100 Mbps UL: 50 Mbps
DL: 7.8 / 3.3 UL: 5.4 / 1.6
10 cm
Purple: Suggested KPIs to be adopted by ITU
10 Mbit/s/m2
10 Mbit/s/m2
1
2
5
4
3
1
Multiple UEDR values are proposed for different deployment cases. See slide 6.
2
Peak data rate values are of diminishing relevance to customers. Lower values should be included for 200 MHz bandwidth (~7 GHz)
3
A quantified target value for Energy Efficiency is recommended. Other KPIs/KVIs also TBD.
4
Integration of TN and NTN is required to improve coverage. Common methods for extending coverage at a lower data rate should be considered for various use cases
Area traffic capacity value applicable for indoor deployment only
7
5
8
10 cm an optional capability for indoor
8
7
For ~7 GHz with ≤[1024] AEs
6
Reliability value applicable for UEs in good coverage in an available network outside of handover periods
6
For mMTC, as for IMT-2020
9
9

## Slide 5: Other considerations
Some of the TPRs might need (re-)definition to ensure the baseline deployment scenarios and the resulting values are representative of today’s predominantly macro networks.
  Peak bitrate, user experienced data rate, latency, etc.
Additional deployment scenarios can explore the technology potential in case of denser networks, e.g. HetNets, Indoor deployment
Bandwidth scaling of simulation results for the UL User Experienced Data Rate performance should NOT be used, as cell edge UL performance is usually UE power limited rather than bandwidth constrained
TPRs should be defined in a way that also 5G-Advanced can fulfill the IMT-2030 requirements (as LTE also fulfilled the IMT-2020 requirements)

## Slide 6: Deployment-dependent User Experienced Data Rates (UEDRs)
Multiple UEDR values should be given for a number of different environments, one of which should show the UEDR dependence upon densification
No bandwidth scaling should be used on the UL.
  It is preferred that full bandwidths are used in the simulations
  If that is not possible and lower bandwidth simulations are done, the absolute 5th percentile user data rate should be used rather than a bandwidth-scaled value
It is not necessary to assume 10 simultaneous users in the UL [& DL?] full buffer simulations
  The number of users can be reduced to 2
Different frequency bands can be considered for UL and DL, to maximise UL/DL data rates for a given site density
Test environment | DL UEDR (Mbps) | UL UEDR (Mbps)
Indoor | 500 | 200
Macro Urban 200m ISD | 300 | 30
Macro Urban 500m ISD | 150 | 10
Rural 5 km ISD | 50 | 2
Illustrative
Note 1: Maximum available spectrum bandwidths in different bands: 2x20 MHz @ <1 GHz, 2x40 MHz @ ~2 GHz, 100 MHz @ ~4GHz, 200MHz @ ~7 GHz
Note 2: Indoor refers to deployment with indoor base stations

## Slide 7: Key message from MNOs to 3GPP
The cosigning operators request that 3GPP agrees on a set of recommended TPRs to ITU which are reachable with typical equipment and deployments in cellular networks, rather than overinflated theoretical research targets
This discussion should take place in RAN#107 and RAN#108 which allows to send a LS to ITU from RAN#107 with an initial indication that 3GPP propose to redefine some scenarios for which TPRs should be met and will communicate final proposals for the TPRs no later than June 13th, 2025 (from RAN#108), to allow ITU to consider the 3GPP input in their Meeting No. 49 (Japan, 24 June – 3 July 2025).

## Slide 8
Thanks