## Slide 1: Views on 6G RAN Architecture and Interfaces
RP-252222
Agenda : 8.3.1.2
RAN#109
September 15-18, 2025, Beijing, China

## Slide 2: Guidance for 6G Study by RAN3: 6G RAN deployment
In 5G RAN architecture study during Rel-14, RAN3 spent significant time on the discussion of RAN deployment scenarios (TR 38.801). In the 6G study, RAN3 should also consider the same TN deployment scenarios as baseline for 6G RAN Architecture.
  Proposal 1: As for 5G in TR 38.801, RAN3 study to consider TN deployment scenarios for 6G RAN as baseline.
One key goal of 6G is to lower the TCO for operators so that more resources become available for the deployment of new services and features. Using cloud platforms for RAN deployments allows operators to leverage best-in-class advanced cloud-native solutions (containers, message brokers, load balancers, foundational services etc) to achieve this objective. The 6G RAN architecture evolution shall allow operators to perform such a paradigm shift in RAN deployment over the 6G timeline.
  Proposal 2: For study of 6G RAN architecture, RAN3 should consider that over the 6G timeline, operators may want to leverage cloud-native solution for RAN deployment, e.g., to simplify RAN management, flexible RAN Architecture and reduce TCO.
As part of the 6G study, RAN3 will discuss the 6G RAN functional split. Since operators may want to upgrade present 5G deployments to 6G, it is essential that the 6G RAN architecture has to support the same functional split options as 5G.
  Proposal 3: For study of 6G RAN functional split, RAN3 should consider that the same deployment scenarios need to be supported for 6G RAN as for (SA) 5G RAN.

## Slide 3: Guidance for 6G Study by RAN3: RAN interfaces
5G introduced the service-based architecture (SBA) for the CN to allow for easier, flexible and lower cost cloud deployments. For 6G, the question arises whether SBA should be extended to the RAN-to-CN interface and to RAN-internal interfaces so that RAN deployments can also benefit from cloud-native solutions to enable RAN virtualization and flexible RAN Architecture. RAN3 should therefore study the benefits and shortcoming of service-based vs. point-to-point interfaces for 6G RAN. This comparison should consider operator-specific requirements and various deployment scenarios.
  Proposal 4: RAN3 should evaluate the benefits and shortcomings of service-based vs. point-to-point interfaces for 6G RAN based on various deployment requirements.
In 5G, RAN3 has spent significant amount on how Ambient IOT can be supported via the legacy point-to-point NG-C. This discussion may have to be repeated for 5G ISAC. To make 6G RAN more flexible to the introduction of new services, RAN3 should study the RAN-to-CN interface separately for connectivity services and for beyond-connectivity new services.
  Proposal 5: RAN3 should study SBI vs. PPI separately for connectivity services and beyond-connectivity new services.

## Slide 4: Guidance for 6G Study by RAN3: RAN protocols
In 5G (and 4G), RAN-based C-plane protocols (NG-C, Xn-C, F1-C) use SCTP for the transport network layer. Since this protocol is (essentially) not used outside of 3GPP, it is not well supported anymore by the IETF. Also, SCTP is not compliant with several cloud-native solutions/deployments. RAN3 should study how the present C-plane stacks can be evolved for 6G to more cloud-friendly alternatives.
  Proposal 6: RAN3 to consider evolution of RAN interface protocols to more cloud-friendly solutions in 6G as evolution.
Since 6G is expected to stay with use for quite many years, RAN protocols should be able to evolve as new better protocol or transport solutions become available. Also, based on deployment, different protocol solutions may be more appropriate. RAN3 may want to consider whether and how 6G can support protocol agility so that RAN deployments can be aligned with each operator’s specific long-term objectives.
  Proposal 7: RAN3 to consider protocol agility to allow evolution of transport and application-layer protocols over the time frame of 6G.

## Slide 5: Thank You