## Slide 1
Huawei, HiSilicon
Addition of study on positioning for outdoor Ambient IoT scenarios in Rel-20
3GPP TSG RAN#109 RP-252363
Beijing, China, September 15-19, 2025
Agenda Item: 9.2.3

## Slide 2
Motivation and Use Case
​​Why Outdoor Positioning in A-IoT?
  Outdoor positioning is one of representative use cases of A-IoT.
  Outdoor positioning expands operational horizons of A-IoT device, which unlocks ​​mass-deployment use cases​​ of urban movable asset management and drives scalable commercial value of A-IoT.
​​ Use Case: Destination Supply Chain Visibility
  ​Stage-by-stage shipment knowledge across a supply chain is crucial for holistic management and control.
  Destination positioning is the bottleneck: cell-level localization cannot meet the localization requirements of delivery destination, necessitating higher precision to monitor delivery to e.g., distinct zones within a port area.
  ​​100m accuracy: A positioning accuracy of 100 meters can meet destination visibility requirements for outdoor environments.
Zones positioning within a port area

## Slide 3
Positioning Solution Comparison
Cramér-Rao bound ：
Bandwidth | SNR（dB） | Theoretical Accuracy(m)
180kHz | -10 / 0 /10 | 2054.7/649.7/205.5
10MHz |  | 37.0/11.7/3.7
100MHz |  | 3.7/1.17/0.37
Rx Channels | Horizontal Rx Channels | AOA resolution | Error of 150m distance | Error of 300m distance
64 | 16 | 7.2° | 18.8m | 37.7m
16 | 4 | 28.6° | 74.1m | 148.2m
4 | 2 | 57.3° | 143.8m | 287.7m
​​TDoA-based Solution: Not applicable to A-IoT device because of narrow bandwidth
  The accuracy of ToA measurements is positively correlated with the bandwidth (Cramér-Rao bound).
  The upper bound of ToA ranging performance at -10dB with a 180kHz bandwidth is 1977 meters, which cannot meet the positioning accuracy requirement of 100 meters.
​​AoA-based Solution: Not applicable to A-IoT device because of limited Rx channels
  The angular resolution of AOA is inversely proportional to the number of Rx channels. The horizontal array with 2 Rx channels results in a 56° AOA resolution and 319m positioning error at a distance of 300m.
​​Fingerprint-based Solution: Worthwhile to study
  Fingerprint positioning relies on the consistent spatial distribution of feature fingerprints and does not heavily depend on bandwidth and the number of Rx channels, with the potential to achieve a positioning accuracy of 100 meters.
  Reader measurement-based fingerprint solution has less impact on device and more effort at NW side.

## Slide 4
Blue: UE drop within three sectors; Red: BS site
DL performance: 79m@90%
UL performance: 82m@90%
Fingerprint-based Evaluation
​​Configurations： UMa scenario, model large scale spatial consistency according to clause 7.5 of TR 38.901, ISD: 500m, carrier frequency:900MHz, bandwidth: 180 kHz, fingerprint collection: one reference-UE per 15m spacing, fingerprint: RSRPs of multi cells, algorithm: WKNN
​​Results & Analysis
  Both DL RSRP-based fingerprinting positioning and UL (reader) RSRP-based fingerprinting positioning can achieve positioning performance within 100 meters.
  Compared to the UL RSRP solution, the DL RSRP solution requires devices to perform downlink measurements and reporting, introducing additional processing procedures and power consumption.
  UL RSRP-based solution is purely reader measurement and has less device impact than DL-based

## Slide 5
RAN1 scope
  Identify the candidate technique: fingerprint-based (e.g., RSRP fingerprint) solution is feasible for A-IoT outdoor positioning.
  Define the evaluation assumption. Most simulation parameters can leverage existing positioning assumptions from 3GPP TR 38.855, TR 38.859, and A-IoT-specific assumptions in TR 38.769, ​​except for the following aspects:
    ​​Positioning Reference Signal: A-IoT communication signals/channels as the starting point, e.g., PDRCH.
    Device-dependent factors: E.g. SFO and CFO for active device as per Rel-20 SI agreements.
  Evaluate positioning performance of the candidate techniques.
Study scope
No TU required for SI in RAN2/RAN3/RAN4: The SI phase involves RAN1 evaluating whether the candidate technique can meet the accuracy requirements, without involving feasibility analysis of RAN2/RAN3/RAN4. RAN2/RAN3/RAN4 directly work on their standard positioning support work in the work item phase.