## Slide 1: Device types for the scalable 6GR design
Sources: Panasonic
3GPP TSG RAN Meeting #109
Beijing, China, September 15-18, 2025
Agenda: 8.2.2 Study on 6G Radio
TDOC: RP-252469
For: discussion

## Slide 2: Background
RAN 1 agreed following for the scalable 6GR design and device types.
  Study a scalable 6GR design for diverse device types, considering aspects:
    What should be commonly applicable to all 6G device types
    FFS: add-on features dedicated to specific device types, if any
  Study the device types from physical layer perspective to be supported by 6GR, subject to further discussion and confirmation in RAN
To study the minimum spectrum allocation were also agreed.
  For the study of RAN1 6GR design, consider the minimum spectrum allocation in which 6G can operate, subject to further discussion and confirmation in RAN.
    Note: RAN4 involvement is necessary.
How UE capabilities/features should be defined for 6GR are proposed in 6G workshop and RAN1 by multiple of companies.
  Not to repeat the UE feature definition of NR. More simplified or more combined definition/reporting for testing and economic scale.

## Slide 3: Low-tier 6G device for scalable design
The discussion on "low-tier 6G device for scalable design " and "how UE feature/capabilities is defined/reported" should be separated.
  The discussion on low-tier 6G device for scalable design would be more urgent for the 6GR framework design.
  How UE feature/capabilities are defined/reported would require more discussion as service, marketing and testing aspect would be related, although it could be started from the discussion on eMBB, URLLC, mMTC like framework of 5G and adding specifically for 6G including FWA.
  It means the conclusion that "the low-tier 6G device for scalable design" itself is defined as specific UE feature/capability/category are not concluded for now.
    mMTC can require 20 to 30 dB coverage extension but "low-tier 6G device for scalable design" may not have such capability.
    Redcap in NR represent only RAN layer meaning as it is the abbreviation of "reduced capability". We think "the low-tier 6G device for scalable design" can take similar approach of RAN layer meaning.
  For "the low-tier 6G device for scalable design", focus on "basic function" definition for now.

## Slide 4: Basic function
Basic function for "the low-tier 6G device for scalable design" is the minimum set of functions for scalable design for 6GR.
  If certain functions are not scalable, separate design is possible but it is not "basic function".
    Ambient IoT, eMTC and NB-IoT are such design.
  Following properties are important for basic function for "the low-tier 6G device for scalable design". This is similar to Redcap properties.
    Common synchronization signal design among device types
    Common system information design among device types
    Common DL and UL control channel design among device types
    Common paging and random access procedure
    Common FEC scheme
    Common target coverage of the order of 8 to 10 dB extension or 154 dB MCL
    Allow sufficient network energy saving gain
  If "the low-tier 6G device for scalable design" is only used for mMTC, to mandate 20 to 30 dB further extension can be separately discussed.

## Slide 5: The minimum spectrum allocation
Both to support 3 to 5 MHz spectrum allocation and to support the efficient design for sufficiently wide system band are required.
  For DL, one-shot reception property is important for synchronization signal design for UE and network energy saving.
    When system band is narrow like 3 to 5MHz, base station power can be concentrated on such bandwidth. Higher PSD can be expected than wider band operation, which makes one-shot reception more easily.
    When system band is wide, base station power needs to be sent over wide band. In order to achieve one-shot reception, wider bandwidth of synchronization signal would be required for more power. Wider bandwidth of synchronization signal is also useful for frequency diversity.
  For UL, to limit 3MHz bandwidth for RF front end complexity for basic feature UE would not make system performance degradation so much. Hopping over the bandwidth also can be considered. Therefore, the bandwidth for DL and UL should be separately discussed.
  If the operator has multiple of fragmented spectrums, spectrum aggregation/segment/virtualized cell should be considered, which would minimize the system overhead.

## Slide 6: Proposals
The discussion on low-tier 6G device for scalable design and how UE feature/capabilities is defined/reported should be separated.
  RAN1 should discuss basic function for "the low-tier 6G device for scalable design"
  RAN plenary should discuss how UE feature/capabilities is defined/reported
Following properties are requirement for basic function for "the low-tier 6G device for scalable design".
  Common synchronization signal design among device types
  Common system information design among device types
  Common DL and UL control channel design among device types
  Common paging and random access procedure
  Common FEC scheme
  Common target coverage of 8 to 10 dB extension from NR
  Allow sufficient network energy saving gain
Both to support 3 to 5 MHz spectrum allocation and to support the efficient design for sufficiently wide system band are required.

## Slide 7: References
6GWS-250004, Nokia's view on 6G Radio and RAN, Nokia Corporation
6GWS-250036, Vision and technologies for 6G radio, Samsung
6GWS-250052, Vision & priorities for 6G radio technology, NTT DOCOMO, INC.
6GWS-250061, Lenovo views on 6G RAN Vision and Priorities, Lenovo
6GWS-250063, Spreadtrum vision & priorities for 6G radio technology, Spreadtrum, UNISOC
6GWS-250068, Qualcomm's 6G Radio Technology vision and priorities, Qualcomm
6GWS-250071, MediaTek Views on 6G Day-1 Radio Aspects, MediaTek Inc.
6GWS-250078, AT&T's Vision & Priorities for 6G RAN, AT&T
6GWS-250091, Telstra’s Vision and Priorities for 6G RAN, Telstra Limited
6GWS-250102, Intel views on 6G RAN and Radio Interface, Intel
6GWS-250111, Apple’s Vision and Priorities for 6G RAN, Apple Inc
6GWS-250127, Vision and priorities for 6G RAN, CATT
R1-2506116, Overview of 6G air interface, Sony, RAN WG1 #122