## Slide 1: Views on RAN4 Rel-20 Demodulation performance evolution WI
China Telecom
2025.09
3GPP TSG RAN Meeting #109
Beijing, China, Sep 15-18, 2025
RP-252536

## Slide 2: Background in RAN#108
Normative work on SCM based requirements for SU-MIMO in FR1 The exact scope also depends on the conclusion of R19 study Study on SCM for MU-MIMO Performance requirements for 6Rx UE with interference Up to 4 MIMO layers for the target cell is considered No RAN1/2 impact is expected Target 0.5 TU allocation from Q1’26 and 1 TU from Q2’26.
In the RAN#108 meeting, the high-level scope (as shown below) for RAN4 Rel-20 WI on Demodulation enhancement is agreed, while the exact scope and WID draft will be discussed and decided in RAN#109.
  As agreed in RAN#108, there will be 3 objectives (2 normative work + 1 study work) in the Rel-20 Demod WI, with no more than 1TU for each meeting.
  Observation 1: It is very challenge to discuss the 3 objectives in parallel in each meeting.

## Slide 3: Considerations for the planning of objectives
  Proposal 1: It is proposed to firstly start the normative work (6Rx UE with interference, SCM requirements for SU-MIMO). The study work (SCM for MU-MIMO) can be started after the new SCM requirements are stable.
  With the above proposal, considering there are totally 11 meetings scheduled for RAN4 Rel-20 (from RAN4#116b 25Q4 to RAN4#123 27Q2), it is proposed to organize the SCM work in 2 phases:
  Phase I: SCM based requirement definition for SU-MIMO
  Phase II: SCM study for MU-MIMO
  Note: Phase I is targeted to be concluded in [5] meetings and leave [6] meetings for the Phase II study
  For SCM normative work, considering operators’ strong request, it is proposed to start this work at the beginning of the Rel-20 demodulation WI.
  The Rel-19 SCM study has included comprehensive combinations including channel model, parameters and cases. In Rel-20, there are many test assumptions pending decision (e.g., selection among the 5 candidate channel models, …).
  For SCM MU-MIMO study, its workload can be much reduced by inheriting the progress from the SU-MIMO normative work, which not only has little impact to the study progress, but also avoid overlapping discussion and save efforts of the group.
  For 6Rx UE with interference, RAN4 already has experience for similar requirements for 2/4/8 Rx UEs. Its workload should be very controllable to start this work in parallel with the SCM normative work.

## Slide 4: Proposed detailed objectives
    Define the following performance requirements for 6Rx TDD UEs with MMSE-IRC receiver:
  PDSCH demodulation requirements with inter-cell and with intra-cell inter-user interference
  CQI reporting requirements with inter-cell interference
  The existing interference model for 2/4/8 Rx UE is a start point
  Define release independent rules if feasible.
    Spatial channel modeling (SCM)
  Phase I: Define new SCM based UE performance requirements for FR1 SU-MIMO (Starts from RAN4#116bis)
    Channel model are selected from the Rel-19 RAN4 study in TR38.753.
    Simulation parameters agreed in the Rel-19 RAN4 study in TR38.753 is a starting point.
    The following requirements will be defined:
      Define PDSCH demodulation requirements for 8T8R 8 layer
      [PMI reporting test case based on SCM with Type I/eType II] (To be discussed during RAN#109)
  Phase II: Study the feasibility of SCM based performance requirements under DL MU-MIMO scenario for FR1 (Starts from [RAN4#120])
    Both baseline MMSE-IRC [and advanced R-ML] receivers can be considered in the study
    Both Type I [and eType II] codebook can be considered in the study.

## Slide 5: Impacted TS/TR
Impacted existing TS/TR |  |  | 
TS/TR No. | Description of change | Target completion plenary# | Remarks
TS38.101-4 | NR; User Equipment (UE) radio transmission and reception; Part 4: Performance requirements | TSG-RAN #116 | Performance part
TS38.307 | NR; Requirements on User Equipments (UEs) supporting a release-independent frequency band | TSG-RAN #116 | Performance part
TR38.753 | Study on spatial channel model for demodulation performance requirements for NR | TSG-RAN #116 | Capture the study outcome for SCM MU-MIMO

## Slide 6: Thanks!