## Slide 1: Sony’s view on RAN4 Rel-20 5G-A package
Sony
3GPP TSG RAN Meeting #109
Beijing, China, September 15-18, 2025
RP‑252585
Agenda item:9.1.4.7

## Slide 2: Background
WF on RAN4 Rel-20 5GA work package was approved in RAN#108 (RP-251879), where potential objectives and topics of RAN4 led Rel-20 5GA work items are identified and it is expected those topics will be further discussed and consolidated in RAN#109
The RAN4 led Rel-20 5G-A work needs to be carefully planned with consideration of the impact from other WGs as well as the maintenance work. Therefore, it is proposed that:
  Rel-20 5G-A enhancements shall focus on the missing features for 5G NR to enable the new market segment and deployment.
  Enhancements requiring extensive studies, causing major changes in implementations, should be considered as part of 6G track instead of 5G-A track.
Based on the principles above, we propose the topics that can be considered in Rel-20 RAN4 5G-A working package.

## Slide 3: UE RF centric evolution
WF in RAN#108
The high-level scope of the WI on UE RF centric evolution (the exact scope and WID draft will be discussed and decided in RAN#109):
FR1 HPUE enhancement
  Further consider/discuss until RAN#109 on the detailed scope
  This work is to focus on the TN application
6MHz channel bandwidth
  It can be prioritized to FDD band <1GHz
Study and, if feasible, reduce UE MPR values with the relaxed Tx EVM requirement for 5G NR higher modulation orders, i.e., 64QAM , 256QAM
  BS demod scope is included.
  The study is performed based on non-AI-based approach at BS receiver as baseline and without RAN1 impact
    The details for study is to be discussed until RAN#109
  This work will be started in Q1’26. If the similar scope (The examples include the enhancements enabled by BS advanced receiver and UE Tx signal modifications. It is noted that referring to these examples in this WF should not be deemed as taking these examples as the baseline or starting point in 6G study) is agreed by RAN4 to be studied in 6G, it will be removed from 5G-A package. In this case, it is possible that 6G related conclusion can be applied to 5G.
No RAN1/2 scope is expected
Target 0.5 RF TU in Q4’25 and 1.25 TU (0.75 RF and [0.5] Demod for EVM relaxation and 6MHz) from Q1’26.
Proposed topics
Considering the needs from commercial deployments, it is proposed to focus on the FR1 HPUE enhancement and also support 6MHz CBW in the Rel-20 UE RF centric topic.
FR1 HPUE enhancement for single carrier
  Single Tx for PC1.5
  Focus on FWA devices.
Define and specify the 6MHz channel bandwidth for FDD band < 1 GHz
For EVM relaxation for MPR reduction, since the topic requires extensive study and likely to be overlapped with 6G discussion, RAN4 may consider to focuses on EVM relaxation study under 6G track, and applied it to 5G if consensus can be reached.

## Slide 4: RRM enhancements
WF in RAN#108
Proposed topics
Based on the WF, the (e)Redcap enhancement is categorized under RRM topic. The most critical and urgent job is to support 3MHz CBW and to achieve the further complexity reduction to (e)Redcap, which can enable the 5G NR use cases on low-end IoT market, and bridge the transition period between 4G IoTs to 6G IoTs
(e)Redcap UE enhancement*
  Support 3MHz CBW for (e)Redcap device, including both TN and NTN.
    RAN4 study and specify 3MHz-only (e)Redcap device in Rel-20 to enable further complexity reduction
  Specify relaxed RLM and BFD for (e)Redcap devices.
* See RP‑252583 for detailed proposals
The high-level scope for WI on RRM enhancement (the exact scope and WID draft will be discussed and decided in RAN#109):
(e)RedCap UE enhancement
  RLM/BFD relaxation based on the conclusions of R17 UE power saving WI
  Less than 5MHz for (e)RedCap, including both 1Rx and 2Rx, based on the conclusions of R18 LT5 WI
    This also include example bands, UE RF scope including potential complexity reduction, UE demod
Fast SCell activation
  Further discussion on the possible down scoping in RAN#109 based on the following two objectives
    SCell activation delay reduction for intra-band co-located CA, including SSB-less cases and enhanced CSI reporting
      Interested companies can propose to extend this work to inter-band case in the check-point in June 2026.
    A-TRS/TRS based unknown SCell activation including both inter-band CA and intra-band non-contiguous CA
  Consider simplification of solution to maintain reasonable work scope in consideration of the TU allocation
No RAN1/2 scope is expected
Target 0.5 TU (0.25RD and 0.25RF) in Q4’25 and 1 TU allocation (0.75RD,0.25RF) from Q2’26

## Slide 5: NTN enhancements
WF in RAN#108
Proposed topics
High level scope for WI on NTN enhancement (the exact scope and WID draft will be discussed and decided in RAN#109):
NTN HPUE
  Finish remaining PC1.5 (~29 dBm) work for hand-held devices for both NR NTN and IoT NTN (several studies and discussions already done in R19)
    NR NTN with 2TX and/or FFS 1TX
NTN HD-FDD VSAT for Ka/Ku bands
  RAN4 will start with HD-FDD mobile VSAT with small antennas (e.g 20x20cm).
  Once the mobile VSAT with small antennas work is done,
    NTN HD-FDD for fixed VSAT and the mobile VSAT with large/normal antenna will be discussed, including how the agreements for the mobile VSAT with small antenna can be leveraged as applicable
  RAN1/2 impact is expected and will be further discussed in RAN#109
    Leverage RedCap over NTN HD-FDD solution to NTN as applicable.
NTN DL CA
  Intra-SAN CA limited to DL intra-band contiguous and non-contiguous with 2CC
    Example bands will be further decided within L/S-band and Ku/Ka-band as example bands
    Depending on the available band combinations, interested companies can propose to extend this work to intra-band with more than 2CC in the check-point in June 2026
  RAN1/2 impact is expected and will be further discussed in RAN#109
Spec clean-up/fixing: Missing Channel BW Common Core and Perf Requirements
  30MHz (DL/UL), 40MHz (priority DL), 25MHz with PC3
    Take one example band with minimum work with PC3
    The rest cases can be considered as part of spectrum work once the requirements on the example band is completed
Target 1TU in Q4’25 and 1.5 TU allocation including RF, RRM and demod from Q1’26
For NTN Topics, there are still many proposals on the table right now based on the agreed WF and down scoping is necessary. In our view, the following objectives are the most meaningful for commercial deployment, and should be prioritized.
NTN HD-FDD VSAT in FR2-NTN to enable reduced cost and size for VSAT.
Specifying the missing BWs in NR NTN in FR1-NTN: 25MHz, 30MHz, 35MHz and 40MHz.
Although we see no urgent commercial demand, HPUE with PC1.5 can be considered if TU allows, to enable the HPUE based on existing PA architectures (e.g., 2Tx for NR NTN) in FR1-NTN

## Slide 6: Other areas
Demodulation performance evolution
For demod, it is proposed to focus on the normative work based on the outcome of the SI on SCM from Rel-19. Further study on SCM in Rel-20 can be deferred to 6G track.
Focus on normative work on SCM based requirements for SU-MIMO in FR1
Study on MU-MIMO can be deferred to 6G track
UE OTA enhancement
For UE OTA enhancement, we think the scope defined in the WF is proper and the following item is proposed accordingly:
Study and specify test method to support NTN VSAT
The performance requirements of TRP/TIS and MIMO OTA of handheld UE in bands n7,n20, n79
Cross RF and Baseband
Currently, 4 objectives are proposed under “cross RF and baseband” areas. In our view, the TU budget may only be able to accommodate 2 out of the 4 objects in Rel-20 5GA track. Therefore, it is proposed to focus on
Extension of LBCA: focus on the dual DL solution in Rel-20.
UAV UE with antenna array with up to 33dBm maximum output power on TDD spectrum