## Slide 1
Discussion on Rel-20 AI/ML for Air Interface
3GPP TSG RAN Meeting #110
Baltimore, US, Dec 8-11, 2025
Agenda: 9.3.1.3
Source: ZTE Corporation, Sanechips
RP-253200

## Slide 2: Background 1/2
Inter-vendor training collaboration
  In RAN#108 meeting, a new work item on AI/ML for NR air interface enhancements was approved with the following objectives.
  The scope includes specification support for three inter-vendor training collaboration options, i.e., 1) Direction A sub-option 4-1 with standardized dataset format/content plus dataset exchange, 2) Direction A sub-option 3a-1 with standardized encoder model structure plus parameter exchange, and 3) Direction C with standardized reference model.
  There are two check points in RAN#110 upon SA WG and RAN4 feedback, which are related to signaling feasibility for dataset/parameter sharing and RAN4 testing feasibility, respectively.
  Since RAN4 testing feasibility is not determined, RAN1 only initiated the normative work for Direction A sub-option 4-1 starting from RAN1#122 meeting. Discussions for Direction A sub-option 3a-1 and Direction C remain pending.
Inter-vendor training collaboration for two-sided AI/ML models Fully defined/specified reference model (“Direction C”) with RAN1 scalability study outcome taken into account [RAN4/RAN1] – check-point in RAN#110 upon RAN4 feedback Specification of standardized encoder model structure plus parameter exchange (“Direction A, sub-option 3a-1” without target CSI sharing) leveraging defined/reference model of “Direction C” and taking RAN1 scalability study outcome into account [RAN4/RAN1/RAN2/RAN3] – check-point in RAN#110 upon SA WG feedback Specification of standardized dataset format/content plus dataset exchange (“Direction A, sub-option 4-1”) [RAN1/RAN2/RAN3/RAN4] – check-point in RAN#110 upon SA WG feedback

## Slide 3: Background 2/2
UE-side data collection
  Another WI objective for AI/ML phase 2 is about the UE side data collection as shown below.
    Data collection [RAN2]:
    - Further study and specify if deemed necessary, standards-based UE data collection at least for UE-side model training in close collaboration with SA WGs and taking into account the agreed principles during the Rel-19 study – check-point in RAN#110 based on SA WG feedback and SA2 study on data collection
  One LS from SA2 has been received in S2-2510958, in which, SA2 claims the study on data collection with Option 2 UP solution have been finished from SA2 perspective, the study report have been filed in the TR 23.700 and require RAN/RAN2 to determine whether option 2 UP is selected or not.
    As feedback to request in RP-243316, SA2 would like to provide information on the outcome of the related SA2 study FS_AIML_CN_Ph2 (SP-250810).
    SA2 has reached interim agreements with remaining open issues on how to support the transfer of standardized data over UP for UE data collection for UE-side model training as described in clauses 7.1.1 and 7.2.1 of TR 23.700-04 v1.2.0.
    Additionally, SA2 would like to ask for RAN/RAN2 to provide feedback on whether Option 2 UP is selected.

## Slide 4: Discussion 1/3
Inter-vendor training collaboration
  Study status from working groups
  The first check-point in RAN#110 pertains to SA WG feedback on the feasibility of dataset/model parameter exchange for Direction A sub-option 3a-1 and sub-option 4-1.
    In S5-254846, SA5 has confirmed that non-OTA approaches involving OAM is feasible for dataset/model parameter exchange subject to further evaluation.
    SA2 hasn't provided reply on this topic in Rel-20 yet.
  The second check-point in RAN#110 pertains to RAN4 feedback on the feasibility of fully defined/specified reference model with RAN1 scalability study outcome taken into account.
    In R4-2522434, RAN4 has confirmed that option 3 (i.e., Direction C in RAN1) is feasible for RAN4 to complete. RAN4 will take into account the conclusions in RAN1 on scalability in order to create a scalable model.
    Additionally, RAN4 has also confirmed that Direction A sub-option 3a-1 is feasible for RAN4 to complete from reference encoder perspective.
    RAN4 agreed the detailed steps to develop the model.

## Slide 5: Discussion 2/3
Inter-vendor training collaboration
  Discussion
  As RAN4 has studied the interoperability of two-sided model and concluded that fully specified test decoder and reference encoder are feasible, RAN1 can now proceed with the normative work for Direction A sub-option 3a-1 and Direction C.
    For Direction C, consider the reference encoder and decoder (structure + parameters) to be the same as RAN4 reference encoder and RAN4 test decoder, respectively.
    For Direction A sub-option 3a-1, consider the RAN4 reference encoder for the standardized encoder model structure.
    For Direction A sub-option 3a-1, leverage the agreements reached for Direction A sub-option 4-1 and discuss the specification impacts at least including model parameter content/format and additional information sharing.
  Proposal
  Proceed with the normative work for Direction A sub-option 3a-1 and Direction C in RAN1 for Rel-20 5G-A CSI feedback enhancements using two-sided model.
    Leverage the agreements reached for Direction A sub-option 4-1 and discuss the specification impacts at least including model parameter content/format and additional information sharing.

## Slide 6: Discussion 3/3
UE-side data collection
  Discussion
  In the subcaluse 7.2 in TR 23.700, there are 20 issues in editor notes waiting for being resolved in SA2 if option 2 UP is selected, and for dealing with those issues, more collaboration between RAN and SA is needed, which is really time consuming from both RAN and SA perspective for 5GA topic.
  Besides, in Rel-19, RAN2 have introduced UE side data collection request mechanism in order for UE to request NW with the UE side data collection configuration, UE side data collection request plus the option 1a (i.e. 3GPP transparent data collection solution) has been workable for UE to collecte the data, and transfer the collected data to the UE server.
  Proposal
  Option 2 UP solution for UE side data collection is not supported in 5GA.

## Slide 7: Summary
Proposals
  Proposal 1: Proceed with the normative work for Direction A sub-option 3a-1 and Direction C in RAN1 for Rel-20 5G-A CSI feedback enhancements using two-sided model.
    Leverage the agreements reached for Direction A sub-option 4-1 and discuss the specification impacts at least including model parameter content/format and additional information sharing.
  Proposal 2: Option 2 UP solution for UE side data collection is not supported in 5GA.

## Slide 8: Thank You！