## Slide 1: Proposed Solutions to Support Efficient MANET Multicast over PC5 Groupcast
S2-2510222
NIST, KPN N.V., FirstNet, AT&T

## Slide 2: Introduction
Objective of TEI20_5G_ProSe_Ph4-ARC (SP-250839):
  The following aspect will be considered:
  WT-1: Enhance ProSe to support efficient MANET multicast for Layer-3 IP Type UE-to-UE multi-hop Relay.
    Enhance ProSe to support multicast transmission of MANET HELLO and TC messages.
    Enhance ProSe to support MANET multicast traffic delivery.
  NOTE 1: This WT is subject to coordination with RAN WG2 to determine RAN impact.
  NOTE 2: Security aspects will be handled by SA WG3.
  NOTE 3: Existing MANET protocols (e.g. Simplified Multicast Forwarding as defined in RFC 6621) will be used for multicast IP traffic routing. The scope of this work will be limited to the mapping between the group ID, IP addresses, and Layer-2 Link IDs.
Anticipated WGs to be impacted: SA2, RAN2, SA3, CT1
  There are dependencies with RAN WG2 and SA WG3 for bearer level security protection.
Relevant Tdocs: S2-2510227 (SA2 CR on TS 23.304), S2-2510223 (LS to RAN2 and SA3, cc CT1)
S2-2510222

## Slide 3: Enhancement 1 -- for MANET HELLO and TC msgs
Enhance ProSe to support the multicast transmission of MANET HELLO and TC messages:
Proposed solution: MANET routing messages (i.e., HELLO and TC messages) are mapping to IP multicast address, and then mapping to L2 groupcast mode bearer & Dst L2 ID:
  MANET HELLO and TC messages are assigned to the IP multicast address defined by IETF:
    (RFC 5494) The address for LL-MANET-Routers is 224.0.0.109 for IPv4, and FF02:0:0:0:0:0:0:6D for IPv6;
  Sender: If the “PC5 groupcast for MANET multicast" option is configured for the RSC,
    Mandate that the “LL-MANET_Routers” IP multicast address to be mapped to a L2 groupcast mode bearer;
    The Relay node always use the corresponding groupcast bearer for the transmission of MANET HELLO and TC messages;
    The Dst L2 ID of the groupcast bearer needs to be configured according to the RSC; -- to be defined by CT1, e.g. derived from the RSC using a HASH function
  Receiver: L2 checks whether the pkt is from a node (based on src L2 ID) with which a L2 link is established already.
    If yes, pass the pkt to upper layer, finally to IP layer to update the MANET routing table.
    If no, discard the pkt, otherwise the MANET routing table might include a path to a node with no established L2 link..
    The Src L2 ID needs to be verifiable using security keys associated with the L2 ID. – to be specified by SA3 and RAN2 PDCP
S2-2510222

## Slide 4: Enhancement 2 -- for MANET Multicast Traffic
Enhance ProSe to support MANET multicast traffic delivery:
Proposed solution: IP multicast traffic (e.g., MCPTT off-network mode group call) are mapping to IP multicast address, and then mapping to L2 groupcast mode bearer & Dst L2 ID:
  Specify/provision IP multicast address(es) for the traffic that requires multicast delivery over the MANET cloud;
  Sender: If the “PC5 groupcast for MANET multicast" option is configured for the RSC,
    Mandate that the traffic for IP multicast address(es) to be mapped to L2 groupcast mode bearers respectively;
    The corresponding Dst L2 ID of the groupcast bearer needs to be configured according to the RSC and IP multicast address; -- to be defined by CT1, e.g., derived from RSC and IP multicast address using a HASH function
  Receiver: L2 checks whether the pkt is from a node (based on src L2 ID) with which a L2 link is established already.
    If yes, pass the pkt to upper layer, finally to IP layer to be handled by IP multicast protocol (e.g. SMF);
    If no, discard the pkt.
    Security will be checked at PDCP layer, before forwarding the packet to the IP layer; – to be specified by SA3 and RAN2 PDCP
  All relay nodes shall use the same multicast protocol at IP layer, e.g., SMF.
S2-2510222

## Slide 5: Summary of Proposed Changes in S2-2510227
Modified Clause (TS 23.304) | Purpose
2 | References
5.1.3.1 | IP multicast address for HELLO and TC msgs
5.1.5.1a | Indication of “PC5 groupcast for MANET multicast” option and the pointer to configuration parameters
5.14.3.2 | The same multicast protocol for all nodes in one RSC Map MANET multicast to PC5 groupcast @ sender; check L2 link status @ receiver Derivation of Layer 2 ID NOTE on security protection
6.4.3.10.1 | Ensure the Relay node always use the corresponding groupcast bearer for the transmission of MANET HELLO and TC messages, i.e., a single interface
Both enhancements can be combined into one CR given the similarity in proposed solutions.
S2-2510222
Notes:     (modification of the interface language in 6.4.3.10.1)
    mandate that there is a single MANET interface for all established layer-2 links, instead of the current “each layer-2 link is treated as a MANET interface”;
      Why ?
        RFC7181 (OLSRv2) section 16.2: “…… Complete TC messages are generated and transmitted periodically on all OLSRv2 interfaces,……”
        RFC6130 (NHDP) section 4.3.1: “HELLO messages are generated by a router for each of its MANET interfaces……”