## Slide 1: Discussion on reducing reporting load from UPF
SA2#172 FS_AIML_CN_Ph2
NTT DOCOMO

## Slide 2: Problem statement
The following topic is under further consideration in the TR:
  How to reduce the reporting load of input data sources and control plane signalling overhead? For example by configuring appropriate Analytics Filter Information, combining notification to NWDAF at UPF for multiple events, instructions from NWDAF to UPF for pre-processing in the UPF, etc.
There are several proposals from companies (please see pages 3 and 4.)

## Slide 3: Company's views from interim conclusion paper (1/2)
TDoc | Company | Statement
S2-2509986 | China Mobile | - The reporting load of input data sources and control plane signaling overhead may be reduced via configuring appropriate Analytics Filter Information, combining notification to NWDAF at UPF for multiple events, instructions from NWDAF to UPF for pre-processing in the UPF, etc.
S2-2510061 | Nokia | - Filters can target special traffic patterns identified by UPF internal logic to be identified by a UP traffic pattern ID or application ID known to analytics consumer, NWDAF and UPF , special UEs or UE group IDs, special data sources, and/or provide thresholds for a minimum volume of an observer traffic pattern, or for a minimum increase rate in the observation of an observer traffic pattern.
S2-2510204 | Ericsson | - To reduce reporting load, the existing Event Reporting Instructions can be used to provide a threshold to UPF, other pre-processing instructions can be requested by NWDAF at UPF, to aggregate or to provide statistics on data measurements with different level of granularity such as per PDU Session. Other actions defined in 29.564 applies.

## Slide 4: Company's views from interim conclusion paper (2/2)
TDoc | Company | Statement
S2-2510295 | Samsung | - the analytics consumer may include the Analytics Filter Information (as described in clause 6.1.3 of TS 23.288 [5]) for input data filtering to NWDAF in analytics request. Then the NWDAF may include the necessary information in the Analytics Filter Information. - UPF may combine the measurement data related to multiple event ID(s) into one notify message and send a combined notification to NWDAF. - SMF may instruct rules to UPF for pre-processing data in UPF before reporting data to NWDAF.
S2-2510314 | NTT DOCOMO | - The NWDAF may include instruction information in the subscription request to direct the UPF to perform preprocessing, including limiting the volume of the data set to be sent, sampling and statistical processing, skipping or bundling reports, compressing or encoding data, applying an ML model by the UPF on the raw data and providing the inference result to the NWDAF.

## Slide 5: Potential Way Forward
Solution | Proposing Companies | Comment | Potential Way Forward?
A) Analytics filter | China Mobile (Nokia) Samsung | 1- Existing mechanism 2- Filters for the new Analytic(s) should be specified 3- Behavior of NWDAF to reduce load on UPF based on the filter should be specified (Nokia’s proposal: application ID, special UEs or UE group IDs, special data sources) | Conclude the general principle Leave 2 and 3 to the normative phase (+ clarification Note)
B) Preprocessing Instructions | China Mobile Ericsson Samsung NTT DOCOMO | 1- Majority view 2- List of instructions should be specified (Ericsson: aggregate, statistics) (DCM: sampling, statistic, compression,…) | Conclude the general principle Leave 2 to the normative phase (+ some examples)

## Slide 6: Potential Way Forward
Solution | Proposing Companies | Comment | Potential Way Forward?
C) Mechanism in TS 29.564 | Ericsson (Nokia) | 1- Existing mechanism 2- Applicable mechanism? (Nokia: thresholds for a minimum volume) | Conclude the general principle Minor normative work (reference to TS 29.564 mechanisms)
D) Special traffic pattern | Nokia | Nokia: “Traffic pattern ID known to analytics consumer, NWDAF and UPF” If the pattern is not standardized  left to implementation  interoperability issue  Concern from some companies If the pattern is going to be standardized  how to make a list of traffic pattern | Needs further discussion and comments from other companies to reach a consensus Don’t any conclude in study phase?