## Slide 1: R20 AIoT key issue 1 conclusion way forward
Huawei, OPPO (rapportures)

## Slide 2
Key issue 1 progress after SA2#172, Oct 2025
Current situation
Key issue 1 has already used the 0.5 TU planned in the SID, and not been completed yet.
Guidance from SA2 Chair
For this, and the other studies that are due to complete in November we (SA2) will need to discuss during the November work planning sessions how to handle the situation if parts of a study are not complete.
Down-scoping is one option. Continuing some study work in February is another option, but requires agreement in SA2 and an understanding of where the additional TU(s) will come from (from the normative budget for that item, or from the buffer, for example).
Allocating additional time for 5G Advanced studies in November over and above the budget will be challenging

## Slide 3
Overall consideration of key issue 1 conclusion in future meeting
General principles
Very limited time will be allocated to discuss the remaining issues, i.e. editor’s notes in the TR
For each editor’s note, conclusion options are listed (see next slides).
If consensus cannot be reached, the feature will be dropped
Nov meeting workplan
Rapporteurs provides the conclusion options before the meeting and collects the feedback from all companies
Use the drafting session to discuss companies’ feedback and decide the conclusion way forward
Endorse the conclusion way forward for Feb meeting
Feb meeting workplan
Finalize key issue 1 conclusion within very limited time, based on the endorsement in November meeting

## Slide 4
Handling of editor’s notes
Conclusion aspect | Editor’s note | Open issue(s) description
UE reader authorization and revocation | Whether and what additional subscription information for the UE Reader is needed is FFS. | Two more subscription data for further discussion (other proposals were dropped): Validity information: valid time duration and area that allowed for UE to act as an AIoT Reader AF ID information indicating that the UE reader belongs to the designated AF
Conclusion options:
Option 1: not to support additional subscription information
>> LGE
Option 2: agree “Validity information”: valid time duration and area that allowed for UE to act as an AIoT Reader
Option 3: agree “AF ID information” indicating that the UE reader belongs to the designated AF
Rapporteurs’ proposal: option 3
Endorsement:

## Slide 5
Conclusion aspect | Editor’s note | Open issue(s) description
UE reader authorization and revocation | Whether to inform the UE about the authorization information is FFS. | Two options have been discussed Option 1: YES. UE need to got authorization result, similar like other legacy features e.g., ProSe, V2X Option 2: NO. UE is authorized or not is controlled by whether it can get radio resource from RAN. RAN will decide based on authorization indication from CN, together with UE reader radio capability, available radio resource in the serving cell.
Conclusion options:
Option 1: yes. UE needs to be informed of the authorization information, i.e. authorized indication.
Option 2: no. UE does NOT need to be informed of the authorization information
>> LGE
Handling of editor’s notes
Rapporteurs’ proposal: option 1
Endorsement:

## Slide 6
Conclusion aspect | Editor’s note | Open issue(s) description
UE reader authorization and revocation | Whether UE reader capability is provided to AMF is FFS. | Two UE reader capability have been discussed: UE MM capability, provided from UE to AMF via NAS. AMF based on UE subscription information in the UDM, and the UE MM capability, to authorize or revoke the UE as reader UE radio capability, provided from UE to RAN, and RAN provides it to AMF. AMF based on the UE radio capability, and available radio resource in the UE serving cell, to authorize or revoke the UE as reader NOTE: UE radio capability can be left to RAN WG to decide
Conclusion options:
Option 1:agree “UE MM capability”, indicating UE is capable to operate as AIoT reader, provided by UE to AMF
Option 2: agree “UE radio capability”, indicating the supported frequency bands used to AIoT operation, provided by RAN to AMF
>> LGE
Handling of editor’s notes
Rapporteurs’ proposal: option 1
Endorsement:

## Slide 7
Conclusion aspect | Editor’s note | Open issue(s) description
UE reader selection | How to select UE reader(s) based on the AF provided area information is FFS | SA2#171 discussed two UE reader types: (1) fixed UE reader (2) mobile UE reader. In case that AF provided area information, the open issue is: Whether and how to select the mobile UE reader?
Conclusion options:
Option 1: only fixed UE reader will be selected
Option 2: both fixed and mobile UE reader selected
>> LGE
Rapporteurs’ proposal: option 1
Handling of editor’s notes
Endorsement:

## Slide 8
Conclusion aspect | Editor’s note | Open issue(s) description
AIOTF Discovery and Selection for UE reader ID | How to discover and select AIOTF when AF provides UE reader ID is FFS | When AF provides the UE reader ID e.g. GPSI to the NEF, how the NEF selects the AIOTF based on the AF input? Due to the lack of time, the solution are not discussed in the study phase. From all the proposed solutions, two candidate options : Query UDM Query NRF
Conclusion options:
Option 1: NEF query the UDM
>> LGE
Option 2: NEF query the NRF
Handling of editor’s notes
Rapporteurs’ proposal: option 1
Endorsement:

## Slide 9
Conclusion aspect | Editor’s note | Open issue(s) description
UE reader ID allocation | Whether and how to allocate the UE reader ID | Open issue 1: what identifier is used to identify UE reader by UE, RAN, and CN NF? Option 1: existing UE identifier, like NG-AP ID or GPSI; Option 2: new identifier (AIoT specific UE ID) Open issue 2: how to allocate the UE reader ID? (Dependency on UE reader selection) Option 1: allocated by AIOTF Option 2: allocated by AMF
Open issue 1, conclusion options:
Option 1: existing UE identifier
Option 2: new UE identifier
>> LGE
Open issue 2, conclusion options:
Option 1: allocated by AIOTF
Option 2: allocated by AMF
>> LGE
Handling of editor’s notes
Rapporteurs’ proposal: UE NGAP ID is used as UE reader ID
Endorsement:

## Slide 10
Summary of endorsement for SA2#173 meeting
Will be provided after the drafting session