## Slide 1
Voice Over LTE
Dan Warren, Director of Technology, GSMA
PCG24_10
Agenda 10

## Slide 2: The Voice challenge for LTE
  LTE is an all-IP mobile network
  No support for ‘traditional’ CS domain voice
  New Voice and SMS solutions required
    CSFB, VoLGA, ‘One Voice’
The risk – industry fragmentation
  Poor customer experience
  No common implementation
  Economies of scale are lost
The Reality – the industry knows where it is going
  ‘OneVoice’ adoption as GSMA Voice over LTE (VoLTE)
  Massive backing from operator and vendor community.
  ‘Migratory solutions’ filling the gap between LTE launch and IMS deployment for some operators.
Notes:   The Voice challenge for LTE
  LTE is an all-IP mobile network
  LTE does not support ‘traditional’ CS domain voice
  New Voice and SMS delivery are needed - Different potential solutions proposed
    CSFB, VoLGA, ‘One Voice’
The risk – industry fragmentation
  No common implementation impacts interoperability and roaming
  Economies of scale are lost - higher costs and reduced consumer choice

## Slide 3: ‘Migratory’ Solutions
Migratory solutions fill the gap between existing CS voice and the Target Solution.
  Short window of opportunity for deployment
  Not required by all operators (some will move directly to the Target Solution).
Once in a network, Migratory solutions may prove difficult to remove
  Handset impact => need to support handsets with network functionality even once Target Solution is deployed.
More than one Migratory solution defined
  CS Fallback (CSFB) in 3GPP, VoLGA defined by VoLGA Forum
  Industry fragmentation leads to non-optimal economies of scale and breakage of roaming

## Slide 4: Target solution - GSMA VoLTE
GSMA VoLTE Task Force
  Single ‘target’ solution – IMS-based
  Shorten the ‘window’ for Migratory solutions
    For as many operators as possible, try and avoid the need for any migratory solution at all
VoLTE Task Force and One Voice collaboration
  VoLTE adopted One Voice Profile of IMS SIP, 8th January 2010
  GSMA VoLTE initiative announced 15th February 2010
One Voice closed, all future work through VoLTE initiative.
Notes: GSMA Voice over LTE (VoLTE)
Created VoLTE Task Force November 2009
  Operators signed up to create a single ‘target’ solution – IMS-based
VoLTE Task Force and One Voice collaboration
  VoLTE adopted One Voice Profile of IMS SIP, 8th January 2010
  GSMA VoLTE initiative announced 15th February 2010
One Voice closed, all future work through VoLTE initiative.

## Slide 5: From today to the Target
CSFB
VoLGA
CS Voice

## Slide 6
CS Voice
What GSMA VoLTE will deliver

## Slide 7: Customer Interface
Common UNI (User Network Interface) needed
  Common implementation results in
    Roaming capability maintained
    Global scale and global ecosystem
    Lower per unit cost for vendors as a result greater amortisation of R&D
VoLTE protocol profile enables these benefits
IMS
UNI
Notes: UNI (User Network Interface)
Has to be commonly implemented by all devices and networks
differing implementations mean devices cannot be guaranteed to work across all networks
  Roaming no longer guaranteed
  Framents global scale – higher costs for vendors due to more R&D; higher cost of device to consumer due to reduced ammortisation of R&D costs.
One Voice protocol profile addresses these issues

## Slide 8: Interconnection
Interconnect Network-Network Interface (i/c NNI) creates end-to-end call connectivity
Common functionality required
Common implementation required
Need for expensive interworking functionality is removed
Work initiated in GSMA IREG Packet Working Group
Interconnect
NNI
IMS
UNI
IMS
UNI
Notes: Interconnect Network Network Interface (i/c NNI)
Essential for end-to-end call connectivity
Requires common functionality in all IMS implementations
Requires common implementation of IMS protocols as Voice calls leave one network domain headed for another
Differing i/c NNI implementation creates need for expensive interworking functionality – barrier to establishing connectivity

## Slide 9: Roaming – how it will work
VPLMN
Roaming
NNI
HPLMN
?
?
VoLTE will define functional split between Home and Visited networks
  3GPP has different options for split
  GSMA VoLTE will select one option
VoLTE will define a common Roaming NNI
VoLTE will define how emergency call for roaming is supported
All work to be executed in GSMA IREG RiLTE group
Notes: Roaming – how it will work
Define functional split between HPLMN and VPLMN
  3GPP has different options for this split – VoLTE will select one option.
Once functional split is defined, define the roaming NNI
  interface between the network a customer usually is within (their Home Network) and the network they are currently using (Visited Network)
Roaming NNI needs to be common to all networks to enable roaming service.
Also need to define emergency call service for roaming customers

## Slide 10: Completing the work
GSMA Working Groups with expertise in
  inter-network charging
  interoperability with existing systems
  handover from IMS to CS domain
  Interconnectivity models
GSMA VoLTE will work with industry bodies for overall solution – 3GPP, NGMN Alliance, IMTC, GCF, PTCRB
Notes: Technical work underway in GSMA Working Groups
Other areas to address –
inter-network charging
interoperability with existing systems,
handover from IMS to CS domain
Interconnectivity models
GSMA Working Groups host expertise in all of these areas
GSMA VoLTE will work with industry bodies for overall solution – 3GPP, NGMN Alliance, IMTC, GCF, PTCRB

## Slide 11: Industry Support

## Slide 12: Get Involved
If you are interested to learn more about GSMA VoLTE or would like to support the work…
volte@gsm.org
www.gsmworld.com/volte