## Slide 1
TSG CT WG4 Chairman
Nigel Berry (Alcatel-Lucent)
CT WG4 Status Report to TSG CT #71
3GPP TSG CT Plenary Meeting #71 CP-160010
Goteborg, Sweden; 7 – 8 March 2016 Revision of CP-16

## Slide 2: TSG CT WG4 Organisation
Meetings
  CT4 has had two meetings since the last CT plenary:
  CT4 Ad-hoc on MCPTT (Nashville), co-located with CT1;
  CT4#72 (Jeju) co-located with all CT WGs
    The Meeting Reports are in CP-160011.
  CT4 will have two meetings during the next plenary cycle:
    CT4#72bis (Ljubljana) collocated with CT1 and SA6;
    CT4#73 (Osaka) co-located with CT1, CT3 and CT6;
TSG CT WG4 officials are:
  Chairman:
    Nigel Berry (Alcatel-Lucent / ETSI)
  Vice chairs:
    Lionel Morand (Orange / ETSI)
    Yvette Koza (DT / ETSI)
  MCC support:
    John Meredith
    Kimmo Kymäläinen
Legend Blue – (re)elected since previous plenary Red – for (re)election in coming plenary period
Notes: 2

## Slide 3
TSG CT WG4 Statistics
TSG CT WG4 statistics:
  154 Change Requests agreed
  Rel-14 Work Items / Study Items approved
    2 new Work Item(s)
  Rel-? Work Items / Study Items approved
    1 endorsed Work Item(s)
  1 Rel-13 TS/TRs for approval
  1 Rel-13 TS/TRs for information and approval
  CT4 MCPTT Ad-Hoc:
    28 Registered Participants
    ~12 Participants Attending
  CT4#72:
    87 Registered Participants
    ~70 Participants Attending

## Slide 4
Rel-13 WIs Status – CT4 Led
voE_UTRAN_PPD-CT4 100%
RTCP_MUX-C4 100%
EVSoCS-CT 95% => 100%
SHARED_SubData_UPD 100%
PCSCF_RES_WLAN-CT4 100%
FS_DLoCME 40%
WebRTCH248DC 90% => 100%
FS_EPC_SIG_RACE 100%
MONTE-CT 85% => 100%
MEI_WLAN 100%
FS_SCCAS_RES 100%
SDPCN_IMS 70% => 100%
Legend Blue – new since previous plenary
Green – progressed since previous plenary
HLcom-CT 100%
GROUPE-CT 100%
ROI-CT 100%
FS_eSDU 100%
EPC_SIG_RACE 100%
DECOR-CT 90% => 100%
FS_DBPU 60% => 79%
DiaPri 70% => 100%
UTRA_LTE_iPos_enh-CT 100%

## Slide 5
Rel-13 WIs Status – CT4 Supported
UPCON-DOTCON-CT4 100%
QOSE2EMTSI-CT4 0% => 100%
ePCSCF_WLAN-CT4 100%
WSR_EPS 100%
ISAT 90% => Rel-14
eProSe-EXT-CT 80% => 100%
NBIFOM-CT 100%
AESE-CT 100%
SEW1-CT 100%
eDRX-CT 100%
MCPTT-CT 0% => 100%
Legend Blue – new since previous plenary
Green – progressed since previous plenary
eWebRTCi_CT 0% => 100%
MBMS_enh-CT 100%
CIoT-CT 0% => 65%
EASE_EC_GSM

## Slide 6: Agreed New WIs
Tdoc CP-16# | WIDS Agreed | Source | Notes
CP-160117 | WID new Rel-14 CT aspects of MTSI Extension on Multi-stream Multiparty Conferencing Media Handling | Ericsson | CT4 led Endorsed by CT1 and CT3.
CP-160118 | WID new SCC AS Restoration | China Mobile | CT4 led.

## Slide 7: Endorsed WIs
Tdoc CP-16# | WIDS Endorsed | Source | Notes
CP-160054 | WID new CT Aspects for non-IP CIoT for 2G/3G-GPRS | Orange | CT1 led Needs endorsing.

## Slide 8: Technical Specifications for Approval
Tdoc CP-16# | TSs for Approval | Source | Notes
CP-160119 | TS 29.128 v110 Mobility Management Entity (MME) and Serving GPRS Support Node (SGSN) interfaces for interworking with packet data networks and applications T6a/b | Peter Schmitt (Rapporteur) | TS to go for approval at the next Plenary

## Slide 9: Technical Specifications for Information and Approval
Tdoc CP-16# | TSs for Information and Approval | Source | Notes
CP-160120 | New Skeleton and content pCR for the new Diameter application for MCPTT-2 and CSC-13 reference points Final TS ??? v020 | Orange, HPE, Motorola | Final version of TS for e-mail approval. To go for information and approval to CT Plenary.

## Slide 10: CT4 Summary for CT Plenary
CT4 had parallel sessions for three days. Breakout sessions were chaired by Lionel Morand (Orange) and Yvette Koza (Deutsche Telekom AG) while the main session was chaired by Nigel Berry (ALU).
The updated CT4 work plan is available in C4-161547.
Focus of the meeting was on completion of Rel-13.
CT4 made good progress was made on all WIs and especially MCPTT (where Lionel is to be congratulated) and CIoT (where Bruno is to be congratulated).
All Rel-13 WIs are now at 100% apart from CIoT => 65% and the feasibility studies: Diameter Load Control and the Diameter Base Protocol update.
CT4 will need another plenary cycle to complete CIoT provided all the necessary requirements are available from SA2 before the next meetings, otherwise this is in jeopardy for Rel-13.
John Meredith got down and dirty with 3GU in action with CT4.

## Slide 11: CT Plenary Decisions for CT4
For CIoT the S11-U tunnel establishment was controversial in CT4. The CR was CT4 agreed bar one company, the GTPv2 CR defining new S11-U F-TEIDs and enabling the establishment of the S11-U tunnel via a single CSReq/Rsp exchange. The objection may need to be discussed at CT Plenary. See CRs in CP-160033 pack C4-161531 and C4-161383.
Guidance is required from CT on the target Release for the new WID on CT Aspects for non-IP CIoT for 2G/3G-GPRS.
For MONTE, the CP-160029 pack contains a wrong CR in C4-161511. A company contribution in CP-160129 is provided to replace this with the correct one.

## Slide 12: Incoming liaisons to CT plenary
To CT:
  None
CCed to CT:
C4-161504 | LS on New sub-domain for ePDG selection with DNS-based Discovery of Regulatory Requirements | GSMA IREG | CT, CT1 | Nokia contact: Bruno Landais (bruno.landais@nokia.com) LS Author: ALU Background: CT4 ask GSMA IREG to review their proposal to create a new sub-domain to support the Rel-13 stage 2 requirements on ePDG selection (i.e. enable a roaming UE to determine whether the country it is located in mandates or does not mandate the selection of an ePDG in this country, for regulatory requirements). CT Plenary can Note

## Slide 13: CRs for Conditional Approval (CT4)
 | TS | CR | Rev | Rel | Title | TD# | Other Aff Specs
CP-160013 | 23.008 | 0482 | 1 | Rel-12 | IP-SW-GW number format | C4-161391 | 29.328-0550 (CT4)
CP-160013 | 23.008 | 0483 | 1 | Rel-13 | IP-SW-GW number format | C4-161392 | 29.328-0551 (CT4)
CP-160013 | 29.328 | 0550 | 1 | Rel-12 | Encoding of IP-SM-GW Number | C4-161389 | 23.008-0482 (CT4)
CP-160013 | 29.328 | 0551 | 1 | Rel-13 | Encoding of IP-SM-GW Number | C4-161390 | 23.008-0483 (CT4)
CP-160015 | 23.333 | 0092 | 1 | Rel-12 | Corrections to EVS AMR-WB IO mode-change-capability MIME parameter handling | C4-161418 | 26.445-0012 (SA4)
CP-160015 | 23.333 | 0093 | 1 | Rel-13 | Corrections to EVS AMR-WB IO mode-change-capability MIME parameter handling | C4-161420 | 26.445-0013 (SA4)
CP-160015 | 23.334 | 0108 | 1 | Rel-12 | Corrections to EVS AMR-WB IO mode-change-capability MIME parameter handling | C4-161416 | 26.445-0012 (SA4)
CP-160015 | 23.334 | 0109 | 1 | Rel-13 | Corrections to EVS AMR-WB IO mode-change-capability MIME parameter handling | C4-161417 | 26.445-0013 (SA4)
CP-160016 | 29.274 | 1684 | 1 | Rel-13 | Add cause values to TWAN mapping table | C4-161357 | 24.302-0526 (CT1) 24.244-0030 (CT1) 29.273-0447 (CT4)
CP-160025 | 29.274 | 1687 | - | Rel-13 | P-CSCF_RESELECTION_SUPPORT Private Status Type | C4-161133 | 24.302-0540 (CT1)
CP-160027 | 23.153 | 0131 | 1 | Rel-13 | Resolution of Editor's notes on EVS over UMTS CS | C4-161327 | 26.103-0042 (SA4)
CP-160027 | 29.232 | 0659 | - | Rel-13 | Resolution of Editor's note on EVS over UMTS CS | C4-161059 | 26.103-0042 (SA4)
CP-160028 | 29.334 | 0105 | 2 | Rel-13 | WebRTC Data Channels | C4-161329 | 23.334-0104 (CT4)
CP-160029 | 29.230 | 0505 | 3 | Rel-13 | New AVP assignment for MONTE | C4-161509 | 29.336-0039 (CT4) 29.336-0040 (CT4)
CP-160029 | 29.230 | 0509 | - | Rel-13 | Change of type of Monitoring-Duration AVP to represent an absolute time | C4-161141 | 29.336-0045 (CT4)
CP-160029 | 29.336 | 0039 | 2 | Rel-13 | SCEF Restart | C4-161474 | 23.007-0330 (CT4)
CP-160030 | 29.060 | 1034 | - | Rel-13 | Triggering MT SM retransmission by the SMS GMSC to a UE in eDRX during inter MME/SGSN mobility procedure for GTPv1 | C4-161339 | 23.040-0146 (CT1)
CP-160030 | 29.230 | 0511 | - | Rel-13 | Alert procedure from MME/SGSN to SMS-GMSC for MT SMS to UE using eDRX | C4-161153 | 29.338-0019 (CT4)
CP-160030 | 29.274 | 1695 | 1 | Rel-13 | Triggering MT SM retransmission by the SMS GMSC to a UE in eDRX during inter MME/SGSN mobility procedure | C4-161340 | 23.040-0146 (CT1)
CP-160030 | 29.305 | 0062 | - | Rel-13 | Alert procedure from MME/SGSN to SMS-GMSC for MT SMS to UE using eDRX | C4-161155 | 29.338-0019 (CT4) 29.002-1202 (CT4)
CP-160033 | 23.007 | 0332 | 1 | Rel-13 | S11-U Error Indication handling | C4-161383 | 23.401-2942 (SA2)
CP-160033 | 23.007 | 0334 | 3 | Rel-13 | Behaviours upon receipt of unknown NIDD | C4-161546 | 23.682-0160 (SA2)
CP-160033 | 23.007 | 0335 | 3 | Rel-13 | Enhance restoration procedure to be compatible with SCEF PDN connection and Attach without PDN connectivity | C4-161481 | 23.401-2942 (SA2)
CP-160033 | 23.007 | 0336 | 2 | Rel-13 | Connection Resume procedure used during restoration | C4-161477 | 23.401-2934 (SA2)

## Slide 14: CRs for Conditional Approval 2 (CT4)
CP-160033 | 23.008 | 0486 | 1 | Rel-13 | Addition of NB-IoT radio access type to the Access-Restriction-Data feature | C4-161321 | 23.401-2948 (SA2)
CP-160033 | 23.008 | 0487 | 1 | Rel-13 | Storage for CIoT control plane optimization related information at MME | C4-161403 | 23.401-2948 (SA2) 23.401-2942 (SA2)
CP-160033 | 23.008 | 0488 | 2 | Rel-13 | New PDN-Type for Cellular IoT | C4-161529 | 23.401-2934 (SA2)
CP-160033 | 29.002 | 1204 | 2 | Rel-13 | Addition of NB-IoT radio access type to the Access-Restriction-Data feature | C4-161492 | 23.401-2948 (SA2)
CP-160033 | 29.002 | 1205 | 2 | Rel-13 | New PDN-Type for Cellular IoT | C4-161527 | 23.401-2934 (SA2)
CP-160033 | 29.230 | 0513 | 2 | Rel-13 | Definition of AVP Authorization of NIDD | C4-161326 | 29.336-0046 (CT4)
CP-160033 | 29.230 | 0520 | 2 | Rel-13 | New PDN-Type for Cellular IoT | C4-161528 | 29.272-0631 (CT4)
CP-160033 | 29.272 | 0623 | 1 | Rel-13 | Allow SMS for NB-IoT UE without Combined Attach | C4-161323 | 23.401-2951 (SA2)
CP-160033 | 29.272 | 0630 | 2 | Rel-13 | Addition of NB-IoT radio access type to the Access-Restriction-Data feature | C4-161491 | 23.401-2948 (SA2)
CP-160033 | 29.272 | 0631 | 3 | Rel-13 | New PDN-Type for Cellular IoT | C4-161526 | 23.401-2934 (SA2)
CP-160033 | 29.274 | 1689 | 3 | Rel-13 | S11-U tunneling for MO/MT data transport in control plane (SGi based) - with new S11-U F-TEIDs | C4-161531 | 23.401-2942 (SA2)
CP-160033 | 29.274 | 1690 | 1 | Rel-13 | RAT-Type extension for NB-IoT | C4-161399 | 23.401-2951 (SA2)
CP-160033 | 29.274 | 1697 | 6 | Rel-13 | Transfer of non IP PDN to peer MME during mobility | C4-161545 | 23.401-2959 (SA2) 23.401-2951 (SA2) 23.401-2934 (SA2) 23.682-0160 (SA2)
CP-160033 | 29.274 | 1698 | 1 | Rel-13 | Addition of NB-IoT radio access type to the Access-Restriction-Data feature | C4-161322 | 23.401-2948 (SA2)
CP-160033 | 29.274 | 1699 | 1 | Rel-13 | No Delete Session Request for non-existing PDN connection | C4-161432 | 23.401-2954 (SA2)
CP-160033 | 29.274 | 1700 | 1 | Rel-13 | No Create Session Request for Attach without PDN connection | C4-161434 | 23.401-2951 (SA2)
CP-160033 | 29.274 | 1701 | 2 | Rel-13 | No Paging and Service Information in DDN for non-IP PDN connections | C4-161478 | 23.401-2948 (SA2)
CP-160033 | 29.274 | 1704 | 1 | Rel-13 | Protocol change for Connection Suspend and Resume Procedure | C4-161415 | 23.401-2930 (SA2)
CP-160033 | 29.274 | 1705 | 2 | Rel-13 | Protocol change for introducing new non-IP PDN type | C4-161476 | 23.401-2934 (SA2)
CP-160033 | 29.281 | 0074 | 1 | Rel-13 | S11-U tunneling for MO/MT data transport in control plane (SGi based) | C4-161379 | 23.401-2942 (SA2)
CP-160033 | 29.281 | 0075 | 1 | Rel-13 | End Marker handling by MME | C4-161381 | 23.401-2942 (SA2)
CP-160033 | 29.303 | 0087 | 3 | Rel-13 | Impacts on the DNS procedures for CIoT with introduction of NB-IoT and Non-IP | C4-161473 | 23.401-2948 (SA2)
CP-160033 | 29.336 | 0046 | 3 | Rel-13 | Authorization for NIDD procedure over S6t | 4-161530 | 23.682-0160 (SA2)
CP-160035 | 29.273 | 0446 | - | Rel-13 | Remove the default access AVP | C4-161092 | 23.161-0015 (SA2)
CP-160035 | 29.274 | 1692 | - | Rel-13 | PDN Connection Charging ID | C4-161167 | 23.161-0012 (SA2)
CP-160036 | 29.230 | 0517 | 1 | Rel-13 | Monitoring update and Reporting of update result | C4-161380 | 29.345-0036 (CT4)
CP-160036 | 29.274 | 1694 | 2 | Rel-13 | Cleanup of the editor's notes for reporting remote UE | C4-161507 | 24.301-2329 (CT1)
CP-160037 | 29.230 | 0512 | - | Rel-13 | ePDG retrieval of WLAN Location Information | C4-161158 | 29.273-0450 (CT4)
CP-160039 | 23.008 | 0476 | 1 | Rel-13 | User Plane Integrity Protection Indicator | C4-161316 | 43.020-0036 (SA3)
CP-160039 | 29.002 | 1201 | 1 | Rel-13 | User Plane Integrity Protection Indicator | C4-161317 | 43.020-0036 (SA3)
CP-160039 | 29.272 | 0620 | 1 | Rel-13 | User Plane Integrity Protection Indicator | C4-161318 | 43.020-0036 (SA3)
CP-160042 | 29.273 | 0447 | - | Rel-13 | Extension on TWAN-S2a-Failure-Cause | C4-161098 | 24.302-0526 (SA3)
CP-160044 | 23.003 | 0437 | 1 | Rel-13 | ePDG selection with DNS-based Discovery of Regulatory Requirements | C4-161310 | 23.402-2933 (SA2)

## Slide 15: CRs to Plenary
CRs agreed at: CT4#72
  Rel-8 = 0
  Rel-9 = 0
  Rel-10 = 1
  Rel-11 = 1
  Rel-12 = 6
  Rel-13 = 135
  Rel-14 = 1
  No mirror CRs are included in these figures
  Rel-8 to Rel-12 CRs are under FASMO acceptance, i.e. CRs that solve Frequent and Serious Mis-operation Only are accepted.

## Slide 16: Rel-13 Overview
7.1.3 P-CSCF Restoration Enhancements with WLAN [PCSCF_RES_WLAN]
The description of the P-CSCF_RESELECTION SUPPORT attribute in GTPv2 APCO was aligned with the 24.302 CR to explain that the attribute is carried in the Notify payload within the IKE_AUTH request as requested by IANA.
It was clarified that P-CSCF restoration can be done both in 3GPP access and over WLAN depending on which network entities support it.
The HSS shall not report an error to S-CSCF, if the P-CSCF restoration was triggered over 3GPP access or WLAN.

## Slide 17: Rel-13 Overview
7.1.7 CT aspects of EVS in 3G Circuit-Switched Networks [EVSoCS-CT]
CT4 completed their Rel-13 work on EVSoCS based on information received in an LS from SA4 that SA4 has agreed two new related specifications (TS 26.453 "Codec for Enhanced Voice Services (EVS); Speech codec frame structure", and TS 26.454 "Codec for Enhanced Voice Services (EVS); Interface to Iu, Uu, Nb and Mb").
CT4 agreed related updates against TS 23.153 and TS 29.232.

## Slide 18: Rel-13 Overview
7.1.8 H.248 Aspects of WebRTC Data Channel on IMS Access Gateway [WebRTCH248DC]
The stage 2 and stage 3 CRs on WebRTC data channel release at the Iq interface against TS 23.334 and 29.334 were agreed.
The related Rel-13 work item is now considered complete.

## Slide 19: Rel-13 Overview
7.1.9 Monitoring Enhancements CT aspects [MONTE-CT]
The remaining work defined in the exception sheet was covered in this meeting with a 100% achievement of the MONTE-CT WI for the CT4 part. TS 29.128 is sent for approval to the CT Plenary.
The MME/SGSN sends a notify to the HSS when MME/SGSN receives a configuration status from the IWK-SCEF only when this status has changed from the last sent to the HSS;
SCEF does not need to be informed of a HSS restart;
When a SCEF restarts, it will answer with an error when it receives reports for which it has no SCEF Reference ID. The HSS or MME/SGSN will then delete the corresponding MONTE configuration, so there is no need for a reset procedure;
When both SGSN and MME are registered in HSS and support MONTE service, the HSS sends a configuration event to both nodes.
When the number of reports for a Monitoring event type reaches the configured maximum number of reports, the SCEF request the HSS to delete the MONTE configuration.

## Slide 20: Rel-13 Overview
7.1.12 SDP Capability Negotiation for IMS Media Plane [SDPCN_IMS]
Stage 3 Rel-13 CRs for an optional support of the SDP Capability Negotiation were agreed against TS 29.334 (Iq interface), TS 29.238 (Ix interface), TS 29.333 (Mp interface), TS 29.332(Mn interface) against TS 29.232 (Mc interface). The CRs are based on stage 2 CRs agreed at the previous meeting that allow passing SDP capneg related SDP attributes "a=acap", "a=tcap", "a=pcfg" and "a=acfg" (see IETF RFC 5939) to the gateway as one optional possibility (among other that do not require stag3 H.248 profile extensions) to support SDP capneg. The "Enhanced Revised Offer/Answer SDP Support Package" ([ITU-T Recommendation H.248.80) is used for auditing related gateway capabilities.
A proposed support of SDP capneg media capabilities was removed from the stage 3 CR for the Iq interface, as this is only used to offer an alternative transport of media within the CS domain in 3GPP specs.
The related Rel-13 work item is now considered complete.

## Slide 21: Rel-13 Overview
7.1.18 Dedicated Core Networks [DECOR-CT]
CT4 has (nearly) finalized the specification of the DNS procedures' extensions to support the selection of an SGW, PGW or MME/SGSN pertaining to a Dedicated Core Network.

## Slide 22: Rel-13 Overview
7.1.19 Feasibility Study on the Diameter Base Protocol Update [FS_DBPU]
CT4 agreed inputs that SA5 endorsed and attached to their LS. One highlight an issue about the Mbit which is set in new AVPs added to an existing command which should not be the case, and for which SA5 needs a further study. This Tdoc was integrated in TR 29.819.
CT4 in a LS to SA5 asks for SA5 to indicate how they solve this issue before June so to achieve the update to the RFC 6733 reference in Rel-14 3GPP specifications.

## Slide 23: Rel-13 Overview
7.1.20 Diameter Message Priority [DiaPri]
The CRs covering the remaining interfaces listed in the exception sheet were agreed. The WI is 100% complete.

## Slide 24: Rel-13 Overview
7.2.3 QoS End to End MTSI extensions (CT3) [QOSE2EMTSI-CT]
Rel-13 stage 2 against TS 23.334 (Iq interface) and TS 23.333(Mp interface), and stage 3 CRs against TS 29.334 (Iq interface), TS 29.238 (Ix interface), TS 29.333 (Mp interface) and TS 29.332(Mn interface) were agreed that add the optional handling of the new SDP bandwidth attribute specified by SA4 under the QOSE2EMTSI work item.
For bandwidth policing, handling of the bandwidth attribute is a controller-only procedure; the gateway is configured accordingly using the existing packages without extensions. The only use case for providing the bandwidth information to the gateway is transcoding; the bandwidth information may be used by the encoder in the gateway to select an appropriate encoding and redundancy if transcoding happens. For the Iq interface, a mere reference to TS 29.162 (Ix interface stage 2), were CT3 specified related procedures was added, but the Mp interface TS 23.334 contains complete procedures.
The related Rel-13 work item is now considered complete, but additional corrective CRs to align with recently agreed, but still incomplete SA4 changes, are to be expected at the next CT4 meeting.

## Slide 25: Rel-13 Overview
7.2.6 IP Flow Mobility support for S2a and S2b Interfaces on stage 3 (CT1) [NBIFOM]
CT4 has specified a new PDN Connection Charging ID over the S5/S8 and S2a/S2b interfaces, to enable correlations of CDRs for NB-IFOM PDN connections. A few other minor alignment CRs were also agreed.

## Slide 26: Rel-13 Overview
7.2.7 CT aspects of enhancements to Proximity-based Services extensions (CT1) [eProSe-Ext-CT]
The remaining work defined in the exception sheet was covered in this meeting with a 100% achievement of the WI for the CT4 part
Description of ProSe Application Code Prefix and Suffix in TS 23.003;
Two new procedures for ProSe Direct Discovery Authorization Update and ProSe Direct Discovery Authorization Update Result are introduced to support change of authorization in VPLMN/local PLMN and the reporting of the outcome of Authorisation update in VPLMN/local PLMN to the HPLMN;
Designation of the announcing PLMN was changed” to account for the fact that the UE can announce in a PLMN that is not its registered PLMN;
Update of the procedure description for discovery authorization to include the sending and receiving of security materials
Update of the discovery authorization procedure to indicate that the prefix/suffix may be included for announce authorization request;
Update of the discovery authorization to cover the discovery update procedures.

## Slide 27: Rel-13 Overview
7.2.9 Support of Emergency services over WLAN – phase 1 (CT1) [SEW1-CT]
CT4 has specified SWm protocol extensions (Authorization procedure) to enable the ePDG to retrieve the most up to date user's WLAN location information known at the 3GPP AAA server when the ePDG needs to report User Location Information to the PGW and the ePDG has detected a change of the outer IP address of the UE.

## Slide 28: Rel-13 Overview
7.2.10 eDRX [eDRX]
CT4 has finalized the specification of MT SMS enhancements for the PS domain for UEs using extended idle mode DRX. A new Alert procedure has been defined from the MME/SGSN to the SMS-GMSC to enable the immediate retransmission of pending MT SMS at the SMS-GMSC, when the UE originates NAS signalling or moves to another MME/SGSN before its next paging occasion.

## Slide 29: Rel-13 Overview
7.2.11 Mission Critical Push To Talk over LTE protocol aspects (CT1) [MCPTT-CT]
CT4 specified that the Cx interface (TS 29.228) is used for the AAA-1 reference point between the SIP core and the SIP database.
Regarding the MCPP-2 and CSC-13 interfaces to access the MCPTT User Database from a MCPTT server and the Configuration Management server:
  The Ud interface is retained as an option to access the MCPTT user Database when UDC architecture is deployed.
  The principle to have a LDAP data model over this Ud interface was accepted but no CR was produced, as CT4 is awaiting the CT1 final output on the XML files to be transferred over these interfaces, in particular about the handling of multiple MCPTT profiles for the same MCPPT user.
  For the Diameter based solution, there was a debate between a specification based on the reuse as much as possible of the Sh procedures/ commands and AVPs and one creating a new Diameter application with its own commands and new AVPs. To avoid entering a blocking situation, which would have endangered the objective to have a TS for this meeting, it was decided that new would be best,
  A new TS (Diameter Data Management Applications) describing the Diameter application, the procedures/ commands and AVPs to be used over MPPTT-2 and CSC-13 is under email agreement and will be sent for information and approval to the CT Plenary.
  An objective is that this new Diameter application should be reusable for future other Mission Critical applications and more generally to other applications for their access to user application level data stored in an external database.
The MCPTT-CT WI for the CT4 part is completed at 100%.

## Slide 30: Rel-13 Overview
7.2.12 Enhancements to WEBRTC interoperability stage 3 (CT1) [eWebRTCi_CT]
An agreed CR adds WebRTC media plane optimization procedure for the eP-CSCF(IMS-ALG) into stage2 TS 23.334. Based on SDP signaling extensions defined by CT1, the eP-CSCF can recognize that WebRTC media can be transported transparently (from DTLS protocol layer upwards) between WebRTC Clients, and then configures the IMS-AGW accordingly.
Stage 3 CRs that clarify the transparent forwarding in TS 29.238 and TS 29.334 were also agreed.
The related Rel-13 work item is now considered complete.

## Slide 31: Rel-13 Overview
7.2.14 Cellular Internet of Things (CT1) (CT1) [CIoT]
CT4 made good progress: the work is 65% complete, 33 CRs were agreed. The CT4 work is being coordinated by Bruno Landais.
Diameter has been retained for T6a for Non-IP Data Delivery.
For S11-U tunnel establishment, due to a significant majority, CT4 agreed a working assumption based on the GTPv2 CR defining a new S11-U F-TEIDs and enabling the establishment of the S11-U tunnel via a single CSReq/Rsp exchange. The CR was CT4 agreed bar one company. The objection may be discussed at CT Plenary.
DECOR has been specified as one possible option for selecting an SGW/PGW/MME supporting CIoT, but CT4 agreed that this cannot be the only solution as CIoT deployment cannot depend on support of DECOR.

## Slide 32: Rel-13 Overview
7.3.1 GTP and PMIP [TEI13]
The LS from GSMA that PMIP will not be used for roaming signalling over S8 was noted. There is no need to document this in 3GPP specifications.
A note was added to explain the use case for including the RAN/NAS Cause IE in the Delete Bearer Response message.
When using GTP-C load control, the DNS should not be provisioned with a mix of NAPTR records with an "s" flag and with an "a" flag for a given FQDN.
It was specified that the TWAN and ePDG shall send the selected 3GPP AAA Server identifier to the PGW via the GTPv2 based S2a and S2b interface respectively, to ensure that the S6b Authorization Request is sent to the same 3GPP AAA Server without the need for a AAA Server redirection and unnecessary signalling with the HSS.
In Rel-12 the GTPv2 cause values for S2a “user authentication failed” and "Context not found" were mapped to the Diameter cause "Request rejected, unspecified". The cause "Collision with network initiated request" was removed. In Rel-13, these GTPv2 causes are mapped to new S2a cause values defined in TS 29.273

## Slide 33: Rel-13 Overview
7.3.3 AAA Interfaces [TEI13]
The failure cause values "user authentication failed” and “PDN connection does not exist” were added to S2a to align with 24.302 and GTPv2, see above.
It was specified that if the requested APN received from UE is authorized by the wildcard APN, the 3GPP AAA Server shall send the wildcard APN in the Service-Selection AVP to the ePDG, so as to allow the ePDG to set the Selection Mode appropriately in the GTPv2 Create Session Request over S2b (upon receiving the Wildcard APN from the 3GPP AAA Server, the ePDG indicates the Selection Mode value, "…subscription NOT verified", to the PGW). It was stated that the same principles also apply to a TWAN access and that it would be useful to add this clarification also for the S2a interface.

## Slide 34: Rel-13 Overview
7.3.10 EGPRS Access Security Enhancements in relation to Cellular IoT [EASE_EC_GSM]
CT4 has endorsed a new CT WID for Non-IP support in GERAN/UTRAN , completion dates : June 2016 (like for the parent SA WID). Completion of this work for Rel-13 is to be decided at SA Plenary.

## Slide 35: Rel-13 Overview
7.3.1118 bits PDCP PDU Number [TEI13, LTE_CA_enh_b5C-Core]
An exception was added to GTP-U that the SGW shall consider a Next Extension Hearer Field set to "1100 0000" for a PDCP PDU Number as 'comprehension not required'.
As requested by RAN2 for support of enhanced CA, CT4 agreed a 29.281 CR which defines a new GTP-U extension header 'Long PDCP PDU Number'.
CT4 asks RAN2 and RAN3 how a source eNB using 18 bits PDCP PDU Numbers interacts with a legacy target eNB, which does not support the long numbers, see LS guidance for C4-161500.

## Slide 36: Rel-13 Overview
Other Items
ePDG selection enhancements: CT4 has specified a new sub-domain name (C4-161310) to support the Rel-13 stage 2 requirements on ePDG selection, i.e. enable a roaming UE to determine whether the country it is located in mandates or does not mandate the selection of an ePDG in this country, for regulatory requirements.

## Slide 37: Acknowledgements
The Chairman wants to thank
  the delegates for their dedication, hard work and the willingness to be cooperative which resulted in lively discussions and achieved excellent results.
  Lionel Morand and Yvette Koza for expertly taking care of the parallel sessions.
  to my stand-in MCC support, John Meredith, for providing wonderful assistance during the meeting and to Kimmo for his excellent support between the meetings.
  Finally, the hosts of our meetings, for the chance to visit Nashville and Jeju Island.

## Slide 38: Thank You
38
38
Nigel Berry
3GPP TSG CT WG4 Chairman
+44 7880 786 684
nigel.berry@nokia.com